## Slide 1: Wide Bandgap Electronics for High Temperature Wireless Sensing
John R. Fraley
September 28th 2016

## Slide 2: Presentation Outline
Company Introduction
Applications of HT Wireless Sensors in Aerospace Systems
HT Components
HT Electronic Packaging
HT Wireless Sensor Systems

## Slide 3: The World Leader for Wide Bandgap Semiconductors
Lead the innovation and commercialization of SiC and GaN, liberating designers to invent power and wireless systems for a responsible, energy efficient future.
Powering More. Consuming Less.
Notes: This is all that we do. We have the most experience, the most research, the most talent, the most innovation, the best performance.
There are millions of devices out there where power and efficiency are limited by old technology, and we aren’t going to stand for it.
We have the technology, resources and intelligence to lead the wide bandgap semiconductor market.
We are leading the innovation and commercialization of next-generation power and wireless systems based on silicon carbide (SiC) and gallium nitride (GaN).

## Slide 4: WBG Wireless Application Areas

## Slide 5: High Temperature Wireless Telemetry Applications
The high temperature wireless electronic systems currently in development have a wide range of applications within aerospace systems, including:
  Turbine Engine Test Cell Instrumentation
  Prognostic and Health Management (PHM) Systems
  Distributed Engine Control (DCS) Systems
Each of these systems is reliant upon high quality information from sensors and their required electronic infrastructure
These systems can provide for increased safety at each stage of implementation

## Slide 6: Test Cell Instrumentation
The main objectives for test cell instrumentation are to understand the engine, and learn of any engine design or implementation problems early in the design phase.
  Identifying problems early can lead to safer implementation of aerospace systems
  This can lead to very large savings in both overall cost savings, as well as development time
  Early problem identification also allows changes to be made that can result in reduced maintenance costs during the lifetime of the engine
Some examples of needed measurement improvements include:
  Health monitoring of thermal barrier coatings
  Temperature monitoring of the rotors, blades, and gas paths
  Blade tip timing
  Dynamic pressure measurement

## Slide 7: PHM Overview
The main objectives of Prognostics and Health Management Systems include:
  Preventing catastrophic failures from occurring by detecting incipient faults
  Detecting precursor-to-failure trigger points
  Collecting and analyzing system data using realistic and verifiable prognostic models to arrive at a reliability prediction that can be accurately related to the Remaining Useful Life (RUL) of a part, component, or assembly
Successful implementation of a PHM system leads to:
  Increased safety
  Allows for CBM vs. SBM
  Gathering of highly accurate real-time data that can be used for engine performance optimization, or in new engine Designs

## Slide 8: DCS Overview
The main objectives of a Distributed Engine Control System Include:
  Improving overall engine performance, including increased efficiency, reliability, and response
  Reducing engine life cycle costs
  Reducing the time to design and modify engine control systems
The spatial construction of a DCS distinguishes it from a centralized control system
  Data manipulation, decision making and other information processing, as well as one or more sensors and one or more actuators are spatially distributed across the engine.
  This distribution can improve performance and reliability of the engine system as a whole.

## Slide 9: High Temperature Capable Components

## Slide 10: HT Sensors
For wide bandgap wireless instrumentation systems, the sensor elements themselves are the most mature system components
  Some HT sensors such as thermocouples have been available for a century, while new SiC pressure sensors have been demonstrated in recent years
  For our purposes, a sensor is any element which converts a physical parameter into an electrical signal that can be transmitted to an information processing system

## Slide 11: HT Sensors
Temperature is the most widely measured physical parameter, important in nearly every aspect of instrumentation systems
  Can utilize a number of sensor types, common ones include thermocouples and RTDs
Pressure measurements are important many active control systems
  HT pressure sensors commonly utilize piezoresistive sensor elements
Flame Spray TC
Static/ Dynamic Pressure Sensor

## Slide 12: HT Sensors
Vibration information is necessary for structural monitoring of many critical components, including compressors, bearings, and gearboxes.
  HT Piezoelectric accelerometers are commercially available for operation up to 760 °C
Strain information is also used when monitoring structural health of engine components, especially turbine blades.
  HT strain gauges commonly utilize piezoresistive sensor elements
Piezoelectric Accelerometer
Dynamic Strain Gauge

## Slide 13: HT Power Sources
For wireless instrumentation systems, high temperature power sources eliminate the need for hardwired power
  HT electronics require a relatively large amount of power when compared to standard silicon electronic systems
  Commercially available high temperature batteries or other energy storage devices are limited

## Slide 14: HT Power Sources
Vibration
Piezoelectric based vibration energy harvesting systems have been tested in literature up to 300 °C.
RF
Wireless power transmission can induce greater than 50 W over short distances.
TEG
Thermal electric generators produce power from a temperature differential.

## Slide 15: HT Semiconductors
HTSOI
High temperature silicon on insulator devices rated to 225 °C and operable to 300 °C. Devices include 555 times, voltage regulators, microcontrollers, op-amps, logic, ADCs, etc…
SiC
Silicon Carbide devices have been field tested to temperatures in excess of 550 °C, with some literature reporting transistor operation up to 650 °C, and SiC ICs have been demonstrated.
GaN
Gallium Nitride devices are mainly discrete transistors, which have been shown to operate up to 600 °C, with a theoretical operating temperature higher than SiC

## Slide 16: High Temperature Packaging

## Slide 17: HT Substrates
The substrate provides the foundation of the electronic package, giving the circuitry mechanical support and electrical interconnection
Substrates are also a key component of the thermal management of the electronic circuitry
For high temperature systems, most substrates are based on ceramic materials, including alumina, aluminum nitride, silicon nitride, boron nitride, to name a few

## Slide 18: Extreme Environment Substrates
For extreme environment wireless systems, a LTCC or HTCC substrate is used
These substrates provide support to the wireless electronics both for high temperature operation, as well as high vibration or high g-load operation

## Slide 19: Extreme Environment Substrates
The LTCC substrate can provide high density multilayer electrical interconnection, and is suitable for high temperature and high frequency operation
The substrate provides the foundation of a MCM approach, which increases reliability of the overall system
Cavities can be placed in the substrate allowing for low profile dies attachment, minimized wire bond length, and physical support for die
Integrated passives can also be embedded into the substrate

## Slide 20: Field Example – Rotating Electronics

## Slide 21: Wire Bonding
APEI, Inc. Proprietary
1 mil Gold Wire Bonds
Perpendicular Pre-Test
Perpendicular Post-Test
Parallel Pre-Test
Parallel Post-Test

## Slide 22: HT Wireless Systems

## Slide 23: Bearing Sensors
Wireless bearing sensors have been developed to measure temperature and vibration in aerospace engine drive bearings
The systems is a wireless drop in solution that functions to 225 °C and is survivable to 300 °C
The sensor is self powered via a custom thin film thermal electric generator

## Slide 24: Bearing Temperature Transmission
Verification
Calibration

## Slide 25: NASA Nuclear Thermal Propulsion

## Slide 26: NASA Nuclear Thermal Propulsion
500+ °C
1500+ psi
High Radiation
Measurements of Out of Core Thermal Neutrons

## Slide 27: Turbine Blade Sensors
This wireless sensor measures temperature and dynamic strain on power generation turbines
The electronics operate up to 450 °C and in excess of 10,000 g’s
The electronics are powered via an induced power system

## Slide 28: Turbine Sensor Circuitry

## Slide 29: Turbine Sensor Circuitry
25 °C, differential mode
500 °C, common mode
25 °C, common mode
500 °C, differential mode

## Slide 30: Turbine Sensor Spin Testing
Fully functional wireless transmitters are heated to 450 °C
The boards are simultaneously spun achieve g-loading in excess of 10,000 g
Multiple temperature and speed cycles are performed

## Slide 31: Turbine Sensor Spin Testing
Received FM Signal From a Transmitter Operating at 500 °C and > 16,000 G’s Simultaneously

## Slide 32: Summary
Wide bandgap semiconductors hold good advantages over silicon in the context of aerospace sensor systems
Combined with proper packaging designs, wide bandgap technologies can be made to operate in extreme environment conditions, enabling safety monitoring of critical engine components
Many of the new technologies discussed may have a direct benefit to NASA, and we are happy to work with you in all of the extreme environment areas that we have experience with, from semiconductor to system level
11 mil
7
mil
11 mil
7
mil
>1000
°
C
550
°
C

## Slide 33: Acknowledgements
Special thanks to RWTH Aachen University, IEEE, and George Studor