## Slide 1: Dielectric Resonator Based Wireless Passive Sensors
Laboratory of Electrical Instrumentation,
IMTEK, University of Freiburg

## Slide 2: Laboratory for Electrical Instrumentation
Wireless sensing
Energy harvesting
Wireless networking
Low Power Commu- nication
Near field coupling
Inductive coupled
RFID
Chipless sensing
Acoustic
Electro-magnetic
Moni- toring
Locali-zation
RF
Photo- voltaic
Thermo- electric

## Slide 3: Sensor Motes vs Passive Sensors
Battery powered system
  Complex, ‘smart’ sensor node
  Simple reader
Wireless passive system
  Simple, ‘dumb’ sensor node
  More complex reader unit.

## Slide 4: History – Theremin's cavity
Surveillance device ~ 1945
First wireless passive sensor
http://counterespionage.worldsecuresystems.com/the-great-seal-bug-part-1.html

## Slide 5: History - Wireless SAW Sensors
Discovered in mid 1990’s
Surface acoustic delay lines
Harsh Environment compatible
reader
Read-out signal
Response signal
Antenna
IDT
reflectors
piezoelectric crystal
Read-out distance:
1 – 10 m
Notes: This chart shows the principle of a wireless SAW sensor system in more detail: A radio frequency electromagnetic (RF) request signal transmitted by a local radar transceiver (TRx) is picked up by the antenna of the passive SAW transponder where an IDT, connected to the antenna, converts the received signal into a SAW.
The micro-acoustic wave propagates towards reflectors distributed in a characteristic barcode-like pattern and is partially reflected at each reflector. The micro-acoustic wave packets returning to the IDT are re-converted into electrical signals and re-transmitted to the radar Trx unit by the transponder antenna.
This response contains information about the number and location of reflectors as well as the propagation and reflection properties of the SAW wave.
Its evaluation in the radar unit may allow for the extraction of the desired information, f.ex. the sensor effect for a certain measurand and/or a specific ID number.
Passive SAW transponders do not require any power supply, only the energy of the request signal is used. Their antennas are usually of a dipole, patch or loop type. Within the VHF/UHF frequency range, the SAW transponder insertion attenuation is in the order of 20-60 dB.
The achievable access rate is 105/s. The latter fact allows for communication with fast moving objects or vehicles. The read out distance is in the order of some meters, the operating frequencies range is 50 MHz to 2.45 GHz, the delay times are in the order of some ms. Note: There is no power supply in the transponder.
The code length of SAW ID tags is in the order of 32 fixed bits.

## Slide 6: EM Resonators – Basic distinctions
Confined
  Cavity
  Coaxial
Evanescent
  Microstrip/stripline
  Dielectric

## Slide 7: EM Resonators – Evanescent field effect
Confined
  Cavity
  Coaxial
Evanescent
  Microstrip/stripline
  Dielectric

## Slide 8: Parallel plate dielectric resonators
Very high Q resonator
Used traditionally to characterize DR
Adjustable resonance frequency
Operating in the fundamental TE01δ mode

## Slide 9: Parallel plate dielectric resonators
Measurement: return-loss S11 in a parallel plate configuration
Resonant frequency shift (TE01δ Mode) with respect to the displacement of the parallel plates

## Slide 10: Parallel plate Wireless Strain Sensor
Wireless measurement of displacement.

## Slide 11: Sensor concept
Dielectric resonator as a transducer.
Notes: Animation of system?

## Slide 12: Torque sensor prototype
Clamp on device.
Low installation time.
2.4 GHz ISM band compatible
Dual sensors on each side for offset compensation
Offset due to
  Temperature
  Sideways force
  Coupler imperfections

## Slide 13: Torque Sensor - Experimental setup
Notes: Mechanical fabrication by company Schottel

## Slide 14: OWEG Sensor - Force Sensor/Load cell
Evanescent open ended waveguide antenna.
Loaded with a dielectric resonator
Cantilever beam spring.
Force → Displacement → Frequency shift

## Slide 15: OEWG Sensor - Simulations
‘Edge gap’ – main coupling control variable
Weak loop coupling simulation for Q calculations.
Small coupling loop

## Slide 16: OEWG Sensor - Results
High Loaded Q (~3000)
Good Directivity (2 dBi)
High Sensitivity (5 ppm/με)
Good Range (1-5 m)

## Slide 17: High temperature sensor
- 17 -
1.06 m
Inner view of the oven at 700 °C with a dielectric resonator placed inside
Complete measurement setup Reading distance: 1.20 m
reader
PC+ Labview
oven
17 dBi patch antenna
  Tracked resonance frequency shift Maximum frequency shift of -4500 ppm
  Metallization free Dielectric Resonator based high temperature sensing

## Slide 18: Wireless Passive for WAIC
4.3 GHz resonators possible
  Q ~ 2000
  1 – 5 m Wireless range
Possible applications
  Strain sensing for SHM
  EGT sensing
Challenges
  Interoperability with existing systems
  Regulatory

## Slide 19: Wireless Passive for WAIC
4.3 GHz resonators possible
  Q ~ 2000
  1 – 5 m Wireless range
Possible applications
  Strain sensing for SHM
  EGT sensing
Challenges
  Interoperability with existing systems
  Regulatory

## Slide 20: Outlook
https://www.mitre.org/publications/systems-engineering-guide/acquisition-systems-engineering/acquisition-program-planning/assessing-technical-maturity

## Slide 21: Thank You