## Slide 1: Wireless Technology Use Case Requirement Analysis for Future Space Applications
Dr. Ali Abedi, Professor of ECE, University of Maine
DeLisa Wilkerson, Branch Chief/ES36, NASA MSFC

## Slide 2: Overview
Introduction to wireless technology (RF, Acoustic, Optical)
  Wireless standards – Capabilities and limitations
  Reliability of wireless networks – Definitions and basic parameters
Use case scenarios and environmental requirements
  Space vehicles; Satellites and payloads; Surface explorations; Ground systems; Habitats
Application specific requirements
  Engine health monitoring; Wireless power transmission; Radio Frequency (RF) Communications; Cognitive networks; Environmental monitoring and sensors; Habitat systems; Sensors and actuators
Conclusions
  Current interest areas; Potential technology areas for short and long term future implementations; technology road map.

## Slide 3: Overview
Introduction to wireless technology (RF, Acoustic, Optical)
  Wireless standards – Capabilities and limitations
  Reliability of wireless networks – Definitions and basic parameters
Use case scenarios and environmental requirements
  Space vehicles; Satellites and payloads; Surface explorations; Ground systems; Habitats
Application specific requirements
  Engine health monitoring; Wireless power transmission; Radio Frequency (RF) Communications; Cognitive networks; Environmental monitoring and sensors; Habitat systems; Sensors and actuators
Conclusions
  Current interest areas; Potential technology areas for short and long term future implementations; technology road map.

## Slide 4: Wireless standards – Capabilities and limitations
WLAN: Wireless Local Area Network
WPAN: Wireless Personal Area Network
Power
High
Low
Coverage
Large
Limited
Device
Complex
Simple
Lifetime
Long
Short
WLAN
WPAN
Bluetooth: Master/Slave ZigBee: Mesh
* References [2-8]

## Slide 5: Reliability of Wireless Networks
What is the definition of reliability?
  End to end data throughput
  Delay or latency
  Bit Error Rate (BER) or Symbol Error Rate (SER) or Packet Error Rate (PER)
  Packet loss or collision rate
Example: QBSC’2007
  AWGN (left)
  Rayleigh fading (right)
Example: Sensors’2013
  One sensor (left), multiple (right)
* References [9-10]

## Slide 6: Overview
Introduction to wireless technology (RF, Acoustic, Optical)
  Wireless standards – Capabilities and limitations
  Reliability of wireless networks – Definitions and basic parameters
Use case scenarios and environmental requirements
  Space vehicles; Satellites and payloads; Surface explorations; Ground systems; Habitats
Application specific requirements
  Engine health monitoring; Wireless power transmission; Radio Frequency (RF) Communications; Cognitive networks; Environmental monitoring and sensors; Habitat systems; Sensors and actuators
Conclusions
  Current interest areas; Potential technology areas for short and long term future implementations; technology road map.

## Slide 7: Space Vehicles
Space vehicles operate in extreme conditions with notable vibrations on their various sub-systems. Monitoring critical systems such as thermal and pressure systems, cryogenic fluid management, HVAC, ECLSS, Lighting Monitoring, Docking, and Rendezvous systems require specific considerations as follows*. Most of these systems are hard to reach and not accessible easily. The wireless system design need to accommodate operations in confined spaces and often closed metallic chambers or sometimes even inside fluid environments at cryogenic temperatures. A recent work at MSFC demonstrated proof of concept for wireless sensing inside a fuel tank*. Monitoring the engine and heat shield requires sensors that can operate in high temperature environments with harsh chemical vapors present.
Challenges:
Wide range of temperature variations
Vibration tolerance
Accessibility in confined environments
Signal propagation in metallic enclosures
Benefits:
Acquiring more data from supporting structures and engine itself
Reducing weight due to cable elimination
Dynamic performance control with wireless sensing and actuation
* References [11-12]
SLS

## Slide 8: Example: Test of WSN on board a Rocket
2009, 2011, and 2013 Mojave, CA
Funded by NASA MSGC and CSGC

## Slide 9: Satellites and payloads
Satellites and payloads operate in harsh environment and often require monitoring and protection against extreme temperature changes and radiation. Whether using radiation hardened hardware or adding internal heaters or coolers to keep the equipment in desirable environmental condition, it is necessary to monitor the internal temperatures and radiation doses at all times. Although, it may not make sense to replace a short few cm wire inside a small satellite with wireless, but for some applications were drilling a hole in the payload or satellite’s exterior body may lead to loss of heat and energy, short range magnetic coupling wireless solutions will become important. Other applications include monitoring external solar arrays for MMOD impact or damage evaluation as well as transferring power between two disjoint sections.
Challenges:
Wide range of temperature and radiation variations
Size and weight limitations
Signal propagation in metallic enclosures
Power constraints
Benefits:
Wireless connection between two disjoint sections
Reducing heat loss by avoiding drilling holes
More efficient use of harvested power
Cube Sat

## Slide 10: Example: ISS Solar Array Impact Localization
Funded by JACOBS/JSC
3-axis Accelerometers
IEEE 802.15.4 radios
Wavelet based signal processing

## Slide 11: Surface explorations
Autonomous exploration of planetary surfaces may require machine vision and robotics arms to recognize various object types and manipulate them, drill ground to collect soil samples, and navigate to return samples to base. All these applications can benefit from wireless sensors. For instance, Infrared sensors can be used alongside visible light cameras for object detection and classification and assisting the robotics arms to maneuver accurately. Humidity and temperature sensors can be used during ground drilling, while vibration sensors can monitor the drill operation. Navigation without GPS on planetary surfaces requires dedicated active wireless links with precise time of arrival measurements (e.g. one example is the Ultra wide band radios developed at JSC). Other techniques such as passive RFID tags and readers may also be used to find asset in know areas pre-marked with tags.
Challenges:
Capability to operate and survive dust or radiation storm
Mobile chemical and biological sensor units
Long range reliable link back to base with navigation capabilities
Benefits:
In situ testing of samples
Navigation without need for GPS
Dynamic control of robotic arms using wireless sensors and actuators
NASA’s SEV

## Slide 12: Example: JSC’s UWB Tracking System
Resolution: 0.8762m (dynamic), 1.7660m (Static)
Barton, et. al., IEEE/ACES Int’l Conference on Wireless Communications and Applied Computational Electromagnetics, 2005.

## Slide 13: Ground systems
Ground testing often requires structural sensors such as strain gauges, accelerometers, and deflection sensors. Testing fuel tanks may require leak detection sensors, hydrogen or other gas sensors, humidity, and temperature sensors. Performance tests are conducted in controlled environment with thermal cycles that mimic space conditions. Therefore, all these instrumentation, although used on earth, need to be capable of operating in harsh environments. Wiring and cabling may be cumbersome, costly, or may be infeasible in some cases. Therefore, wireless sensing in ground system can open up lots of new opportunities to gather critical data.
Challenges:
High precision in sampling and data transfer
Interference management among large number of sensors sending data
Working within limitations of test setup at specific distances
Benefits:
Acquiring more data for structural analysis that is possible using wires
Reducing cost of tests due to cable elimination
Flexibility of test for adding more sensors later without redesigning the whole wiring plan
Versatility in programming test beds for future tests
MSFC Structural testing laboratory

## Slide 14: Example: Structural Test Data Analysis
Node ID | No of | Packets
5e7b00 | 26175 | packets
5e7ca4 | 79348 | packets
5e7a5a | 24553 | packets
5e7cc5 | 26585 | packets
5e7a47 | 24692 | packets
Lessons learned:
Metal plates around sensors  Add Insulator
Strong WiFi interference  add shielding
Sensor data anomaly  calibrate
Interference among nodes  one at a time
Issues with analog front end  new boards
July 25, 2016 Strain Sensor Test with Synapse radios

## Slide 15: Example: DBOBs/SIL
There are 23 DBOBs on each half cylinder at SIL
Each RS422 connector has 8 ports with 10 MHz bandwidth
Each one communicates with multiple devices analog/digital
Signals range from 4mv to 40v DC

## Slide 16: Habitats
Autonomous monitoring of habitats, living conditions, and inventory tracking are the main use case scenarios that can benefit from wireless technology. RFID based inventory tracking methods for autonomous logistical management (ALM) is being developed at JSC and can tie into the habitat monitoring itself. Integrating sensors as load on RFID devices and reading the changes in the response in addition to ID numbers is a promising approach in this direction. Monitoring living conditions including physical (temperature, humidity, and radiation), chemical (air and water quality) and biological (mold and mildew or other airborne bacteria) are some critical applications that require wireless sensors. Another important aspect of monitoring habitat systems is evaluating cognitive changes of its inhabitants, i.e. crew health monitoring. Real time vital signs tracking and wireless sensors for sleep behavior monitoring are essential for ensuring mission success.
Challenges:
Wide range of temperature and radiation variations
Aggregation challenges in multi model sensor data with different sampling rates and precisions
Signal propagation in metallic enclosures
Benefits:
Acquiring more data from habitat structure
Reducing weight due to cable elimination
Flexibility of change in design and sensor location after the deployment
MSFC Habitat

## Slide 17: Example: Inflatable Space Habitat

## Slide 18: Overview
Introduction to wireless technology (RF, Acoustic, Optical)
  Wireless standards – Capabilities and limitations
  Reliability of wireless networks – Definitions and basic parameters
Use case scenarios and environmental requirements
  Space vehicles; Satellites and payloads; Surface explorations; Ground systems; Habitats
Application specific requirements
  Engine health monitoring; Wireless power transmission; Radio Frequency (RF) Communications; Cognitive networks; Environmental monitoring and sensors; Habitat systems; Sensors and actuators
Conclusions
  Current interest areas; Potential technology areas for short and long term future implementations; technology road map.

## Slide 19: Application specific requirements*
  TA2.4: Engine health monitoring;
  TA3.3: Wireless power transmission;
  TA5.2: Radio Frequency (RF) Communications;
  TA5.5: Cognitive networks;
  TA6.4: Environmental monitoring and sensors;
  TA7.4: Habitat systems;
  TA10.4: Sensors and actuators
* NASA Technology Roadmap [1]
* References [13-16]
* References [17-18]
* References [19]

## Slide 20: TA 5.2 and TA 5.5
NETWORK CODING
COGNITIVE NETWORKS
Lower Latency
Spectrum Efficiency

## Slide 21: Overview
Introduction to wireless technology (RF, Acoustic, Optical)
  Wireless standards – Capabilities and limitations
  Reliability of wireless networks – Definitions and basic parameters
Use case scenarios and environmental requirements
  Space vehicles; Satellites and payloads; Surface explorations; Ground systems; Habitats
Application specific requirements
  Engine health monitoring; Wireless power transmission; Radio Frequency (RF) Communications; Cognitive networks; Environmental monitoring and sensors; Habitat systems; Sensors and actuators
Conclusions
  Current interest areas; Potential technology areas for short and long term future implementations; technology road map.

## Slide 22: Potential technology areas
Dark shaded squares indicate closely related technical areas and application use cases
lightly shaded cells indicate potential benefit from wireless technology broadly defined

## Slide 23: Roadmap for wireless technology development
Where we are | Short term <5 Yr | Long term, 5-10 Yr | Where we want to go
Not space certified, rad tolerant or rad hard Low reliability Limited# of networked nodes Not scalable Not reconfigurable Lack of coexistence in transmit protocols Battery dependent | X X X | X X X X | Space certified High reliability Large network sizes Scalable Reconfigurable Coexisting protocols with cognition Battery free
Concluding Remarks:
Wireless Technology has the potential to be used in space applications
It offers unique capabilities that are not obtainable in wired systems
The space application areas are varied and each have a unique set of requirements
Rapid development in wireless industry can be used as stepping stone

## Slide 24: Future technologies – 5G and beyond
1G (AMPS), 2G (GSM/CDMA), 3G (e.g. UMTS, HSPA and 1X-EV-DO), 4G (LTE, LTE-A), 5G [21].
Massive MIMO RAN Transmission cm and mm Waves New Waveforms Shared Spectrum Access Advanced Inter-Node Coordination Simultaneous Transmission Reception Multi-RAT Integration & Management D2D Communications | Efficient Small Data Transmission Wireless Backhaul/Access Integration Flexible Networks Flexible Mobility Context Aware Networking Information Centric Networking Moving Networks
RAN: Radio Access Networks RAT: Radio Access Technology D2D: Device to Device

## Slide 25: Acknowledgments
Thanks to NASA MSFC Faculty Fellows program managers and their staff members for funding this research project.
Thanks to engineers and scientists at NASA MSFC ES36 group who shared their thoughts and ideas on using wireless sensing technologies in space applications.
Special thanks to Branch Chief, DeLisa Wilkerson, for guiding this research, coordinating tours, visits, and interviews, and great suggestions.
Contact Info: ali.abedi@maine.edu
UMAINE.EDU/WISENETLAB

## Slide 26: References (1-10)
NASA Technology Roadmap, 2015, URL: http://www.nasa.gov/offices/oct/home/roadmaps/
IEEE Standard for Information technology--Telecommunications and information exchange between systems Local and metropolitan area networks--Specific requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications," in IEEE Std 802.11-2012 (Revision of IEEE Std 802.11-2007) , vol., no., pp.1-2793, March 29 2012.
IEEE Standard for Information technology-- Local and metropolitan area networks-- Specific requirements-- Part 15.1a: Wireless Medium Access Control (MAC) and Physical Layer (PHY) specifications for Wireless Personal Area Networks (WPAN)," in IEEE Std 802.15.1-2005 (Revision of IEEE Std 802.15.1-2002) , vol., no., pp.1-700, June 14 2005.
IEEE Standard for Local and metropolitan area networks--Part 15.4: Low-Rate Wireless Personal Area Networks (LR-WPANs) Amendment 3: Physical Layer (PHY) Specifications for Low-Data-Rate, Wireless, Smart Metering Utility Networks," in IEEE Std 802.15.4g-2012 (Amendment to IEEE Std 802.15.4-2011) , vol., no., pp.1-252, April 27 2012.
T. Ngo, Why WiFi stinks and How to fix it, IEEE Spectrum Magazine, June 2016.
IEEE Standard for Information technology-- Local and metropolitan area networks-- Specific requirements-- Part 15.3: Amendment 2: Millimeter-wave-based Alternative Physical Layer Extension," in IEEE Std 802.15.3c-2009 (Amendment to IEEE Std 802.15.3-2003) , vol., no., pp.1-200, Oct. 12 2009.
IEEE Standard for Air Interface for Broadband Wireless Access Systems," in IEEE Std 802.16-2012 (Revision of IEEE Std 802.16-2009) , vol., no., pp.1-2542, Aug. 17 2012.
IEEE Recommended Practice for Information technology-- Local and metropolitan area networks-- Specific requirements-- Part 15.2: Coexistence of Wireless Personal Area Networks with Other Wireless Devices Operating in Unlicensed Frequency Bands," in IEEE Std 802.15.2-2003 , vol., no., pp.1-150, Aug. 28 2003.
Bingxin Shen and A. Abedi, "Error correction in heterogeneous wireless sensor networks," Communications, 2008 24th Biennial Symposium on, Kingston, ON, 2008, pp. 111-114.
A. Abedi and K. Zyck, "Iterative interference management in coded passive wireless sensors," SENSORS, 2013 IEEE, Baltimore, MD, 2013.

## Slide 27: References (11-21)
L. Fabisinski, D. Wilkerson, “Wireless Sensors Applications at Marshall Space Flight Center,” IEEE International Conference on Wireless for Space and Extreme Environments (WiSEE), Dec 2015, Orlando, FL.
G. Merrill, D. Wilkerson, “NASA Fuel Tank Wireless Power and Signal Study,” IEEE International Conference on Wireless for Space and Extreme Environments (WiSEE), Dec 2015, Orlando, FL.
J. Ni, et. al., "UWB Tracking System Design for Lunar/Mars Exploration," IEEE International Conference on Wireless; 13-16 Mar. 2006; Sydney; Australia.
B. H. Fisher and D. C. Malocha, "Cryogenic Liquid Sensing Using SAW Devices," 2007 IEEE International Frequency Control Symposium Joint with the 21st European Frequency and Time Forum, Geneva, 2007, pp. 505-510.
W. C. Wilson et al., "Orthogonal Frequency Coded SAW Sensors for Aerospace SHM Applications," in IEEE Sensors Journal, vol. 9, no. 11, pp. 1546-1556, Nov. 2009.
D. C. Malocha et al., "Orthogonal frequency coded SAW sensors and RFID design principles," 2008 IEEE International Frequency Control Symposium, Honolulu, HI, 2008, pp. 278-283.
D. C. Malocha, B. Fisher, R. Youngquist, A. Weeks and M. Gallagher, "Surface Acoustic Wave Pulsed-Correlator Transceiver for Aerospace Applications," in IEEE Sensors Journal, vol. 14, no. 11, pp. 3775-3781, Nov. 2014.
K. Yasami, A. Razi, A. Abedi, “Analysis of Channel Estimation Error in Physical Layer Network Coding,” IEEE Communications Letters, vol. 15, no. 10, pp. 1029-1031, October 2011.
F. Afghah, M. Costa, A. Razi, A. Abedi and A. Ephremides, "A reputation-based Stackelberg game approach for spectrum sharing with cognitive cooperation," 52nd IEEE Conference on Decision and Control, Firenze, 2013, pp. 3287-3292.
L. Labonte, J. Castro, M. Razfar, A. Abedi, R. Rezaei, F. Ghabrial, P. Shankar, E. Besnard, “Wireless Sensor and Actuator Networks with Delayed Noisy Feedback (WiSAN),” IEEE International Conference on Wireless for Space and Extreme Environments, Nov 2013, Baltimore, MD.
A. Dutta, H. Freeman, President’s page: 5G Perspective, IEEE Communications magazine, May 2016, pp. 4-5.