## Slide 1: Why did my lights go out?
Dr. George Gela, BETC
June 22, 2017
BETC

## Slide 2: Outline
What is a “power outage”?
Planned (scheduled)? Unplanned (unscheduled)?
Large or small? Long or short?
Outages worldwide
Why do they happen?
How can outages be avoided, managed?
Reliability indices
Cost of outage
Long-term effects
Information from local utility
BETC

## Slide 3: What is a “power outage”?
Definition: “Outage” … describes the state of a component when it is not available to perform its intended function due to some event directly associated with that component. An outage may or may not cause an interruption of service to consumers depending on system configuration.
BETC
New Yorkers sleep and wait for their train August 15, 2003 at Grand Central Station in New York, New York.
Duration: 7 to 50 hours, some areas about a week.
http://www.huffingtonpost.com/2013/08/14/2003-northeast-blackout_n_3751171.html

## Slide 4: Planned (scheduled) Unplanned (unscheduled)
Scheduled outage usually does not cause an interruption of service to consumers.
Service to customers can be diverted through alternate routes (lines).
This is one reason that lines, generators, transformers, other equipment are usually NOT loaded to their maximum capacity.
BETC

## Slide 5: Planned (scheduled) Unplanned (unscheduled)
Examples:
  Scheduled maintenance:
    Probably NO interruption of service
    Scheduled outage of this line, but power rerouted via other lines
    Scheduled outage
BETC

## Slide 6: Planned (scheduled) Unplanned (unscheduled)
Examples:
  Significant damage to component(s)
BETC

## Slide 7: Planned (scheduled) Unplanned (unscheduled)
Examples:
  Significant damage to component(s)
BETC

## Slide 8: Planned (scheduled) Unplanned (unscheduled)
Examples: Significant damage to component(s)
BETC

## Slide 9: Large or small? Long or short?
1965:
  Ontario in Canada; Connecticut, Massachusetts, New Hampshire, New Jersey, New York, Rhode Island, Pennsylvania, and Vermont in USA.
  Over 30 million people and 80,000 square miles (207,000 km2) were left without electricity for up to 13 hours. (https://en.wikipedia.org/wiki/Northeast_blackout_of_1965 )
BETC

## Slide 10: Large or small? Long or short?
2003:
  7 to 50 hours
  More widespread that the 1965 event
  Affected some 10 million in Canada and 45 million in eight states in the USA
BETC

## Slide 11: Major outages worldwide
Location | Date | People affected (millions)
USA (Northeast), Canada | 9 November 1965 | 30
Thailand | 18 March 1978 | 40
Quebec, Canada | 7 January 1998 | 2.2
Brazil (Southern) | 11 March 1999 | 97
India | J2 January 2001 | 230
USA (Northeast), Canada | 14 – 15 August 2003 | 55
Indonesia (Java-Bali) | 18 August 2005 | 100
Italy, Switzerland | 28 September 2003 | 55
Brazil, Paraguay | 10 – 11 November 2009 | 87
India | 30 – 31 July 2012 | 620
Bangladesh | 1 November 2014 | 150
Pakistan | 26 January 2015 | 140
Turkey | 31 March 2015 | 70
Sri Lanka | 13 March 2016 | 21
Kenya | 7 June 2016 | 44
BETC

## Slide 12: Why do outages happen?
Many varied reasons:
  Weather (snow, ice, rain storms, wind, lightning)
  Insulator contamination
  Equipment failure
  Human error
  Vegetation
  Wildlife Geomagnetic storms
  Vandalism
  Overloading, overheating
  Traffic accidents
  Systems operation, switching, resonance
  Aging
  Other?
BETC

## Slide 13: Why do outages happen?
BETC

## Slide 14: Why do outages happen?
SEATTLE –Utility officials say a falling fish knocked out power to nearly 200 customers in Seattle.
The Seattle Times reports that a Seattle City Light crew investigating the power outage Wednesday afternoon found an electrocuted fish on the ground below the power lines. They figured that one of the eagles or ospreys that routinely hunt in the nearby Duwamish River must have dropped it.
Power was out for about two and a half hours.
City Light says birds often cause power outages - 162 of them in the city last year, including two by bald eagles. Raccoons are another common culprit. But spokeswoman Connie McDougall says this is the first time she’s heard of a fish knocking out power.
McDougall says the workers who found the fish think it was a salmon, but she notes that “they’re not fish biologists.”

## Slide 15: Why do outages happen?
BETC

## Slide 16: Why do outages happen?
BETC

## Slide 17: Why do outages happen?
BETC

## Slide 18: Why do outages happen?
BETC

## Slide 19: Why do outages happen?
Examples:
BETC

## Slide 20: Why do outages happen?
Examples:
BETC

## Slide 21: Why do outages happen?
Examples:
BETC

## Slide 22: Why do outages happen?
Examples:
BETC

## Slide 23: Why do outages happen?
Did UFO’s Cause the Great New York Blackout in 1965?
Maybe it was a UFO because, according to some conspiracy theorists, the big power outage in 1965 was caused by a UFO.
Here is the UFO angle and it’s relation to the Johnson White House. Never mind that it happened again in 2003 and never mind that it is acknowledged that our electric grid is antiquated and susceptible to catastrophic, large scale failure. No…it was an UFO.
Here is a summary of the whole caper. Look at these UFO reports from the late summer and fall of 1965 and analyze these UFO reports from Nov 9, 1965 yourself!
Truth or Fiction? Apparently one demonstrated part of fiction from the Great Northeast Blackout was that the birthrate in the region skyrocketed 9 months later.
https://symonsez.wordpress.com/2009/11/09/did-ufos-cause-the-great-new-york-blackout-in-1965/
BETC

## Slide 24: Why do outages happen?
Outage in Lenox – Pittsfield, December 1991
Helicopter testing in Lenox – for live work
Two methods of delivery of lineman to live conductors:
  Platform method
  Suspension method
BETC

## Slide 25: Why do outages happen?
Sparkover occurred during tests of the suspension method using the 115 kV line 1211
The 1211 line runs between two 115 kV substations
The feed to the Lenox lab taps off from about the midpoint of the line
This resulted in a low-current line-ground fault on the 115 kV line 1211
The circuit breaker at the Lenox lab operated to clear the fault, and communicated the action to terminal breakers at the ends of the line
BETC

## Slide 26: Why do outages happen?
However, several years prior, communication frequency of the terminal breaker was changed
As a result, the terminal breaker(s) opened the 1211 line to clear the fault
This caused an outage in Lenox and Pittsfield that lasted a few hours.
Subsequently, the communication system was upgraded
BETC

## Slide 27: How can outages be avoided, managed?
Understand your system
Analysis of failures
Inspection of assets
BETC

## Slide 28: How can outages be avoided, managed?
Example: insulator flashover
BETC

## Slide 29: ANALYSIS OF FAULTS BY MONTH
CORRELATION
WITH WEATHER
DATA
T-STORMS &
RAIN
FOG
FOG
Schneider 1996

## Slide 30: TYPICAL PATTERN FOR POLLUTION FAILURES
FLASHOVERS
IN EARLY MORNING
HOURS
Schneider 1996

## Slide 31: ADDRESSING THE REASONS FOR FAILURE ”LONG DURATION”
EMERGENCY
REPAIRS
STORMS
ACCIDENTS
TOWER COLLAPSE
STRATEGIC
PLANNING
PIN CORROSION
ROD BREAKAGE
VIBRATION DAMAGE
DEVELOP
RESTORATION
PROCEDURES
INSPECTION &
REPLACEMENT
PROGRAM
Schneider 1996

## Slide 32: SAFE LIVE WORKING PRACTICES
ELIMINATE OUTAGES
DETERMINE APPROACH DISTANCES
  SPECIFIC TO : STRUCTURE, BUNDLE, INSULATORS, & TOOLS
  EVALUATE WITH HV TESTS
  MAIN CONSIDERATION: OVERVOLTAGES
CONSIDER PROTECTIVE GAPS
  INSULATION COORDINATION
Schneider 1996

## Slide 33: Reliability indices (distribution)
BETC

## Slide 34: Cost of outage
BETC

## Slide 35: COST OF FAILURE
EXAMPLE:
LARGE CHEMICAL PLANT
COULD BECOME
AVOIDED COST
Schneider 1996

## Slide 36: Long-term effects
Loss of revenue
Degradation of power quality
Customer complaints
Disruption to industrial processes, public safety (hospitals, police, fire departments, etc).
Need for back-up power sources
BETC

## Slide 37: POSITIVE long-term effect: NERC, FERC, EPRI
“Following the (1965) blackout, measures were undertaken to try to prevent a repetition.
Reliability councils were formed to establish standards, share information, and improve coordination amongst electricity providers.
The task force that investigated the blackout found that a lack of voltage and current monitoring was a contributing factor to the blackout, and recommended improvements.
The Electric Power Research Institute helped the electric power industry develop new metering and monitoring equipment and systems, which have become the modern SCADA systems in use today.” (https://en.wikipedia.org/wiki/Northeast_blackout_of_1965 )
EPRI was formed in 1972. SCADA: Supervisory Control and data Acquisition
BETC

## Slide 38: Outage information from local utility https://www.eversource.com/wmeco/outage/outagemap.aspx
BETC
In case of an emergency, life threatening situation, downed line or if you are in imminent danger please call 911.

## Slide 39: Thank you!
Questions?
BETC