## Slide 1
Status of 3RD Edition of IEC 60601-1
By Grant Schmidbauer
Nemko USA, Inc. San Diego, CA

## Slide 2: Status of 3rd Edition of IEC 60601-1
CB Scheme
European Union
USA
Brazil
Canada, Japan, China, others

## Slide 3: CB Scheme

## Slide 4: CB Scheme
3rd edition of IEC 60601-1 re-instated for CB Test certificates as of February 12, 2008
CB Testing laboratories must now update their CBTL scope with 3rd edition
CB Test Certificates can now be issued, covering all relevant requirements of the standard(s) as applicable, or may cover “Electrical Safety” only

## Slide 5: European Union
The date of withdrawal (DOW) for EN 60601-1 2nd Edition is September 12th, 2009
The DOW means that all products sold in the EU after that date must conform to the requirements of the new standard
However, the DOW for medical devices is set only for the Part 1 standard, EN 60601-1

## Slide 6: European Union
For medical devices with relevant particular (Part 2) standards, the DOW has not been set
With 40+ particular (Part 2) standards (IEC/EN 60601-2-XX) currently referencing specific clauses in the 2nd Edition, the DOW for medical devices with particular (Part 2) standards, will not be set until the particular (Part 2) standard has been updated with references to specific clauses in the 3rd edition
The transition period for medical devices with particular (Part 2) standards will be extended as necessary

## Slide 7
Published by AAMI as ES 60601-1 and is currently under review by the FDA (not published by UL!)
Missing several of the USA national deviations that were part of 2nd edition (ie, earth leakage current at 500µA whereas in the 2nd edition it was 300µA)
AAMI is working to resolve the national deviations and a revision or notice will be published in the near future
Not currently fully accepted as national standard in the USA
USA

## Slide 8: Brazil
Brazil uses NBR IEC standards for InMetro certification of medical devices
NBR IEC standards are the same as IEC standards, but translated into Portuguese with possible national deviations
The translation of IEC 60601-1 3rd Edition has been completed and sent to ABNT (Associação Brasileira de Normas Técnicas) for final review

## Slide 9: Brazil
The date for the publication of the standard is not yet set
The particular standards are in the process of translation as well and the expected completion date is late 2008, similar to the IEC updates
Once the translation and approval process is completed, ANVISA will determine the date of publication
Until then, only evaluations and reports to the 2nd Edition are accepted

## Slide 10
To our knowledge, at this time, no other countries have yet issued national standards harmonized with the 3rd Edition
However Canada is in the final stages of their publication with Canadian national deviations
For the most current information, please contact the country's public health authorities
Canada, Japan, China, others

## Slide 11
Grant Schmidbauer General Manager Nemko USA, Inc. 11696 Sorrento Valley Road San Diego, CA 92121 USA Tel: 858-755-5525 Ex. 208 Fax: 858-452-1810 Email: grant.schmidbauer@nemko.com Website: www.nemko.com
Contact Information