## Slide 1: Recap of Chernobyl accident causes
Gary Johnson
2019 03 30

## Slide 2: The reactor had a high positive void coefficient at the time of the event
Notes: At the time of the test the thermal void coefficient of reactivity was positive. This by itself was not sufficient to cause the accident. Design provisions and procedures existed to cope with this condition.

## Slide 3: Plant procedures and training did not adequately address low power op’s
Notes: There were issues with some procedures and training for operations at low power. The operators were not aware of the hazards associated with low power operation and low power to flow ratios. The test was originally planned to be run at at a power level where these wouldn’t matter, but neither the test procedure nor the operating procedures prohibited performing the test at low power.

## Slide 4: The 9 hour delay at 50% power changed the situation
Notes: The 10 hour delay at 50% power for test setup followed by an additional 9 hour delay ordered by the load dispatcher allowed a large build up of Xe-135 which inserted significant negative reactivity into the core. Thus when power dropped to near 1% as the operators tried to reduce power to 22% there was not enough reactivity in the core to bring power back up to the intended test level.
The best that the operators could do was withdraw nearly all control rods to bring power up to about 6%. This had two important effects. First, at low power the reactor coolant temperature was lower than planned, so there were fewer voids in the coolant thus more new voids (and more reactivity) could be produced if there was a sudden increase in coolant temperature. Second, with few control elements in the core the control elements provided insufficient negative reactivity to counter the reactivity increase that would be caused by sudden creation of voids.

## Slide 5: Starting the test caused a reactivity transient
Notes: The operators did not consider the consequences of rapid void generation in the coolant and ignored the rules that required them to shut down the plant when the operating reactivity margin was low. They didn’t understand that ORM limits had a safety purpose. Starting the test under these conditions caused a reactivity transient that probably would have grown large enough to destroy the core, but perhaps the damage would have been contained in the reactor tank or the reactor building.

## Slide 6: When the operators saw power increase they scrammed the reactor
Notes: The operators initiated a scram when they saw power increasing. They expected that this would stop the transient, but considering that it would take the control rods 7 seconds to drop 90% in their action may have been too late to save the core. But there was something else that the operators didn’t know.

## Slide 7: The scram initially inserted more reactivity
Notes: The area of the core just below the graphite displacers was highly reactive, so when the control elements started to insert the graphite displacers moving into the highly reactive area caused a significantly increase in reactor power.

## Slide 8: The safety analysis was inadequate or not communicated
Notes: This sequence of events was only possible because of decisions made long before the accident. Thorough safety analysis was not performed for low power operation – or if it was the results were not adequately communicated to the procedure writers, the trainers, and the operators

## Slide 9: The test was not reviewed from a nuclear safety perspective
Notes: To make maters worse review of the test procedure did not include nuclear safety experts: the test was considered as only an electrical test. This view could be another consequence of the inadequate safety analysis.

## Slide 10: Operating experience from other plants was not communicated
Notes: Furthermore the Unit 4 operators were unaware of the possibility of a “positive scram” even though this had been observed during operation at other RBMK reactors, including Chernobyl Unit 1.