## Slide 1: A Brief History of Motorola with a Focus on Semiconductors in the ‘70s, ‘80s & ‘90s
August 18, 2022
By
Michael G. Collins
Especially prepared for the
IEEE CTS CTCN and LM
Notes: NETFLIX – Inventing Anna

## Slide 2: Agenda
Early days – Galvin Manufacturing
Motorola Semiconductor
  Birth of Semiconductors
  Product Line
  Applications
  The split up

## Slide 3
All early radios were battery powered
A Battery – 6 Volt
B Battery – 45V
Batteries were consumable. Needed to be replaced
Fahnestock clip

## Slide 4
Battery Eliminators – No need to buy batteries
1920s ~ 35% of US households had electricity
As more US households had electricity, Battery Eliminators Became Popular
Battery Eliminators = Power Supply

## Slide 5: MOTOROLA – The Beginning
1928 Motorola started in Chicago, Illinois, as Galvin Manufacturing Corporation by building battery eliminators.
Brothers, Paul V. and Joseph E. Galvin, purchased the bankrupt Stewart Battery Company's battery-eliminator plans and manufacturing equipment at auction for $750.
Galvin Manufacturing started making Battery Eliminators
Radio manufacturers started to integrate power supplies into their radios and the market for Battery Eliminators soon became obsolete.
Galvin Manufacturing needed other products

## Slide 6
Paul Galvin learned that some radio technicians were installing sets in cars.
Challenged his engineers to design an inexpensive car radio that could be installed in most vehicles.
Galvin demonstrated a working model of the radio at the June 1930 Radio Manufacturers Association convention in Atlantic City, New Jersey.
Brought home enough orders to keep the company in business.
“Motorola” was created by linking "motor" (for motorcar) with "ola" (from Victrola)
“Motorola” was created by linking "motor" (for motorcar) with "ola" (from Victrola)
Motorola went public in 1943,
became Motorola, Inc. in 1947

## Slide 8: Motorola tried other automotive products
. . . not all were successful.

## Slide 9: A Brief History of Semiconductors from Conception to the first Transistor
Earliest Semiconductor application – Crystal Radio Cat Whisker, point contact rectifier
1909 - Physicist William Eccles discovered the crystal diode oscillator.
1926 - Physicist Julius Edgar Lilienfeld proposed and patented the concept of a field-effect transistor.
1947 - American physicists William Shockley, John Bardeen and Walter Brattain demonstrate point contact transistor at Bell Labs.
1949 - Motorola started a research and development laboratory in Phoenix, Arizona, to research new solid-state technology. (Dan Noble)
1952 April - Over 100 representatives from 40 companies that had paid a $25,000 patent-licensing fee came for a nine-day Transistor Technology Symposium, including a visit to Western Electric's ultramodern transistor manufacturing plant in Allentown, PA.
  There were participants from such electronics titans as GE and RCA, as well as from then-small firms like Texas Instruments and Sony.
1952 – Motorola licenses transistor technology from Bell Labs.
  Early Applications:
    Power Supplies
    Amplifier output stage
    Automotive Alternators
1962 – Motorola Semiconductor had more than 4,000 components in the market.

## Slide 10: Logic

## Slide 11: Logic Family Examples
Transistor Transistor Logic
Metal Oxide Semiconductor Field Effect (MOSFET) Logic
Complementary MOS(FET) Logic
1962 - Motorola introduced MECL I. Their first digital monolithic integrated circuit line.
1966 - MECL II
1968 - MECL III 1-nanosecond gate propagation time and 300 MHz flip-flop toggle rates.
1971 - 10,000 series (lower power consumption and controlled edge speeds)
1981 - The MECL 10H family.
Emitter Coupled Logic
(Current Mode)

## Slide 12: Linear & Interface

## Slide 13: Driven by Mainframe Technology

## Slide 14: Consumer

## Slide 15: Discrete

## Slide 16: Specialty
Vertical
Integration

## Slide 17: Solar Power Systems

## Slide 18: Liquid-Crystal Displays

## Slide 19: Memories
Bubble Memories

## Slide 20: Memory System 3000
Year 1981
2MB Memory Card
12” x 18”
Cost $9,210
16 cards/19in Chassis
32MB/Chassis
Notes: Jeff Nutt – Marketing Manger
Things were different in the 1980s

## Slide 21: Packages – Speed Ranges – Temp Ranges
Temperature Ranges
Commercial: 0 to 70 °C
Industrial: −40 to 85 °C
Military: −55 to 125 °C
One Die could be a dozen parts
Motorola SPS was a broad line supplier with
OVER 25,000 unique products!
Notes: As an FAE, this is what I had to support.
All products over all applications over thousands of customers.
No way I could do this
I was a Paid Professional Data Sheet Reader.

## Slide 22: Processors & Peripherals
6800
6801
6809
6805
68000
8 Bit
4 Bit
16/32 Bit & Peripherals
Intel
8051
146805
CMOS
141000
CMOS (TI)
2900
TTL - AMD
10800
ECL
32-64 Bit
PowerPC
AIM
88000
RISC
Other
DSP56000
24 Bit
DSP96000
96 Bit
DSP56100
16 Bit
LonWorks
Neuron
MC14500
1-Bit
VeCOMP701
Vector
Industrial Control
Notes: Too many processors to list
Intel Processor was 8051. Used in Engine Control for Motorola Seguin.
Who knows about Motorola Seguin? Show of Hands.
Car Radios
Microwave Front Panels
Engine Controls
LonWorks – Neuron Chip
http://147.32.193.59/semi/motorola/books/sg73/pdf/2_7lon_msg.pdf
Highlight the MC14500 – The processor that thought he could.

## Slide 23: MC14500B 1-bit Processor (1977)
Notes: Customer called and asked if there was a floating point package for this chip?
I had to decline

## Slide 24
Vacuum Tube Implementation
MC14500 1-bit Processor Derivatives

## Slide 25: APPLICATIONS
DATAPOINT
San Antonio
Terminals
Networking
Created 8008
PELLERIN MILNOR
New Orleans
Industrial Washers
& Dryers
INTERMEDICS
Freeport
Pacemakers
DISTRIBUTORS
Hall-Mark
Hamilton/Avnet
Schweber
Sterling
OEHLER Research
Austin
Ballistic Testing
NASA
Houston
Texas Instruments
IBM
Austin
National Instruments
Austin
IEEE488 GPIB
Notes: OEHLER – Microprocessor for Machine Gun
Pellerin Milnor – BIG Washing machines. TUNNEL - Converting Relay Logic to Microprocessor
TEXAS INSTRUMENTS – Watch – Mot made LCD, CMOS Clock chip, Crystal They added battery and plastic
IBM – 5.6V Zener diode all 5000 BAD
National Instruments – KC Brown delivered MC68400 GPIB chip to Dr James Truchard on Bee Caves. Now many buildings on MoPac near Domain
NASA – Flew shuttle simulator to reentry – Crashed it
Datapoint – TTY silent replacement, Created 8008 architecture, First NETWORK. ARCNET. Infrared building to building optical connection
Intermedics – Used RCA CMOS processor. Mot would not support life critical applications. Pacemaker programmer 6809 - LAZARUS selection
POSTER – Sears Die Hard

## Slide 26: Digital Signal Processing
Wrote DSP Training Courses - 1987
MTTA5 – Cassette
MTT31 – Instructor led course <- Looking for this
DSP Marketing Manager - 1988
16-Bit - Cellular
24-Bit – Audio Industry Standard
32/96 Bit Floating point
VeComp701 – Vector Computer - 1995
Created largest patent - > 450 citations
Notes: DSP
Bryant Wilder
Paul Marino
Kevin Kloker
Garth Hillman
Keith Essency
Eric Cheval
VeComp
Terry Lawell
Steve Marsh
Bob Seaton
Jason & Terrance Spielman

## Slide 27
https://www.slideserve.com/bailey/video-conferencing-unit
Mirrored Closet Doors
Sony Customer at Home

## Slide 28: 4G LTE Prototype Development & Demo Platform
“Off the shelf” RF, FPGA based baseband
  2 downlink paths, 1 uplink path
Provides an FPGA platform to test RF, DSP and MAC protocol
Provides a test environment to simulate a base station, host processor and RF channel
Provides early demonstrations for checking interoperability
RF Transceiver
PCIX
USB 2.0
JTAG
FPGA Board
Rohde Schwarz CRTU
Protocol Tester
RF Rx Channel 1
Host Processor
RF Interface Board
SPI
RF Rx Channel 2
RF Tx
BB Tx
BB RX Chan 1,2
Elektrobit C8 Fading Simulator
FPGA A
MAC Protocol
Processor
FPGA B
PHY Engine
(MODEM)
FPGA C
Decoder/
Encoder
Test Controller &
Instrumentation Display
Traffic Data
Application Server
Base station emulation
Notes: 135 engineers in 6 design locations
Austin, Toulouse France, Boca Raton Florida, Chicago, Phoenix, San Diego
Feb 2008 - Demoed 4K Video over 4GLTE in Barcelona Spain – World Mobile congress.
We were the only company with such a demo.
Motorola SPS had a great RF team. Sold to Fujitsu.

## Slide 29
Notes: 2008 – Great Recession
March 2009 – 1,800 riffed.

## Slide 30: Motorola Semiconductor Products Sector Split
Power
Analog
Logic
Discrete
LED
Automotive
Networking
Processors
Broadband
RF
Sensors
2006
1999
2015

## Slide 31: THANK YOU For your time

## Slide 32: Links
Fahnestock Clip
https://en.wikipedia.org/wiki/Fahnestock_clip
LonWorks
https://www.csimn.com/CSI_pages/LonWorks101.html
Motorola Wikipedia
https://en.wikipedia.org/wiki/Motorola
Semiconductors
https://www.britannica.com/science/semiconductor
History of Auto Radio
https://blog.consumerguide.com/a-brief-history-of-car-radio/
Motorola Timeline
https://www.landley.net/history/mirror/6800_MotDoc.pdf
Motorola History
https://www.britannica.com/topic/Motorola-Inc
https://www.company-histories.com/Motorola-Inc-Company-History.html
Transistor History
https://en.wikipedia.org/wiki/Transistor
1952 Bell Labs License symposium
https://www.computerhistory.org/siliconengine/bell-labs-licenses-transistor-technology/
1 bit processor
Datasheet
http://ww.bitsavers.org/components/motorola/14500/MC14500B_Rev3.pdf
Handbook
http://www.bitsavers.org/components/motorola/14500/MC14500B_Industrial_Control_Unit_Handbook_1977.pdf
Discreet version
https://www.youtube.com/watch?v=BJSHJkaYqaE
Motorola Video Conferencing
https://www.slideserve.com/bailey/video-conferencing-unit

## Slide 33
Notes: ARPANET - Advanced Research Projects Agency Network (the World's first operational packet switching network)
Department of Defense
Approx 150 systems online
PENTAGON – MILITARY – UNIVERSITY
NOTE – Mystery TEXAS node
MORE NODES IN THIS BUILDING THAN THE ENTIRE INTERNET BACK THEN

## Slide 34: Interface Message Processor
LINK:
https://en.wikipedia.org/wiki/ARPANET
Notes: ARPA awarded the contract to build the network to Bolt Beranek & Newman who developed the first protocol for the network
Required Interface Message Processor (GIANT BOX) to connect.
TIMELINE
1969 – First Connect
1971 – Declared operational
I HAD NOTHING TO DO WITH THIS.
Just an interesting fact.