## Slide 1: Spectrum Database Interfaces – Data Structures
Sajeev Manikkoth
IEEE 1900.6
DCN 6-16-0038-00-CNTS

## Slide 2: Spectrum Databases
Spectrum Database – “An entity that contains current information about available spectrum at a given location and time, as well as other types of information related to spectrum availability and usage.”
Details Spectrum Databases require from Sensors
  Available spectrum/channels or whitespace
  Permissible transmission power levels
  RF Noise levels
  Contextual Info – location, time, antenna height, user priority (primary/secondary/tertiary)
  Accuracy or certainty of info
Requirements from Upstream Databases
Geolocation Regulatory Databases
PAWS RFC 6953 and RFC 7545

## Slide 3: Typical Deployment
Spectrum DB
Geolocation DB
(Regulatory)
Whitespace Radio/AP
PAWS RFC 7545
IEEE 1900.6b
Spectrum Sensing System

## Slide 4: PAWS Parameters
Regulatory Domain (FCC, ETSI, etc.)
Ruleset, Supported Ruleset Ids - RuleSetInfo
Geo-location - GeoLocation
  Single point or a Region polygon with percentage confidence
Available spectrum
  SpectrumSpec
    Spectrum Schedules, Time Range, Frequency Range, MaxTotalBwHz, MaxContiguousBwHz
  GeoSpectrumSpec
    GeoLocation, SpectrumSpec

## Slide 5: PAWS Data Types
JSON encoded data
1. string: A string, as defined by JSON [RFC7159], restricted to the UTF-8 encoding.
2. int: A number, as defined by JSON without a fractional or exponent part.
3. float: A number, as defined by JSON
4. boolean: A boolean, as defined by JSON
5. list: A structured type that represents a list of elements, as defined by JSON array type. All elements of the list are of the same data type
All parameter names are case sensitive. All timestamps are in UTC and are expressed using exactly the form, YYYY-MM-DDThh:mm:ssZ, as defined by "Date and Time on the Internet: Timestamps" [RFC3339].

## Slide 6: Spectrum Schedule
EventTime : EventTime
  startTime : string
  stoptime : string
Spectra : list
  Spectrum : list
    ResolutionBwHz : float
    Spectrum Profiles : list
      Hz :float
      Dbm : float

## Slide 7: Example
Over any 6 MHz within the frequency range [518 MHz, 530 MHz), maximum permitted power is 30.0 dBm (1000 mW)
[
  {
  "resolutionBwHz": 6e6,
  "profiles": [
  [
  {"hz": 5.18e8, "dbm": 30.0},
  {"hz": 5.30e8, "dbm": 30.0}
  ],
  ...
  ]
  }
  ]

## Slide 8: Contd..
Over any 6 MHz within the frequency range [518 MHz, 530 MHz), maximum permitted power is 30.0 dBm (1000 mW), and over any 100 kHz within the frequency range [518 MHz, 530 MHz), maximum permitted power is 27.0 dBm (500 mW)
[
  { "resolutionBwHz": 6e6,
  "profiles": [
  [
  {"hz": 5.18e8, "dbm": 30.0},
  {"hz": 5.30e8, "dbm": 30.0}
  ], ...
  ] },
  { "resolutionBwHz": 1e5,
  "profiles": [
  [
  {"hz": 5.18e8, "dbm": 27.0},
  {"hz": 5.30e8, "dbm": 27.0}
  ], ...
  ] } ]

## Slide 9: GeoLocation
Point : Ellipse
    center : point
      Latitude : float
      Longitude : float
    semiMajorAxis : float
    semiMinrAxis : float
    Confidence : float
Region : Polygon
    Exterior : list
      Latitude : float
      Longitude : float
Confidence : int

## Slide 10: PAWS Protocol Functionalities
spectrum.paws.init
  INIT_REQ
  INIT_RESP
spectrum.paws.register
  REGISTRATION_REQ
  REGISTRATION_RESP
spectrum.paws.verifyDevice
  DEV_VALID_REQ
  DEV_VALID_RESP

## Slide 11: Protocol Functionalities
spectrum.paws.getSpectrum
  AVAIL_SPECTRUM_REQ
  AVAIL_SPECTRUM_RESP
spectrum.paws.getSpectrumBatch
  AVAIL_SPECTRUM_BATCH_REQ
  AVAIL_SPECTRUM_BATCH_RESP
spectrum.paws.notifySpectrumUse
  SPECTRUM_USE_NOTIFY
  SPECTRUM_USE_RESP

## Slide 12: Request Example
{
"jsonrpc": "2.0",
"method": "spectrum.paws.getSpectrum",
"params": {
"type": "AVAIL_SPECTRUM_REQ",
"version": "1.0",
"deviceDesc": {
"serialNumber": "XXX",
"fccId": "YYY",
"rulesetIds": ["FccTvBandWhiteSpace-2010"]
},
"location": {
"point": {
"center": {"latitude": 37.0, "longitude": -101.3}
}
},
"antenna": {"height": 10.2, "heightType": "AGL"}
},
"id": "xxxxxx"
}

## Slide 13: Contd..
[
{"hz":6.20e8, "dbm":30.0},
{"hz":6.26e8, "dbm":30.0}
],
...
]
}
]
},
{
"eventTime": {
"startTime": "2013-03-02T22:00:00Z",
"stopTime": "2013-03-03T14:30:21Z"
},
"spectra": [
...
]
}
]
}
]
},
"id": "xxxxxx"
}

## Slide 14: Response Example
{
"jsonrpc": "2.0",
"result": {
"type": "AVAIL_SPECTRUM_RESP",
"version": "1.0",
"timestamp": "2013-03-02T14:30:21Z",
"deviceDesc": {
"serialNumber": "XXX",
"fccId": "YYY",
"rulesetIds": ["FccTvBandWhiteSpace-2010"]
},
"spectrumSpecs": [
{
"rulesetInfo": {
"authority": "us",
"rulesetId": "FccTvBandWhiteSpace-2010"
},
"needsSpectrumReport": false,
"spectrumSchedules": [
{
"eventTime": {
"startTime": "2013-03-02T14:30:21Z",
"stopTime": "2013-03-02T20:00:00Z"
},
"spectra": [
{
"resolutionBwHz": 6e6,
"profiles": [
...
[
{"hz":5.18e8, "dbm":30.0},
{"hz":5.36e8, "dbm":30.0},
{"hz":5.36e8, "dbm":36.0},
{"hz":5.42e8, "dbm":36.0}
],

## Slide 15: IEEE 1900.6 Parameters
Functional
  GeoLocation, Depth/Height
  EventTime, Timestamp
  Spectrumspec
  GeoSpectrumSpec
  RuleSetInfo
  Regulatory Domain
  Accuracy or Confidence level
Informational
  SensorSpec
    Sensor Id
    Sensor Owner
    Sensor Type
    Operating band
    Update method / frequency
  DatabaseSpec
    Spectrum Database Id
    Spectrum Database URI
    Spectrum Database Owner

## Slide 16: Questions on 1900.6b
How will sensors know which DB to use? Registration, Initialization, Change of DB, etc.
Publish-Subscribe/Request-Response or Both?
Delta update or full info always?
Pure text data or Binary encoded data
Error handling and error codes