## Slide 1
Minseok OH, Namgi KIM
Kyonggi University
IEEE 802.11ay for Wireless VR

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html

## Slide 3
Introduction of IEEE 802.11ay for Wireless VR |  |  | 
Date: 2017-07-25 |  |  | 
Author(s): |  |  | 
Name | Affiliation | Phone [optional] | Email [optional]
Minseok OH | Kyonggi University |  | msoh@kgu.ac.kr
Namgi KIM | Kyonggi University |  | ngkim@kgu.ac.kr
IEEE P3333.3 HMD Based 3D Content Motion Sickness Reducing Technology
[Dongil Seo, Dillon@volercreative.com]

## Slide 4: Abstract
IEEE 802.11ay has been working on PHY and MAC to support at 20 Gbps (at MAC SAP)
IEEE 802.11ay defines operations for license-exempt bands above 45 GHz, while ensuring backward compatibility and coexistence with legacy directional multi-gigabit stations (defined by 802.11ad)
Along the augmented capacity provided by the addition of IEEE 802.11 directional multi-gigabit devices, WLAN usage continues to grow and find new applications, such as wireless VR/AR demanding additional capacity
Many wireless HMDs in the market use 802.11ad standard at 60 GHz
TPCast, KwikVR, DisplayLink XR, IMR, etc.
Many wireless HMDs is expected to follow the post-802.11ad standard for their wireless part

## Slide 5: IEEE 802.11ay Use Case for AR/VR [1]
Pre-Conditions:
The high-end wearable (e.g. AR/VR headsets, etc.) and its managing device (e.g. gaming console, smartphone, etc.) are equipped with 11ay interfaces and form a PBSS (Personal BSS).
All desired media content, processing power, and control needed by the high-end wearable resides within the managing device (i.e., the Internet connectivity not required).
Application:
A user plays a game, watches a movie, etc. using his high-end wearable, which is communicating with the managing device.
Both devices must be able to tolerate moderate user movement.
Data rate at ~20 Gbps, latency < 5 ms, jitter <5 ms, PER < 10E-2
Notes: One of 9 use cases developed in 802.11ay TG

## Slide 6: IEEE 802.11ay Use Case – cont’d
Environment:
The high-end wearable may be used at home or in public.
At home, there are less than 4 interferers.
In public (e.g. commuter train) there can be up to 120 interferers.
Interferers have varying QoS requirements.
Transmissions (both desired signal and interference) can be LOS or NLOS.
The D2D link between the high-end wearable and its managing device < 5 m.

## Slide 7: IEEE 802.11ay Use Case – cont’d
Traffic Conditions:
The D2D link may be obstructed (i.e. NLOS) and there may be significant interference from other 11ay users (e.g. other wearables, access points, etc.)
Devices may be stationary or moving (pedestrian speed) while in use.

## Slide 8: IEEE 802.11ay Use Case – cont’d
Use Case:
A passenger on a crowded commuter train is playing a game using his AR/VR headset and smartphone.
Some percentage of his fellow passengers are also playing a game using their AR/VR headsets and smartphones.
All passengers are semi-stationary, i.e. they shift and move in response to the game.
The QoS/QoE requirements of the gaming application are met.

## Slide 9: IEEE 802.11ay Use Case – cont’d
High-end wearable and its managing device may both be subject to low level movement.
Operating environment is usually indoor < 5 m.
AR/VR headsets touting close-to-reality user experience with 3D video and 7.1 audio.
Video quality can support up to 3D 4K.
Features | Requirements | Notes
Distance | 5 m | 
Video Quality | 3D 4K | HDMI 2.0
Range of Motion for head-worn wearable | Neck Roll | 0.17 (s/60deg)
 | Neck Pitch | 0.14(s/60deg)
 | Neck Yaw | 0.13 (s/60deg)
Device mobility | Pedestrian speeds | < 4 km/hr

## Slide 10: Functional Requirements [2]
Maximum throughput
At least 20 Gbps, as measured at the MAC data service access point (SAP).
Coexistence
Support backward compatibility with legacy directional multigigabit (DMG) devices (IEEE 802.11ad) operating in the same band.
Support coexistence with legacy devices operating in the same band.

## Slide 11: Functional Requirements – cont’d
Range
At least 10 meters in an indoor environment and at least 100 meters in an outdoor environment.
Power Efficiency
At least the same power efficiency per STA as legacy DMG devices (11ad).
Note that 802.11ad does not assert any power consumption requirements. [3]

## Slide 12: Functional Requirements – cont’d
Video Requirements
Support lightly compressed 4K and 8K UHD video for data rate, packet loss rate, delay measured at MAC SAP
Parameter | Value | Description
Data rate | 1.5 Gbps (Peak) | 4K UHD 2160p (RGB): 3840x2160 pixels, 24 bits/pixels, 60 frames/s, 8 bit per color
Packet loss rate | 1e-8 | 
Delay | 10 ms | 
Parameter | Value | Description
Data rate | 8.0 Gbps (Peak) | 8K UHD 4320p (RGB): 7680x4320 pixels, 24 bits/pixels, 60 frames/s, 8 bit per color
Packet loss rate | 1e-8 | 
Delay | 10 ms | 

## Slide 13: Functional Requirements – cont’d
Video Requirements
Support uncompressed 4K and 8K UHD video for data rate, packet loss rate, delay measured at MAC SAP
Parameter | Value | Description
Data rate | 18.0 Gbps | 4K UHD uncompressed 3840x2160 pixels, 30 bits/pixels, 60 frames/s, 8 bit per color. Chroma subsampling (4:4:4)
Packet loss rate | 1e-8 | 
Delay | 10 ms | 
Parameter | Value | Description
Data rate | 28.0 Gbps | 8K UHD uncompressed 7680x4320 pixels, 24 bits/pixels, 60 frames/s, 8 bit per color. Chroma subsampling (4:2:0)
Packet loss rate | 1e-8 | 
Delay | 10 ms | 

## Slide 14: Functional Requirements – cont’d
Fast Link Setup
Provides a means of providing secure fast link setup
Outdoor Support
Provides a means of supporting outdoor operations
Mobility Support
Provides mobility operations at a pedestrian speed (e.g., 3 km/h) or body movements (i.e., neck roll, neck pitch, neck yaw)

## Slide 15: TGay in progress
The TG still receives use cases.
Wireless backhaul use case has been enhanced with a new requirement in July meeting.
More comprehensive requirements can be added to 11ay to better support for wireless VR.

## Slide 16: Development Timeline
PAR approved: 3/2015
Draft 1.0: 11/2017 (shifted by 4 months in July meeting)
Draft 2.0: 3/2018 (shifted by 4 months in July meeting)
Letter ballot: 11/2017 – 3/2019
WG approval: 9/2019
RevCom approval: 11/2019
Jul
14
Oct
14
Jan
15
Apr
15
Jul
15
Oct
15
Jan
16
Apr
16
Jul
16
Oct
16
Jan
17
Apr
17
Jul
17
Oct
17
Jan
18
Apr
18
Jul
18
Oct
18
Jan
19
Apr
19
Jul
19
Oct
19
May
14
802
.
11
SG vote
Sep
14
NG
60
SG formed
Mar
15
PAR approval
May
15
11
ay formed
Jan
17
D
0
.
1
Jul
17
D
1
.
0
May
17
D
0
.
5
Nov
17
D
2
.
0
Sep
14
-
Mar
15
Use cases
,
PAR
/
CSD
May
15
-
Dec
15
Development
of TG docs
Sep
15
-
May
17
SFD
Jul
17
-
Dec
19
Balloting process

## Slide 17: References
[1] https://mentor.ieee.org/802.11/dcn/15/11-15-0625-04-00ay-ieee-802-11-tgay-usage-scenarios.pptx
[2] https://mentor.ieee.org/802.11/dcn/15/11-15-1074-00-00ay-11ay-functional-requirements.docx
[3] https://mentor.ieee.org/802.11/dcn/09/11-09-0228-05-00ad-functional-requirements.doc