## Slide 1
Suk-Ju Kang, Sogang University
Efficient Image Interpolation Using Deep Learning for Virtual Reality

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html

## Slide 3
Efficient Image Interpolation for Virtual Reality Using Deep Learning |  |  | 
Date: 2018-10-06 |  |  | 
Author(s): Suk-Ju Kang |  |  | 
Name | Affiliation | Phone [optional] | Email [optional]
Suk-Ju Kang | Sogang University | +82-10-7103-6520 | sjkang@sogang.ac.kr
IEEE 3079 Cybersickness Reduction Working Group
[Dong Il Seo and dillon@volercreative.com]

## Slide 4: Outline
Introduction
Motivation
Proposed Hardware Architecture
Experimental environments and results
Summary

## Slide 5: Introduction
The low-cost HMD systems with a novel optical structure have been presented by several companies

## Slide 6: Motivation
Motion-to-Photon latency is the time needed for a user movement to be fully reflected on a display screen.
Low motion-to-photon (< 20ms) latency is a prerequisite to convince user’s mind that user is in another place.
A high motion-to-photon latency makes a poor virtual reality experience.
Tracker
CPU
GPU
Display
Photons
Optics
Head motion
User’s retina
Under 20 milliseconds of latency for comfortability

## Slide 7: Motivation
A challenge of Virtual Reality
  Users feel gaps on their sense between the reality and virtual reality because of a motion-to-photon latency
  This causes dizziness and motion sickness to user
Motion-to-photon latency must be compensated!
Problems from latency of HMD
Motion sickness
Dizziness
Human perception
Blurring
Image judder

## Slide 8: Motivation
Convolutional neural networks (CNN) can solve the problems faced by existing machine learning algorithms in such as object recognition and natural language processing, etc.

## Slide 9: Proposed HMD System
Distorted Stereoscopic Image

## Slide 10: Proposed HMD System

## Slide 11: Proposed HMD System
Distorted Stereoscopic Image

## Slide 12: Proposed HMD System (Background)
Especially, deconvolutional neural networks (DCNN) are mainly used to reconstruct target images in image enhancement applications.
Convolution +
Activation
Convolution +
Activation
Deconvolution +
Activation

## Slide 13: Proposed HMD System (Background)
FSRCNN*
  Deep networks (7 CNN + 1 DCNN)
  More cost effective than SRCNN, but it’s even better.
*C. Dong, et al. Accelerating the super-resolution convolutional neural network. In Springer ECCV 2016.

## Slide 14: Proposed Hardware Architecture
Output image
Filter
Input image
Convolution in CNN

## Slide 15: Proposed Hardware Architecture
Output image
Filter
Input image
Convolution in CNN

## Slide 16: Proposed Hardware Architecture
Output image
Filter
Input image
Deconvolution in DCNN

## Slide 17: Proposed Hardware Architecture
Output image
Filter
Input image
Deconvolution in DCNN

## Slide 18: Proposed Hardware Architecture
Problems with DCNN
  Overlapping sum problem
  Loop dimensions
Need to sum these overlaps up

## Slide 19: Proposed Hardware Architecture
Problems with DCNN
  Overlapping sum problem
  Loop dimensions
<General CNN Acceleration system>
Off-chip
Memory
On-chip
Memory
Registers & Processing Engine Arrays
Pixels
Weights
Pixels
Pixels
Weights
Pixels
Pixels
Weights
Pixels
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE

## Slide 20: Proposed Hardware Architecture
Problems with DCNN
  Overlapping sum problem
  Loop dimensions
<General DCNN Acceleration system>
Off-chip
Memory
On-chip
Memory
Registers & Processing Engine Arrays
Pixels
Weights
Pixels
Pixels
Weights
Pixels
Pixels
Weights
Pixels
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE

## Slide 21: Proposed Hardware Architecture
Problems with DCNN
  Overlapping sum problem
  Loop dimensions
Deconvolution

## Slide 22: Proposed Hardware Architecture
Problems with DCNN
  We solve these problems using TDC method*.
*Chang, et al. Optimizing FPGA-based convolutional neural networks accelerator for image super-resolution. In IEEE/ACM ASP-DAC 2018.
Deconvolution→Convolution

## Slide 23: Experimental Environments
Hardware Implementation Tool
  High-Level Synthesis
  Vivado HLS 2016. 4
  Xilinx Virtex-7 485T FPGA
  Single-precision floating point
CNN model
  FSRCNN
    7 convolution + 1 deconvolution

## Slide 24: Experimental Results
TDC Method
  Loop tiling factor (Tn, Tm) was set to (56, 9).
  Two reasons for the increase in the throughput
    Kernel size
    Resource underutilization problem is resolved
12.96
8
7
[1]
[1]X. Zhang, et al. A design methodology for efficient implementation of deconvolutional neural networks on an FPGA. In arxiv: 1705.02583.

## Slide 25: Experimental Results
Latency
Execution time
Conv1
Conv2
Conv3
Conv4
Conv5
Conv3
Conv3
Conv1
Conv2
Conv1
Conv2
Conv1
Conv2
Conv5
Conv4
Conv4
Conv3
Conv1
Conv2
Conv5
Conv4
Timeline
Conv1
Conv2
Conv3
Conv4
Conv5
Conv3
Conv3
Conv1
Conv2
Conv1
Conv2
Conv1
Conv2
Conv5
Conv4
Conv4
Conv3
Conv1
Conv2
Conv5
Conv4
Timeline
QHD 21.27ms(×2)
9.45ms(×3)
5.34ms(×4)
QHD 7.09ms(×2)
3.15ms(×3)
1.78ms(×4)

## Slide 26: Experimental Results
FPGA Utilization (130MHz)
FPGA resources 사용량

## Slide 27: Summary
Propose the TDC Method based DCNN Accelerator.
  Improves throughput and could resolve the spatial problem.
  Increase the parallelism of the output feature maps.
  Outperform the state-of-the-art DCNN accelerator up to 81.
Propose the DNN-based Efficient Architecture.
  Implement FSRCNN on Xilinx Kintex-7 FPGA.
  Resolve the motion-to-photon latency in VR.