## Slide 1: Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience
Presenter: Jong-Beom Jeong (uof4949@skku.edu)
Tuan Thanh Le, Jong-Beom Jeong, Soonbin Lee, Il-Woong Ryu, Sungbin Kim, Inae Kim, Eun-Seok Ryu
Multimedia Computing Systems Lab. (MCSL)
http://mcsl.skku.edu
Department of Computer Education
Sungkyunkwan University

## Slide 2: Compliance with IEEE Standards Policies and Procedures
Subclause 5.2.1 of the IEEE-SA Standards Board Bylaws states, "While participating in IEEE standards development activities, all participants...shall act in accordance with all applicable laws (nation-based and international), the IEEE Code of Ethics, and with IEEE Standards policies and procedures."
The contributor acknowledges and accepts that this contribution is subject to
The IEEE Standards copyright policy as stated in the IEEE-SA Standards Board Bylaws, section 7, http://standards.ieee.org/develop/policies/bylaws/sect6-7.html#7, and the IEEE-SA Standards Board Operations Manual, section 6.1, http://standards.ieee.org/develop/policies/opman/sect6.html
The IEEE Standards patent policy as stated in the IEEE-SA Standards Board Bylaws, section 6, http://standards.ieee.org/guides/bylaws/sect6-7.html#6, and the IEEE-SA Standards Board Operations Manual, section 6.3, http://standards.ieee.org/develop/policies/opman/sect6.html
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience

## Slide 3: IEEE 3079 HMD Based VR Sickness Reducing Technology Dongil Dillon Seo, dillon.seo@telekom-capital.com
Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience |  |  | 
Date: 2020-07-09 |  |  | 
Author(s): Tuan Thanh Le, Jong-Beom Jeong, Soonbin Lee, Il-Woong Ryu, Sungbin Kim, Inae Kim, Eun-Seok Ryu |  |  | 
Name | Affiliation | Phone [optional] | Email [optional]
Tuan Thanh Le | Gachon Univ. |  | 
Jong-Beom Jeong | Sungkyunkwan Univ. |  | uof4949@skku.edu
Soonbin Lee | Sungkyunkwan Univ. |  | 
Il-Woong Ryu | Gachon Univ. |  | 
Sungbin Kim | Sungkyunkwan Univ. |  | 
Inae Kim | Sungkyunkwan Univ. |  | 
Eun-Seok Ryu | Sungkyunkwan Univ. |  | esryu@skku.edu
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience

## Slide 4: Challenges
High Bandwidth Requirement of VR
  Requires 40 pix/deg, 12K resolution for High quality VR
  To avoid the sickness, 90 fps and 20 ms MTP are required
  Immersive video contains texture (color) and depth (geometry) -> (×2)
  Also, immersive video has high quality (nearly 4K) multiple views -> (×N) -> Requires high bandwidth
Requirements for high quality VR
Source: Mary-Luc Champel, Thomas Stockhammer, Thierry Fautier, Emmanuel Thomas,
and Rob Koenen. “Quality Requirements for VR”, document MPEG116/m39532,
116th MPEG meeting of ISO/IEC JTC1/SC29/WG11.
Characteristics of immersive video
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience

## Slide 5: Virtual Reality Streaming Technologies
Viewport Adaptive Streaming
Motion Constrained Tile Sets (MCTS) refer to the encoder for time and space movement reference for independent tile transfer within the current location tile
Extract and composite specific tiles from the bitstream with MCTS to form an adaptive environment at the time of the user
Reduce bandwidth when sending only tiles that correspond to a user’s area of interest
Ensure independence between tiles
…
Motion Constrained Tile Sets
Tile/ Slice | Tile/ Slice | Tile/ Slice
Tile/ Slice | Tile/ Slice | Tile/ Slice
Tile/ Slice | Tile/ Slice | Tile/ Slice
viewport
Viewport-adaptive decoding and rendering
Viewport
Tiles
viewport
Viewport-driven tiled streaming system based on MCTS
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience

## Slide 6: VR Tiled Streaming Latency
We define latency as the total time between movement of the user’s head and the updated image being displayed on the screen
It includes the times for sensor response, fusion, rendering, image transmission, and display response
+ + + +
Head’s movement
Client request
Server Listen
Output Tiled Bitstream
Client received tiled bitstream
Decoding & Rendering VR-HMD
Processing latency
Request Latency
Processing latency
Transmission Latency
Processing latency
( is quite small)
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience

## Slide 7: VR Tiled Streaming System Architecture
File encapsulation
Delivery (MPEG DASH/ RTSP/RTP)
DASH/RTSP/RTP
Client
Prediction Model
Adaptive Network Bandwidth Model
Tile Priority Generator
VR rendering
File
decapsulation
Decoding,
mapping
Tile selection,
chunk request
viewport
Server Listen
Client Request
Selected Tiles
Head’s movement
Streaming Server
PC - Client
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience

## Slide 8: Opportunities for Research
viewport
viewport
Head’s movement
Optimizing size of tiles
  Adaptive Bandwidth
  Reduce latency (∆𝑡_3, ∆𝑡_4 and ∆𝑡_5)
Head’s movement prediction
  According to eyes-coordinates function and a prediction model
  Decide the next tiles of new tiled stream
  Reduce latency (∆𝑡_1)
High quality and low-quality streams
  Instead of requesting a new chunk, client uses low-quality tiles at exact same location
  Reduce latency (∆𝑡_1, ∆𝑡_3,∆𝑡_4, and ∆𝑡_5)
3079-20-0029-02-0003 Latency for Viewport-adaptive 360-degree Video Streaming Toward Immersive Experience