## Slide 1: IEEE802 as a Component of 5G
Date: 2016-05
Authors:
Name | Affiliation | Email
Yonggang Fang | ZTE TX | yfang@ztetx.com
Li Zhang | ZTE Corporation | Zhangli2@zte.com.cn
Bo Sun | ZTE Corporation | Sun.bo1@zte.com.cn
Zhendong Luo | CATR | luozhendong@catr.cn
Xia Shen | CATR | shenxia@catr.cn

## Slide 2: Understanding of 5G
    5G
      5G refers to the term of next generation telecommunication involved from previous generations like 4G, 3G. The original meaning of 5G is related and refer to International Mobile Telecommunication (IMT). But it could be expanded.
      Multiple industry forum and SDOs are working on 5G
        Industry: NGMN, 5G PPP, METIS II, FANTASTIC 5G, 5G-EX, 5G Forum
        SDO: ITU/IMT2020, 3GPP (SA1, SA2, SA5), ETSI/NFV, IEEE802
      5G in ITU-R would represent the global agreement by industries including major operators and vendors, SDOs and governments for the next generation of telecommunication systems.
      According to the timeline of ITU-R, the WP5D has started to draft IMT-2020 requirements, evaluation criteria and submission at the 23rd meeting on Feb 2016.
      IEEE 802 is at the time to decide whether and how to participate the ITU-R 5G development.

## Slide 3: Why Joining 5G
    Market Segment
      IEEE 802.11 is designated for wireless local area network, and mainly targets at consumer markets. It provides simple and low cost solution of wireless access for those type of electronic devices.
      IEEE802.11 is currently not under IMT, but IEEE802.11 technologies contribute a large portion of data volume of global internet traffic, much more than IMT labeled cellular networks.
    Technology Assurance
      As ITU-R IMT-2020 will specify wireless technologies for many traditional IEEE802.11 use cases, joining ITU-R will help the widely used IEEE 802.11 technologies to be accepted globally and make future IEEE802.11 technologies continuously adopted by the industries around the world.
      Assure IEEE 802 technology coexistence with other 5G technologies

## Slide 4: ITU and ITU-R
    ITU
      ITU is the leading United Nations agency for information and communication technology and the global focal point for governments and the private sector in developing networks and services. The related sectors are
        Radiocommunication Sector (ITU-R),
        Telecommunication Standardization Sector (ITU-T)
    ITU-R
      ITU-R plays an essential role in the management of the radio-frequency spectrum resources to meet demand from a large number of services such as fixed, mobile, broadcasting, amateur, global positioning systems, etc
      It develops and adopts the ITU Radio Regulations to govern the use of radio-frequency spectrum adopted by the members around the world, and propose to the WRC for review and revise.
      Study Groups established and assigned study Questions by a Radiocommunication Assembly (RA) to prepare draft Recommendations for approval by ITU Member States. The related SG is
        SG 5 for terrestrial services

## Slide 5: ITU-R
    ITU-R WP 5D
      Responsible for investigating issues related to the terrestrial component of IMT, including technical, operational and spectrum-related.
        Spectrum Aspects: Frequency Arrangements, Sharing Studies, etc
        Technology Aspects: IMT Specifications,
        Radio Aspects:
      IMT2000 (M.1457)
        It is specification of the terrestrial radio interfaces of IMT
          CDMA direct Spread
          CDMA Multi-Carrier
          CDMA TDD
          TDMA Single Carrier
          FDMA/TDMA
          OFDMA TDD WMAN
      IMT Advanced (M.2012)
        It is specification of the terrestrial radio interfaces of IMT
          LTE-Advanced and WirelessMAN-Advanced
      IMT2020 is the project of next mobile telecommunication

## Slide 6: ITU-R
    ITU-R WP 5A
      responsible for land mobile service excluding IMT, including
        amateur and amateur-satellite service
        Radio Local Access Network (RLAN), including the wireless communication over unlicensed band such as 2.4GHz, 5GHz, TV white space band,
        Public protection and disaster relief communications (PPDR)
      M.1450
        Characteristics of broadband radio local area networks, including
          IEEE 802.11-2012
          IEEE 802.11ad
          IEEE 802.11ac

## Slide 7: Spectrum Allocation Discussion
    WRC
      World Radio Conference (WRC) is responsible to update radio regulations and adopts resolutions and recommendations.
        The spectrum allocation is determined by each region or government, but its decision would be influenced and based on the global spectrum allocation defined by WRC.
      WRC-19 AI 1.13 will determine the spectrum needs for the terrestrial component of IMT in the frequency range between 24.25 GHz and 86 GHz, the deployment scenarios for IMT-2020 systems and the related requirements of high data traffic.
        28 GHz is not identified for study item at ITU, but as for global primary mobile.
        60 GHz band is not in study item, but is identified as ISM bands,
      WRC-19 AI 1.16 will consider in the demand for Wireless Access Systems including radio local area networks (WAS/RLAN) applications with multimedia capabilities for the spectrum between 5.350 – 5.460GHz, 5.460 – 5.470GHz for sharing with primary EESS, and 5.725 – 5.850GHz/5.825 – 5.925GHz for sharing with primary FSS.

## Slide 8: Spectrum Allocation Discussion
    Spectrum allocation
      ITU-R Study Group is assigned by ITU-R RA to study the topic related to agenda items of WRC and provide the Resolutions and Recommendations to ITU-R as input to WRC-19.
      In current ITU-R organization structure,
        WP5D is responsible for IMT systems on the licensed spectrum. Therefore it develop the Resolutions and Recommendation for IMT-2020 on identified spectrum by WRC.
        WP5A is responsible for all non-IMT radio telecommunication systems, which are operated on licensed exempt spectrum, such as 5.150GHz – 5.925GHz. Some portion in the unlicensed spectrum could be shared with other radio communication systems.

## Slide 9: 5G Use Case and Requirements
    5G Use Cases
      Broad access in the dense areas and everywhere
      Higher user mobility
      Massive IoT
      Extreme real-time communication
      Ultra-reliable communications
      Etc
    5G requirements
      data rate: 1 - 10Gbps
      Capacity: 36TB/month/user
      Energy efficiency: 10% of today’s consumption
      Latency : ~ 1ms
      Reliability: 99.999% within time budget
      Density: 300k devices per access node
      etc

## Slide 10: Approaches toward 5G
    Approaches identified by IEEE 802 EC SC
      IEEE 5G:
        this is an evolution of telecommunication defined within IEEE/IEEE802. It may not be related to ITU-R/WP5D IMT evolution.
      IMT2020 – single technology
        IEEE/IEEE802 will participate ITU-R/WP5D and submit a proposal of single solution to ITU-R IMT2020
      IMT2020 – a set of technology
        IEEE/IEEE802 will participate ITU-R/WP5D and submit a proposal of set of technologies to ITU-R IMT-2020.
      IMT2020 – a component of external party
        Joint activity with external SDO (i.e. 3GPP) about IEEE802 technology for ITU-R/WP5D IMT2020 submission.

## Slide 11: Approach Analysis (1)
    IEEE 5G
  It is an independent evolution defined within IEEE/IEEE802.
  It may not be related to ITU-R IMT evolution.
  Benefits:
    IEEE/IEEE802 may have its own evolution time line, which might be different from ITU-R.
    Each IEEE Society or SDO WG could evolve independent and easily.
  Costs:
    May not be able to get stamp of ITU-R 5G
    It would be difficult to meet all the 5G requirements according to the current IEEE802 scope.
    Requires a lot of work to complete end to end solution for 5G networks.
    Not sure how to align with industries to get global accepted spectrum.

## Slide 12: Approach Analysis (2)
    IMT 2020 – as a single technology
      Need to be proposed by IEEE/IEEE802
        One radio interface to be selected
          802.11, or 802.15.4, or …
        Require a complete proposal to ITU-R/WP5D IMT2020
      Benefits:
        IEEE 802 could be as an independent technology in the ITU-R/WP5D 5G
        Help to promote IEEE802 in 5G branding
      Costs:
        It would be difficult for single technology of IEEE802 to cover all the aspects of IMT2020.
        IEEE802 lacks of network specification to support 5G end to end solutions.
        IEEE802.16 as a single technology specified in IMT2000 and IMT-Advanced may cover IMT scenario, but lacks of market supports in future.

## Slide 13: Approach Analysis (3)
    IMT 2020 – as a set of technologies
      Need to be proposed by IEEE/IEEE802
        At least one radio interface to be selected
          IEEE 802.11, IEEE 802.15, etc
        Management and Control
        Backhaul and fronthaul
          IEEE 802.1/3, IEEE 802.11, etc
      Benefits:
        As IEEE 802 technologies covers different areas, IEEE802 as a set of technologies for IMT 2020 could help to cover different aspect of 5G requirements and scenario.
        Help to promote IEEE802 in global 5G branding
        May help ITU-R to study the need of new spectrum for IMT-2020
      Costs:
        Need more involvement to evaluate and select IEEE802 technologies
        Coordinate in IEEE802 to complete the standardization work (i.e. final publication) before the ITU-R/WP5D IMT2020 deadline.

## Slide 14: Approach Analysis (4)
    IMT 2020 – external party (e.g., 3GPP)
      IEEE802 is as a part of 5G radio and networks of other technologies.
        Radio interface
          IEEE802.11 as LWA or (e)LWIP
        Network management and control
          under external party’s submission.
        Back haul and front haul
          under external party’s submission
      Benefits:
        IEEE802 is as a component in ITU-R 5G architecture, and gain 5G branding
        Align with the current scope of IEEE802 SDO: PHY and MAC
        Help ITU-R to study the need of new spectrum for IMT2020
        The least effort among four approaches
      Costs:
        IEEE 802 needs to incorporate with the external body (i.e. 3GPP) for submission of IMT-2020 proposal in ITU-R.

## Slide 15: Proposal of Approach (5)
    IEEE802 as a Component for ITU-R non-IMT 5G
      Analyze use cases and requirements for ITU-R 5G
      Submit proposals to ITU-R WP5A WAS/RLAN as a complementary solution of IMT-2020
      Possible IEEE802 technology for component of 5G
        Radio interface
          IEEE802.11, IEEE802.15, etc
        Network management and control (TBD)
        Back haul and front haul
          IEEE 802.1/3, IEEE 802.11, etc
      Benefits:
        Align ITU-R WP5A scope for non-IMT systems: WAS/RLAN
        May identify some use cases and requirements for non-IMT 5G services.
        Support new spectrum sharing mechanism with other technologies
        Promote IEEE802 in ITU-R 5G branding complementary to IMT-2020
      Costs:
        Requires more work than the approach 4.

## Slide 16: Conclusion
    Participate ITU-R IMT-2020
      WP5D will develop IMT-2020 (and update IMT-2000 and IMT-Advanced standards), over possible IMT bands identified by WRC.
      Approach 4, i.e. joining with 3GPP as a component of 5G might be an easy way for IEEE802 to get ITU-R 5G stamp for next generation of telecommunication systems.
        Note: It might not help to acquire new spectrum in unlicensed band
    Participate ITU-R non-IMT
      Align with ITU-R current scope of Radio telecommunication in unlicensed spectrum and inherit IEEE802 technologies in ITU-R
      Promote spectrum sharing over unlicensed band and support new use cases
      Participating ITU-R WP5A activities would be complementary to IMT-2020 proposal.

## Slide 17: References
ITS WRC-19 agenda item
ec-16-0017-02-5GSG-5g-sc-agenda-march-2016
ec-16-0035-01-5GSG-ieee-5g-steering-committee-update-march-2016
ec-16-0041-01-5GSG-802-11-5g-technologies-for-5g-sc
ec-16-0062-00-5GSG-what-s-in-scope-for-5g-imt-2020-standing-committee
ec-16-0065-00-5GSG-5g-sc-report-layout
NGMN 5G White Paper v1.0
ITU-R Recommendation M.1457
ITU-R Recommendation M.2012
ITU-R Recommendation M.1450