## Slide 1: Views on Revision of IEEE Std 802
Roger Marks
(EthAirNet Associates)
2021-06-09
802-ec-21-0131-00-00EC

## Slide 2: IEEE Std 802
IEEE Std 802, “IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture”
Originally IEEE Std 802-1990
  10 years after IEEE 802 was founded
Revision IEEE Std 802-2001
Revision IEEE Std 802-2014
  Amended by IEEE Std 802d-2017: Amendment 1: Allocation of Uniform Resource Name (URN) Values in IEEE 802 Standards
  Amended by IEEE Std 802c-2017: Amendment 2: Local Medium Access Control (MAC) Address Usage
  Third amendment in progress: P802f: Amendment: YANG Data Model for EtherTypes
  Procedurally, revision should follow before further amendments
2

## Slide 3: The IEEE 802 Family?
IEEE Std 802 says:
  This standard serves as the foundation for the family of IEEE 802 standards published by IEEE for local area networks (LANs), metropolitan area networks (MANs), personal area networks (PANs), and regional area networks (RANs).
  several types of medium access technologies are currently specified in the family of IEEE 802 standards
What is a “Family of Standards”?
In what way are the standards “related”:
  The nature of the relationship is not explained or explored.
What do IEEE 802 standards have in common?
  They largely share addresses.
So, is this a family, or simply a group of “roommates” with shared addresses?
3

## Slide 4: What is the IEEE 802 Architecture?
What does IEEE Std 802 say about the IEEE 802 architecture?
  Very little
  The Scope says “The IEEE 802 architecture is defined”
  The word “architecture” appears sparsely.
  Subclause 7.2.2 (“Management architecture”) includes three brief paragraphs about management that do not refer to architecture.
  Annex B.6 uses the word ““architecture” in reference to the 802.22 RM.
  No content purports to specify the architecture.
  The closest to a specification of the architecture is in Clause 5 (“Reference models (RMs)”) says “Figure 3 shows the architectural view of IEEE 802 RM for end stations and its relation to the OSI/RM. A variation of the model applies within bridges, as described in 5.3.2.”
  Conclusion: The IEEE 802 architecture is neither defined nor specified here.
4

## Slide 5: The “Common” LLC
In relation to the IEEE 802 RM figure (Fig. 3), IEEE Std 802 says:
  For the mandatory data services supported by all IEEE 802 networks, the DLL is structured as two sublayers, with the logical link control (LLC) sublayer, described in 5.2.2, operating over a MAC sublayer, described in 5.2.3.
So, the LLC is the commonality in the 802 architecture.
IEEE Std 802.2 is “Logical Link Control.” IEEE Std 802 says:
  IEEE Std 802.2-1989 (reaffirmed 2003) was administratively withdrawn as an IEEE standard on 11 January 2011 in deference to the stabilized standard ISO/IEC 8802-2:1998 where the same material continues to be available.
IEEE Std 802 does not detail a role for 8802-2 in the architecture.
IEEE Std 802 explains 8802-2 only in relation to protocol identification; however, it requires support for a different method of protocol identification, and the Introduction says:
  While the protocol identification mechanism specified by ISO/IEC 8802-2 (IEEE Std 802.2™, withdrawn) is still used, its use for new standards has been deprecated.
    See EPD and LPD
So, what exactly is the common LLC?
5

## Slide 6: Data Link Layer, per OSI
Open Systems Interconnection (OSI) specifies seven layers.
ITU-T X.212 (OSI “Data Link Service [DLS] Definition”) describes the service provided by the DLS to the Network Layer, including:
  Provides for the transparent transfer of DLS user-data. It does not restrict the content, format or coding of the information, nor does it ever need to interpret its structure or meaning.
  The DLS relieves the DLS user from loss, insertion, corruption or, if requested, misordering of data which may occur. In some cases of unrecoverable errors in the Data Link Layer, duplication or loss of DLSDUs may occur.
  Data Link addresses have only local significance within a specific Data Link configuration over a single transmission medium (point-to-point or multi-point physical connection) or a group of parallel transmission media (multi-link or splitting function). Therefore it is not appropriate to define a global addressing structure.
  and more
Connectionless-mode and Connection-mode services are specified
How does 802 specify the 802 Data Link Layer Service?
  Not currently specified, except in 802.2/8802-2.
6

## Slide 7: IEEE 802: General requirements
IEEE Std 802 Clause 6 is a single page detailing “General requirements for an IEEE 802 network”
  capabilities to support the MAC service specified in IEEE Std 802.1AC, between two or more MSAPs… the ability to convey LLC sublayer data from one MSAP to n other MSAPs
  Minimal error performance is specified over fiber and wire.
  A network outage due to a station change is limited to around 1 s.
Basic characterization of the service is unspecified; e.g.
  Frame duplication?
  Frames misordering?
  Latency or latency bounds?
  Priorities?
  VLANs?
7

## Slide 8: The 802 Data Link Layer Service
per 802.2, Data Link Layer Service has three forms:
  Unacknowledged connectionless-mode
    may be useful when higher layers provide any essential recovery and sequencing services so that these do not need replicating in the data link layer
  Connection-mode
    includes support of sequenced delivery of data link layer data units
  Acknowledged connectionless-mode
    in-sequence delivery is guaranteed for data sent by the initiating station
Per 802.1AC, the MAC service is connectionless
  In general, the MAC Service provider can perform any or all of the following actions: Discard objects, Change the order of the objects
  The MAC Service exhibits a negligible rate of the following: Object duplication, Reordering of objects for a given priority
    But “priority” is not part of the IEEE 802 Architecture
  Awareness of the characteristics of the MAC Service provided, e.g., the rate at which objects can be discarded, duplicated, or misordered, is part of the MAC Service user’s a priori knowledge of the environment.
8

## Slide 9: What else is in the 802 Architecture?
Is bridging in the 802 Architecture?
  A secure data exchange standard and MAC bridging standards are intended to be used in conjunction with the MAC standards.
  Subclause 5.3.2 covers “MAC-sublayer interconnection: Bridges” and provides basic detail:
    A bridge processes protocols in the MAC sublayer and is functionally transparent to LLC sublayer and higher layer protocols. MAC frames are forwarded between access domains, or filtered (i.e., not forwarded to certain access domains), on the basis of addressing and protocol information contained in the MAC frame. Figure 7 shows the position of the bridging functions within the MAC sublayer; note particularly that relaying and filtering are considered to belong entirely within the MAC sublayer.
    IEEE Std 802.1D and IEEE Std 802.1Q specify transparent bridging operation, so called because the MAC bridging function does not require the MAC user frames transmitted and received to carry any additional information relating to the operation of the bridging functions; end-station operation is unchanged by the presence of bridges.
Not in the 802 Architecture:
  VLANs
  priorities and queuing
  PDU size limits
9

## Slide 10: IEEE Std 802.1CF
IEEE Std 802.1CF-2019: (“IEEE Recommended Practice for Network Reference – Model and Functional Description of IEEE 802® Access Network”)
Abstract: An access network (which connects terminals to their access routers) utilizing technologies based on the family of IEEE 802 ® standards is specified in this recommended practice. An access network reference model (NRM) that includes entities and reference points along with behavioral and functional descriptions of communications among those entities is provided in this recommended practice.
5.2 “Basic architectural concepts and terms” (in its entirety) says:
  The architectural concepts used in this and other IEEE 802.1™ standards are based on the layered protocol model introduced by the OSI Reference Model (ISO/IEC 7498-1:1994 [B25]) and used in the MAC Service definition (IEEE Std 802.1AC), in IEEE Std 802, in other IEEE 802 standards, and, with varying degrees of fidelity, in networking in general. IEEE 802.1 standards in particular have developed terms and distinctions useful in describing the MAC Service and its support by protocol entities within the MAC sublayer.
  Conclusion: The 802 architecture is not specified here.
10

## Slide 11: Topics to consider in a revision
Thorough documentation of existing architecture
  data link service, customer VLANs, priorities and queuing, PDU sizes, bridging, link aggregation, protocol discrimination, etc.
LLC or equivalent
Support for new and evolving technologies; e.g.
  Time-Sensitive Networks, structured addresses, cut-through forwarding, etc.
MAC-specific architecture optimization
  e.g., architectural optimization specific to full-duplex Ethernet networks
Usage-specific features useful for specific scenarios (some, not all)
  e.g., data center, high-performance computing, data storage, automotive, industrial, factory, aerospace, various telecom
Conformance requirements
11

## Slide 12: Key elements of 802 Revision PAR (excluding dates)
Project title:
  Existing: Standard for Local and Metropolitan Area Networks: Overview and Architecture
Scope of proposed standard:
  Existing: This standard contains descriptions of the IEEE 802(R) standards published by the IEEE for frame-based data networks as well as a reference model (RM) for protocol standards. The IEEE 802 architecture is defined, and a specification for the identification of public, private, and standard protocols is included.
Purpose clause:
  Existing: This standard serves as the foundation for the family of IEEE 802 standards published by IEEE for local area networks (LANs), metropolitan area networks (MANs), personal area networks (PANs), and regional area networks (RANs).
Need for the project:
  Existing: Revision of existing IEEE 802-2001 standard is needed to remove redundant material and reflect the current IEEE 802 architecture and its suite of standards.
Stakeholders for the Standard:
  Existing: Standards developers within IEEE 802. Manufacturers, distributors, and users of products and services that conform to the LAN, MAN, and PAN standards developed by IEEE 802.
Working Group:
  Existing: Higher Layer LAN Protocols Working Group
12

## Slide 13: Key PAR elements: Possible Updates
Scope of proposed standard:
  Existing: This standard contains descriptions of the IEEE 802(R) standards published by the IEEE for frame-based data networks as well as a reference model (RM) for protocol standards. The summarizes the IEEE 802 family of standards and specifies the IEEE 802 architecture is defined, and a specification for the identification of public, private, and standard protocols is included. providing a frame-based data link layer service to the network layer.
Need for the project:
  Existing: Revision of existing IEEE 802-201401 standard is needed to remove redundant material and reflect the current IEEE 802 architecture and its suite of standards. incorporate amendments and to specify a more complete, updated IEEE 802 architecture that meets both existing and new future needs for data link layer services.
Stakeholders for the Standard:
  Existing: Users of data link client services. Standards developers within IEEE 802. Manufacturers, distributors, and users of products and services that conform to the LAN, MAN, and PAN standards developed by IEEE 802.
Working Group: ?
Note: Further details should be documented in a report far more detailed than a CSD.
13

## Slide 14: Proposal
A project to revise IEEE Std 802 should be initiated.
The project should be charged with ambitious but documented goals.
The goals should be specified in a consensus report to accompany the PAR.
The report and PAR could be generated by a focused pre-PAR activity, conducted in, for example, a Study Group or an Industry Connections Activity such as Nendica.
14