## Slide 1: Proposed Nendica Presentation to NANOG 75
Roger Marks
Huawei
roger@ethair.net +1 802 capable
5 February 2019
    IEEE 802.1-19-0004-02-ICne
Abstract: NANOG, the North American Network Operators Group, is a “professional association for Internet engineering, architecture and operations.” The Executive Director of NANOG has invited the author to speak to NANOG 75 (18-20 Feb 2019), based on 802.1-18-0068-00-ICne. This contribution provides a slide set proposed for presentation to NANOG 75 by the Nendica Chair as an input from Nendica. The set is based on 802.1-18-0068 and includes additional material encouraging a cooperation with NANOG on further developments regarding data center networks. This Rev2 is a proposed final update to Rev1, which was agreed by Nendica on 2019-01-09. References 4-5 are added, and Slides 18-19 are new.

## Slide 2: Lossless Data Center Networks: Opportunities for NANOG Engagement with IEEE 802 Nendica
Roger Marks
Chair, Nendica
roger@ethair.net +1 802 capable
5 February 2019
    DRAFT

## Slide 3: Disclaimer
All speakers presenting information on IEEE standards speak as individuals, and their views should be considered the personal views of that individual rather than the formal position, explanation, or interpretation of the IEEE.

## Slide 4: Nendica
Nendica: IEEE 802 “Network Enhancements for the Next Decade” Industry Connections Activity
  An IEEE Industry Connections Activity
Organized under the IEEE 802.1 Working Group
Chartered March 2017 - March 2019
  may be extended
Chair (until March 2018): Glenn Parsons
Chair (from March 2018): Roger Marks
Open to all participants; no membership

## Slide 5: IEEE Industry Connections Activity
Under IEEE-SA, but not standardization.
“Industry Connections activities provide an efficient environment for building consensus and developing many different types of shared results. Such activities may complement, supplement, or be precursors of IEEE Standards projects, but they do not themselves develop IEEE Standards.”

## Slide 6: Nendica Motivation and Goals
“The goal of this activity is to assess… emerging requirements for IEEE 802 wireless and higher-layer communication infrastructures, identify commonalities, gaps, and trends not currently addressed by IEEE 802 standards and projects, and facilitate building industry consensus towards proposals to initiate new standards development efforts.
Encouraged topics include enhancements of IEEE 802 communication networks and vertical networks as well as enhanced cooperative functionality among existing IEEE standards in support of network integration.
Findings related to existing IEEE 802 standards and projects are forwarded to the responsible working groups for further considerations.”

## Slide 7: Nendica Work Items
The Lossless Network for Data Centers
  Paul Congdon, Editor
  published Nendica Report, 2018-08-17
    IEEE 802.1-18-0042-00
  Published report invites further comments
  Stimulated new standardization project IEEE P802.1Qcz (Congestion Isolation)
Flexible Factory IOT
  Nader Zein, Editor
  Draft report 802.1-18-0025-06
  Significant focus on wireless
  Comment resolution underway

## Slide 8: Nendica Report: The Lossless Network for Data Centers
Paul Congdon, Editor
Key messages regarding the data center :
  Packet loss leads to large delays.
  Congestion leads to packet loss.
  Conventional methods are problematic.
  Even in a Layer 3 network, we can take action at Layer 2 to reduce congestion and thereby loss.
  The paper is not specifying a “lossless” network but describing a few prospective methods to progress towards a lossless data center network in the future.
The report is open to comment and may be revised.

## Slide 9: Use Cases: The Lossless Network for Data Centers
Online Data Intensive (OLDI) Services
Deep Learning and Model Training
Non‐Volatile Memory Express (NVMe) over Fabrics
Cloudification of the Central Office
An overall theme of these use cases is the dependence of parallel computation on the network.

## Slide 10: Data Center Applications are distributed and latency-sensitive
Tend toward congestion; e.g. due to incast
Packet loss leads to retransmission, more congestion, more delay
Source: IEEE 802 Nendica Report: The Lossless Network for Data Centers [2]

## Slide 11: Folded-Clos Network: Many Paths from Server to Server

## Slide 12: Equal-Cost Multi-Path (ECMP): Path assigned per flow (~random)

## Slide 13: ECMP may still lead to congestion; e.g. large flows may collide

## Slide 14: Incast fills output queue (note: ECMP cannot help)

## Slide 15: Priority flow control (PFC)
Output backup fills ingress queue
PFC can be used to pause input per QoS class
IEEE 802.1Q (originally in 802.1Qbb)

## Slide 16: PFC pauses all flows of the class including “victim” flows

## Slide 17: Congested-flow Isolation (see IEEE Project P802.1Qcz [5])
Source: IEEE 802 Nendica Report: The Lossless Network for Data Centers [2]

## Slide 18: Traffic-class blocking analysis
Source: IEEE 802.1-19-0012-00 [4]

## Slide 19: Congested-flow Isolation Analysis
Source: IEEE 802.1-19-0012-00 [4]

## Slide 20: Explicit Congestion Notification (ECN) pauses flows at source

## Slide 21: Load-Aware Packet Spraying (LPS)
Source: IEEE 802.1-17-0007-01 [3]

## Slide 22: Push & Pull Hybrid Scheduling(PPH)
Congestion aware edge switch scheduling
Push when load is light
Pull when load is high
Push Data
Grant
(Pull)
Long
RTT
Short RTT
Request
(Pull)
Pulled
Data
Request (Pull)
Push
Data
Pulled
Data
Light load: All Push. Acquire low latency.
Light congestion: Open Pull for part of the congested path
Heavy load: All Pull. Reduce queuing delay, improve throughput.
Chart: 
Chart: 
Chart: 
Source: IEEE 802.1-17-0007-01 [3]

## Slide 23: Key Issues: Nendica Report on Lossless Network for Data Centers
Dynamic
Virtual
Lane
Priority-based Flow Control is coarse. Victim flows paused due to congested flows
Allow time for end-to-end congestion control. Move congested flows out of the way. Eliminate victim blocking.
Push & Pull
Hybrid
Scheduling
Unscheduled incast without awareness of network resources leads to packet loss.
Source
Network
Destination
Schedule using integrated information from source, network, and destination.
Source
Network
Destination
Load-aware
Packet
Spraying
Unbalanced load sharing. Multiple elephant flows congest and block mice flows..
Load-balance flows at higher granularity. Use congestion awareness to avoid collisions
Isolate Congestion
Schedule Appropriately
Spread the Load
Congestion Cause
Mitigation
Innovation
Extracted from IEEE 802.1-17-0007-01 [3]

## Slide 24: Bibliography
IEEE 802 “Network Enhancements for the Next Decade” Industry Connections Activity (Nendica)
  https://1.ieee802.org/802-nendica
IEEE 802 Nendica Report: “The Lossless Network for Data Centers” (18 August 2018)
  https://mentor.ieee.org/802.1/dcn/18/1-18-0042-00.pdf
Paul Congdon, “The Lossless Network in the Data Center,” IEEE 802.1-17-0007-01, 7 November 2017
  https://mentor.ieee.org/802.1/dcn/17/1-17-0007-01.pdf
Pedro Javier Garcia, Jesus Escudero-Sahuquillo, Francisco J. Quiles, and Jose Duato, “Congestion Management for Ethernet-based Lossless DataCenter Networks,” IEEE 802.1-19-0012-00, 4 February 2012
  https://mentor.ieee.org/802.1/dcn/19/1-19-0012-00.pdf
IEEE P802.1Qcz Project: “Congestion Isolation”
  https://1.ieee802.org/tsn/802-1qcz

## Slide 25: Going forward
IEEE 802 Nendica Report: “The Lossless Network for Data Centers” (18 August 2018) is published but open to further comment.
  Comments are welcome from all
Could open an activity to revise the report, addressing new issues.
  Proposal [5] may be discussed in future teleconference.
Report could help identify issues in need of further research or unified action.
Nendica could instigate standardization of key topics
  Mainly in IEEE 802; perhaps also in e.g. IETF

## Slide 26: Nendica/NANOG Cooperation?
Nendica is open to all participants; no membership
  e.g. teleconference participation; comment process
IEEE 802 Nendica Report: “The Lossless Network for Data Centers”.
  Comments are welcome from NANOG participants
An activity to revise the report could address issues important to advance NANOG goals.
Might be useful to convene Nendica meetings in conjunction with NANOG meetings:
  NANOG 76 (Washington, 10-12 June 2019)
  NANOG 77 (Austin, 28-30 Oct 2019)

## Slide 27: Nendica Participation
Nendica is open to all participants: please join in!
  no membership requirements
  Comment by Internet or contribute documents
  Call in to teleconferences
  Attend meetings
Nendica web site
  https://1.ieee802.org/802-nendica
  Details of in-person and teleconference meetings
Feel free to contact the Chair (see first slide)
  or the Work Item Editors

## Slide 28: Possible next steps
Teleconferences targeted at identifying issues regarding Data Center networks
  NANOG participants welcome
Opening of activity to revise “The Lossless Network for Data Centers” report
Decision to convene Nendica meetings in conjunction with NANOG 76
Detailed presentation, open to NANOG participants, regarding the new P802.1Qcz project on Congestion Isolation [5]