## Slide 1
1
Congestion Signaling (CSIG)
Simple and Effective In-band Network Signals for Efficient Traffic Management in Datacenter Networks
IEEE 802 Nendica Meeting
November 16, 2023
Paul Bottorff (HPE)
Jai Kumar (Broadcom)

## Slide 2: Networking for ML Workloads
2
Trend: More accelerators, more bandwidth per accelerator
  Horizontal scaling → exercises shared data center network fabric
Network efficiency is critical for AI/ML
  Bursty traffic, large # of connections, flow collisions
  Large-scale synchronized bursts stress the network unlike traditional compute / storage applications
  Training → throughput and latency sensitive,
  Inference / serving → latency sensitive
Network performance directly impacts Training step time
  Barrier collectives in training sensitive to 100p network latency
  Throughput sensitive where compute/communication overlap.

## Slide 3: Networking for ML Workloads continued…
2 or 3 stage CLOS or Dragonfly+ topologies
High bandwidth, high radix, ultra low latency switches
  AI Inference: Needs Latency SLA aimed at distributed models
  AI Training: Needs High bandwidth, low latency for small models
256K+ network endpoints
Low tail latency and FCT
High performant transport in tandem with efficient end-to-end congestion control
Network signals for optimal bandwidth utilization, flow ramp up and scheduling
3

## Slide 4: Limitations of Existing INT Technologies
PMTU overhead
Increased switch latency, power budget and hardware complexity
Difficulty in working with tunneled domains and complexity in propagating INT metadata stack
Not very well suited for brownfield deployment
Protocols using IPv6 Hop-by-Hop options are processed in slow path
Considerable overhead for small sized packets
Enters CSIG
4

## Slide 5: CSIG: Practical & Effective In-band Signaling protocol
Provides fixed-length simple summaries from the path bottlenecks
Designed for Congestion Control, Traffic Management and Network debuggability use-cases
Designed for brownfield deployment with backward compatibility / interoperability
Link to IETF Draft - https://datatracker.ietf.org/doc/draft-ravi-ippm-csig/
HW Offloaded Transport
TCP
UDP
IP
CSIG-tag
Ethernet
Custom Transport
CSIG Reflection

## Slide 6: CSIG Tag 4B Version
Byte 1-4
16 bits - CSIG-ethtype: IEEE allocated code point for 4Byte CSIG frame
3 bits - T: Signal Type (0:minABW, 1: minABW/C, 2:maxDelay) [maxQueueSize/C][sumTrimTxByte per port or per trim queue]
1 bit - reserved
5 bit - S: Signal: Bucketed Signal Value (fully configurable)
7 bits - LM: Locator Metadata of bottleneck link (fully configurable per port information)[Port down notification back to sender]
CSIG
1 | 2 | 3 | 4
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| CSIG-ethtype | T |R| Signal | Locator |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: CSIG Tag 8B Version
Byte 1-4
16 bits - CSIG-ethtype: IEEE allocated code point for 8Byte CSIG frame
16 bits - LM: Locator Metadata of bottleneck link (fully configurable per port information)
Byte 5-8
4 bits - T: Signal Type (0:minABW, 1: minABW/C, 2:maxDelay)
20 bits - S: Signal: Quantized Signal Value
8 bits - Reserved
CSIG
1 | 2 | 3 | 4
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| CSIG-ethtype | Locator |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| T | Signal Value | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
5 | 6 | 7 | 8
8B: Fixed step function BW quantization
4B: Fully configurable 32 BW range buckets

## Slide 8: Ether Type Layering
Bridge Domain will forward the traffic and “MAY” update the CSIG Tag if bridging device is capable
Routed Domain need to understand the new ethtype and router will treat CSIG tag either as opaque tag for forwarding or will update the tag.
ARPA | dstmac / srcmac / csig-tag / ethertype / payload
802.1q: | dstmac / srcmac / vlan-tag / csig-tag / ethertype / payload
802.1ad | dstmac / srcmac / vlan-tag / vlan-tag / csig-tag / ethertype / payload
802.1ad tunnel | dstmac / srcmac / vlan-tag / vlan-tag / vlan-tag / vlan-tag / csig-tag / ethertype / payload
802.1ae | dstmac / srcmac / security-tag / vlan-tag / csig-tag / ethertype / payload

## Slide 9: Backed By Industry Leaders
Google
Broadcom
Cisco
HPE
9

## Slide 10
Thank You