## Slide 1: The ITU-R Structure and Process
Bob Huang
Matsushita/Panasonic
802.11
12 January 2000, Tel Aviv

## Slide 2
Radiocommunications Sector
Telecommunications Standardization Sector
Development Sector
ITU Structure
ITU
World Radiocommunications Conference
(an ITU meeting, not a Sector meeting)

## Slide 3
Radiocommunications Sector
Radiocommunications Bureau
Administers the
Radio Regulations
(Table of Frequency
Allocations)
Radiocommunications
Assembly
(meeting of all Study Groups)
Study Groups
Guides SG
technical work
Plans and approves
technical work
(Recommendations)
Working Parties
Task Groups
Performs technical
work and drafts
Recommendations
(permanent)
Performs technical work
drafts Recommendations
(highly urgent, short term)

## Slide 4
How is frequency use decided within a country?
Government controls:
  Frequency allocation (designation to a service)
  Frequency assignment (permission to use)
Based on:
  National needs
  Conformance with the Radio Regulations (contains the International Table of Frequency Allocations)
  Potential to cause harmful interference to radio systems another country

## Slide 5
How do the Radio Regulations fit in?
They contain international treat-binding agreements on how to use frequencies.
  They are maintained by the WRC (World Radiocommunications (Formerly the WARC). The WRC is attended by ITU member countries.
  Arguments for a new allocation have a small chance of success without frequency sharing
  Sharing criteria from ITU-R Recommendations are easily accepted
Thus campaigns for a frequency allocation often start in the ITU-R

## Slide 6
If the ITU-R shows that sharing is possible between existing services (in use) and the new service, is a new allocation assured?
  No. An Administration (country) can oppose a new allocation based future use of a current allocation.
How is a new allocation approved?
  All administrations present at the WRC vote (one country one vote).
Will a single no vote stop an allocation?
  No. However, any country can insert a footnote in the Table indicating an exception in their country.

## Slide 7
What about the ITU process in the US?
There are two parts:
The ITU-R process for obtaining a recommendation
The WRC process for obtaining an allocation
But first, it is useful to understand the structure within the US

## Slide 8
The US structure for frequency allocation matters is a triumvant, consisting of:
Department of State (DoS)
  Final control due to treaty binding text and foreign relations nature of agreements.
FCC
  Congress approves the WRC text and decides on the US table of frequency allocations
  Administers frequency allocations within the US for non-government (commercial and public) use
NTIA
  Administers frequency allocations within the US for government use (military, public service, FAA, etc.)

## Slide 9
The Department of State administers the US ITU-R process by:
Forming the US Study Groups
Appointing a US chairman (may be from the government or private sector)
Insuring that all US positions are agreed to by the FCC, NTIA and the private sector
Accrediting delegations to Study Group meetings and Radiocommunications assemblys

## Slide 10
How can a company (or individual*) participate in the US ITU-R process?
By attending the meetings and bring contributions.
Which Study Group deals with wireless LANS*?
WLANs are dealt with* in Working Party 8A (under Study Group 8 - Mobile Services).
As Mobile Services typically share with Fixed Services, there is a continuing need for close cooperation between WP 8A and WP 9B.
This is achieved through Joint Rappeatuers Group 8A-9B
* Radio LANs (RLANs)
** Study Group 9, dealing with Fixed Services, has long contended that WLANs are in their domain.

## Slide 11
What is the contribution approval process?
Approval by US Study Group (includes approval by FCC and NTIA)
Approval by US ‘National Committee’ for radio matters
Approval by JRG 8A-9B
Approval by Study Group 8 (Recommendation for Mobile Services)
Approval by Study Group 9 (Recommendation for Fixed Services)
note: There are alternate fast track procedures for the final approvals

## Slide 12
ITU-R Groups
1 Spectrum Management
3 Radiowave Propagation
4 Fixed Satellite Service
7 Science Services
8 Mobile, Radiodetermination, Amateur and related Satellite Services
9 Fixed Service
10 Broadcasting Service - Sound
11 Broadcasting Service - Television
sc Special Committee on Regulatory/Procedural Matters
ccv Coordination Committee for Vocabulary
cpm Conference Preparatory Meeting

## Slide 13
Not covered: The WRC Process
Perhaps this can be provided in the future:
At this time the ITU-R process is most important.
The End
Questions?