## Slide 1: Extensible Security
Standardizing for Change
Bob O’Hara
Albert Young
Dan Nessett
Bofu Chen
Bruce Kendall

## Slide 2: Security Environment
The choice of “best” security algorithms for authentication and privacy are not static over time
Affected by
  Government regulation
  Newly discovered attacks
  Advances in mathematics
  Advances in processing capabilities
  Newly discovered faults
  Uninformed opinions of users

## Slide 3: Standardization Environment
Define solution(s) based on current conditions and best estimates of future
Solution is fixed and generally inflexible
Difficult to change
  Requires a group (like us) to meet and accomplish the task
  Generally, will not take less than 18-24 months to complete a change

## Slide 4: Standardize for Change
Standardize mechanism(s) that are not rigid
  Based on negotiation, rather than fixed requirements in the standard
Allow for ongoing adaptability and innovation
Provide processes that encourage/enforce exchange of information
Provide one (or two) starting points using the new mechanism

## Slide 5: Three Alternatives
Use the existing authentication algorithm number field
Redefine the authentication algorithm number field
Extend the authentication frame format to add an information element

## Slide 6: Use the Authentication Algorithm Field
Define a registration process that allows anyone to petition the IEEE for a new value to be used in this field
  Exactly the same as the process used for OUI and Ethertype registration
    See http://standards.ieee.org/regauth/oui/index.shtml and http://standards.ieee.org/regauth/ethertype/index.html
Require full disclosure of information to enable multi-vendor interoperability

## Slide 7: Redefine the Authentication Algorithm Number Field
Change the field to be the Security Algorithms field
Define two new subfields
  Privacy Algorithm Number, 8 bits
  Authentication Algorithm Number, 8 bits
Define privacy algorithm to be 40-bit WEP only when authentication is not open system
Privacy Algorithm
Authentication Algorithm

## Slide 8: Use New Information Element
Define a single new value for the Authentication Algorithm field (say 2) that indicates that the new element is present, following the challenge text
  In the first Authentication frame
  Or in every Authentication frame
The new Information Element several fields
  Identify both the authentication algorithm and privacy algorithm, independently
  Include key lengths for both privacy and authentication

## Slide 9: Authentication and Privacy Information Element
Field | Length (octets)
Element ID | 1
Length | 1
Authentication Algorithm | 2
Authentication Key Length | 2
Registering OUI-A | 3
Privacy Algorithm | 2
Privacy Key Length | 3
Registering OUI-P | 2

## Slide 10: Merits of Flexibility
Vendors can adapt quickly to changes in the security environment
The standard does not need to be changed for this reason in the future
The market can select the “correct” algorithms
Encourages both competition and interoperability within the scope of the standard

## Slide 11: Relative Merits of Alternatives
Using only the Authentication Algorithm field
  No change is needed to the Authentication frame format
  Minimizes likelihood of interoperability problems with existing APs
    Unless AP performs only a single test to differentiate between the two current allowable values
  Does not easily provide a mechanism for selecting privacy algorithm or key length, without overloading the definition of this field

## Slide 12: Relative Merits of Alternatives
Redefining the authentication algorithm number field
  No change is needed to the Authentication frame format
  Minimizes likelihood of interoperability problems with existing APs
    Unless AP performs only a single test to differentiate between the two current allowable values
  Adds capability to select both privacy and authentication algorithms in the authentication exchange

## Slide 13: Relative Merits of Alternatives
Using a new information element
  Changes basic format of Authentication frame
    Adds new information element to first (or each) Authentication frame
  Likelihood of interoperability problem is slightly greater than with previous methods
  Allows independence of choice for both authentication and privacy algorithms
  Provides significantly greater identifier space
    Algorithm values are assigned independently to each OUI
    Provides for the possibility that half of each identifier space can be reserved for “experimental” values that need not be registered

## Slide 14: Recommendation
Define the Authentication and Privacy information element, its fields, and its usage
Define a registration procedure
  Registrant must have an IEEE-assigned OUI
  Complete algorithm and handshake protocol details must be provided, including external references (if any)
  In exchange for providing registration services, IEEE gets right to publish details (preferably on web site)
Include a pointer to the registration web site in the standard

## Slide 15: Procedural Stuff
Write a proposal to IEEE Registration Authority Committee
  What is to be registered?
  Why should it be registered?
  What special procedures are needed?
Next RAC meeting is at July 802 plenary
Work with IEEE to implement the procedures