## Slide 1: Dynamic Channel Selection (DCS) Scheme for 802.11
G. Cervello, S. Choi, S. Mangold, and A. Soomro
Philips Research-USA
Briarcliff Manor, New York

## Slide 2: Introduction
Dynamic Channel Selection (DCS) instead of DFS for 802.11
  ETSI requires DFS and TPC
  Nice to have DCS for some environments, e.g., home environment and offices in a building
  DCS first, if not working, overlapping BSSs
Need to define a DCS mechanism WITHOUT requiring any change in PHYs
  It should work with all the current and future PHYs
Algorithms subject to implementations

## Slide 3: Basic Mechanism for Infrastructure BSS
Initiation of a new channel selection
Request of a channel measurement by AP
Channel measurement process of STAs
Measurement report from STAs to AP
Decision making by AP
Channel switch announcement by AP
Switch into the new channel

## Slide 4: 1. Initiation of Channel Selection
Two cases of channel selection initiation
  A BSS is formed by an AP
  When AP and/or STA(s) of a BSS experience bad channel condition persistently
Need to define management frames for the channel condition feedback from STAs to AP
  Same frames can work for overlapping BSS finding
When to initiate will be up to implementation

## Slide 5: 2. Channel Measurement Request
AP requests channel measurements to some STAs to find the best channel to run its BSS
  Those STAs will be considered as sleeping STAs
  Measurement by AP not desirable
New management frames need to be defined
  When to begin the measurement
  Which channels to measure
  How long to measure
  How to measure (explained next)

## Slide 6: 3. Channel Measurement Process
STA moves to channel(s) to measure as requested by AP
Three ways of channel measurements
  Detection of other BSSs running in the channel
  Measure RSSI and PER when BSSs detected
  Measure busy channel portion
Detection of other BSSs
  Using the “scan” service from MLME to SME
  MLME-SCAN.request and MLME-SCAN.confirm

## Slide 7: 3. Channel Measurement Process (Cont.)
Measure of RSSI and PER
  RSSI value is available to MAC via PHY_RXSTART only when a meaningful MAC frame is received
  Need to standardize the RSSI values
Measure of busy channel portion
  Measure time and number of cases of PHY_CCA(BUSY) without PHY_RXSTART
  Can be used to measure alien devices, e.g., H/2 and microwave

## Slide 8: 4. Measurement Report to AP
Measurement report of STA(s) to AP
If no BSS detected in a channel, the result of the third measurement is only meaningful
May be reported during CP or CFP (per being polled)
Need to define new management frames

## Slide 9: 5. Decision Making by AP
AP make a decision per hearing the reports from STAs
  Whether to move or not
  To which channel per deciding to move
  When to move
Need to compare other channels with the current channel
Need to consider sleeping STAs to determine when to move

## Slide 10: 6. Announce of Channel Switch
Need to announce the channel move decision to STAs
Need to define new management frames or define new fields in beacon frames
May need to broadcast it several times to ensure the decision reception
May need to implement some ACK mechanism for some STAs such as ones with isochronous connections

## Slide 11: 7. Switch into New Channel
AP moves first, then STAs follow
As simple as changing the carrier frequency
However, no such a service primitive defined
Need to define new MLME primitives such as MLME-JUMP.request & MLME-JUMP.confirm
Expected not to require any change in PHY since channel change can be ordered to existing PHY by MAC
May need to move at the end of a CFP

## Slide 12: Summary
Basic DCS mechanism proposed for infrastructure BSS of 802.11
Three ways of channel measurements
Need to add some management frames
Need to define some new primitives
The proposal can be defined WITHOUT any change in PHY