## Slide 1: Implementation Options for the Distribution System in the 802.11 Wireless LAN Infrastructure Network
Amre El-Hoiydi,
CSEM, Switzerland
IEEE ICC 2000

## Slide 2: IEEE 802.11
PHY
  Frequency-Hopping / DSSS / Infra Red
MAC
  Wireless Ethernet
Network Architecture
  Ad Hoc Network
  Infrastructure Network

## Slide 3: Ad Hoc Network

## Slide 4: Infrastructure Network

## Slide 5: Definitions
Basic Service Set: A wireless cell
Extended Service Set: All wireless cells
Distribution System:
Access Point: Connection DS - BSS
Portal: Connection DS - Wired LAN
Glue between the BSS to form the ESS

## Slide 6: Distribution System
Several cells form a virtual single shared-medium
Distribution system responsible of routing frames
Distribution system transparent to LLC
Portal + Access Points = MAC Bridge between the wired LAN and the cells

## Slide 7: Operation: Traffic
No direct traffic between stations

## Slide 8: Operation: Roaming
Association protocol gives to the distribution system the necessary information to perform the mobility management

## Slide 9: Logical Services
Station Service
  Authentication,
  Encryption,
  MSDU Delivery
Distribution System Service
  Association,
  Distribution (unspecified),
  Integration (unspecified)

## Slide 10: Implementation Options for the Distribution System
Choice of a distribution transport protocol and addressing
  LLC Type 1 (connectionless) transport, MAC addressing
  or
  UDP/IP transport, IP layer addressing
Choice of a mobility management signalling protocol

## Slide 11: Overview of the discussed options
MAC Layer Addressing
  Option 1: Separated Access Points and Portals
  Option 2: Joined Access Point and Portals
  Option 3: MAC Bridges
Network Layer Addressing
  Option 4: Network Layer Addressing

## Slide 12: Separated AP / Portals
Option 1:

## Slide 13
Max size of a 802.11 MSDU = 2304 Bytes
Max size of the payload in 802.3 = 1492 Bytes
Segmentation needed
Connection protocol needed to avoid mixing segments from different sources
Transport plane
Option 1:

## Slide 14
Goal of the mobility management signalling is that each access point or portal knows through which access point or portal a given MAC address can be reached.
What access point correspond to what MAC address ?
It is proposed to use a dynamic route resolution protocol similar to the Ethernet Address Resolution Protocol (ARP, RCF826)
Option 1:
Signalling

## Slide 15
Option 1:
Route Resolution

## Slide 16
Option 1:
Handover

## Slide 17
Option 2:
Joined AP / Portals

## Slide 18: Option 2 versus Option 1
The mobility management signalling protocol is identical as in option 1
Having the portal functions in the access points prevents the need of forwarding over the distribution medium the traffic to/from the wired LAN

## Slide 19
If the MSDU maximum size in 802.11 is reduced from 2304 to 1476, each access point can be a filtering bridge
The access point will forward into the cell the frames destined to associated stations
No need of mobility management signalling
Association protocol is sufficient to give enough information for the filtering task
Option 3:
MAC Bridge

## Slide 20
Option 3:
Network Architecture

## Slide 21
Option 4:
Network Layer Addressing

## Slide 22
Access points not linked through a broadcast medium anymore
RoutingRequest and RoutingIndication messages cannot be broadcast anymore
It is proposed to use a dynamic address resolution protocol similar to the Address Resolution Protocol over ATM (ARP over ATM, RCF2225)
Each access point must be given the IP address of the server
Option 4:
Signalling

## Slide 23
Option 4:
Route Resolution

## Slide 24
Option 4:
Handover

## Slide 25: Summary

## Slide 26: Standardisation
802.11 TGf Task Group has started the work on IAPP
One IAPP proposal made in 1996
  Uses IP layer addressing
  Transmission of unsolicited “announce” messages
Schedule
  May 2000, fist meeting held
  July 2000, proposals
  Sept 2000, first draft

## Slide 27: Conclusion
MAC bridge solution simple but limited
Should be augmented with a network layer IAPP
Remaining points to study
    impact of lost messages
    impact of crossed handover messages (RoutingIndication)
    comparison between schemes based on requests or on unsolicited messages