## Slide 1: Joint Meeting 5GSG Coexistence ad hoc Regulatory
Wednesday, January 17, 2001
4:00 – 5:30

## Slide 2
Agenda
Introduction – Bruce Kraemer - Intersil
5GSG Work Concept – Pratik Mehta - Dell
5GSG Criteria for Evaluation Document – Don Gray - WebTV
Coexistence - User Expectations – Richard Paine - Boeing
802 Organizational concept – Steve Shellhammer - Symbol

## Slide 3
The chair wishes to acknowledge that the following presentation
is based, in part, upon valuable slide contributions from:
Thomas Kuehnel – NEC
Erik Schylander – Philips
Gil Bar-Noy – hLAN
Takeshi Onizawa – NTT
Pratik Mehta - Dell

## Slide 4: Major 5GSG Topics
Co-existence (of the standards)
    Frequency sharing etiquette
    Interference robustness
Interworking (between two standards)
    co-existence required
    a WT of one standard can work with a (hybrid) AP of the other std.
Single Global Standard
    a new joint developed standard
    based on usage scenarios and applications functional requirements
Regulatory issues
    HL2 need to restrict the frequency range and power for USA to comply to FCC
    What adoptions are needed to use 802.11a outside USA

## Slide 5: 5 GHz Spectrum Europe
HIPERLAN
200 mW
indoor
5.000 5.100 5.200 5.300 5.400 5.500 5.600 5.700 5.800 5.900 6.000 GHz
1. HIPERLAN/2 must comply with (ERC/DEC/(99)23)
2. TPC provides 3dB mitigation factor
HIPERLAN
1 W
indoor/outdoor
ISM
25 mW
5.150 5.350
5.470 5.725
5.725 5.875
Satellite FSS
Aeronautical
Navigation
Radar,
Navigation,
Earth exploration
Satellite
Radio navigation,
Maritime navigation
Radiolocation,
Amateur
3a. DFS across at least 330 MHz (indoor)
3b. DFS across at least
255 MHz (outdoor)
Primary
Users

## Slide 6
Spectrum Allocation at 5 GHz
5.200
5.300
5.400
5.500
5.600
5.700
5.800
5.900
5.100
Europe
USA
Japan
Freq./GHz
5.350
5.150
5.150
5.250
5.350
5.725
5.825
5.150
5.470
5.725
Outdoor 1W EIRP
Indoor 200 mW EIRP
Indoor 200 mW / Outdoor 1 W EIRP
Max mean Tx power
Outdoor 4 W EIRP
Max peak Tx power
DFS & TPC
DFS & TPC
DFS: Dynamic Frequency Selection
TPC: TransmitPower Control

## Slide 7
HL2 MT
Ch2
Internet
802.11 AP
HL2 AP
Coexistence – Level 1 - Using different channels in the same coverage area
Data exchanged between the devices using the backbone (each device communicates with its Access Point)
802.11 STA
Ch1
11a
PHY
11
MAC
MAC
Bridge
H2
PHY
H2
DLC
H2
CL
MAC
Bridge

## Slide 8
HL2 MT
Ch1
Internet
802.11 AP
802.11 STA
Ch1
HL2 AP
Coexistence – Level 2 - Using the same channel in the same coverage area
Data exchanged between the devices using the backbone (each device communicates with its Access Point)
11a
PHY
11
MAC
MAC
Bridge
H2
PHY
H2
DLC
H2
CL
MAC
Bridge

## Slide 9
HL2 MT
Ch1
Internet
Unified AP
2 different MACs
802.11 STA
Ch1
Coexistence – Level 2 - Using the same channel in the same coverage area
Data exchanged between the devices using the backbone
Each device communicates with the Unified Access Point but to a different MAC entity.
Each MAC has a different address
Hybrid
PHY
H2
DLC
11
MAC
H2
CL
MAC
Bridge
MAC/DLC
Convergence Layer

## Slide 10
HL2 MT
Ch1
Internet
Unified AP
Unified Dual MAC
802.11 STA
Ch1
Coexistence – Level 2 - Using the same channel in the same coverage area
Data exchanged between the devices using Layer 2 of the AP
Only one MAC address is used
Hybrid
MAC/DLC
H2
CL
MAC
Bridge
Hybrid
PHY

## Slide 11: 5GHz standardization roadmap
IEEE 802.11a
(wireless Ethernet)
IEEE 802.11e/f/h
(QoS, Security, DFS/TPC, ..)
BRAN-HL/2
(wireless ATM, IP)
HE
(1394 CL, bridge)
2000
2001
joint SG
requirements
co-existence
interworking
spectrum
single
global standard
HE phase2
UMTS - interworking
Public Access
joint work
additions
5GWIAG
MMAC also participating

## Slide 12: Standards Convergence Steps
Interference | Coexistence | Interworking | Single Global Standard
2 standards | 2 standards | 2 standards | 1 standard
Current standards | Changes in standard(s) to remove destructive interference [whether different or same channels] | Changes in standard(s) to remove obstacles to data sharing [beyond interference], but without going to a single global standard | New standard
Current State | Proposals (date) Standard (date) | Proposals (date) Standard (date) | Proposals (date) Standard (date)
Assumption: This will also apply to MMAC

## Slide 13: Standards Convergence Steps
Interference | Coexistence | Interworking | Single Global Standard
2 standards | 2 standards | 2 standards | 1 standard
Harmful interference (2 standards) Communicating devices using 802.11a or HiperLAN2 can not operate in the same coverage area without harmful interference Communicating devices using 802.11a or HiperLAN2 can not exchange data. | Level-1: Operation in the different channels (e.g. DFS, TPC) Communicating devices using 802.11a or HiperLAN2 can operate in the same coverage area by using different channels. Any Wireless Terminal can talk to any AP that is multi-mode, but with two radios. | Level-1: Wireless Terminal of one standard can exchange data with an AP of another standard Communicating devices may not exchange QoS and other aspects. | Any wireless terminal can talk to any AP or any Wireless Terminal Communicating devices using 802.11a or HiperLAN2 can exchange data directly on ad-hoc basis
 | Level-2: Operation in the same channel Communicating devices using 802.11a or HiperLAN2 can operate in the same coverage area using a standardized mechanism that enables devices of both types to efficiently share the same channel. Any Wireless Terminal can talk to any AP that is multi-mode, but with one radio. |  | N/A
Assumption: This will also apply to MMAC

## Slide 14: Regulatory Convergence Steps
Allowing 802.11a in Europe
  DCS/TPC (TGh)
    802.11a would have to add the upper part of the band when talking about DFS, not just the lower 200 MHz portion of the Band
  It is unclear whether there is a 2nd step needed for 802.11a to be classified as a HiperLAN2
    Currently, ERC calls out HiperLAN1 and HiperLAN2 “as defined by ETSI” as the legal standards in Europe, but not certain how this could be interpreted
  Need to write a test specification for 802.11a for certifying the radio
Allowing HiperLAN2 in US
  The band allocation in the US is limited, so the HiperLAN2 solution would have to limit itself to operate in the US-allocated frequency bands
  In the lower 100MHz, the US power limit is lower than in Europe

## Slide 15: Convergence Progression
Hybrid
MAC/DLC
H2
PHY
11a
PHY
H2
DLC
11
MAC
H2
CL
MAC
Bridge
H2
CL
MAC
Bridge
11a
PHY
11
MAC
MAC
Bridge
H2
PHY
H2
DLC
H2
CL
MAC
Bridge
Hybrid
PHY
Hybrid
MAC/DLC/CL
MAC
Bridge
Hybrid
PHY
Hybrid
PHY
H2
DLC
11
MAC
H2
CL
MAC
Bridge
Hybrid
PHY
H2
DLC
11
MAC
H2
CL
MAC
Bridge
MAC/DLC
Convergence
Layer
Implementation
Issue
(2 radios)
Interwork
(?)
Single Global
Standard
(?)
Now
Now
Interwork
(?)
Single Global
Standard
(?)

## Slide 16
802.11
802.11 ad hoc Regulatory
802 Regulatory Ombudsman
FCC
ERC
UK RA
MPT
ITU
WRC
…
BT
ETSI
MMAC
…
Relationships
802.15
802.16
802

## Slide 17: Concept
Motivation:
Unlicensed spectrum is sparse
There are multiple types of equipment sharing the spectrum
Standards acceptance (and Market) success depends on vendor and customer confidence in robust products
Observation:
IEEE 802 Wireless working groups need to improve the method by which standards using the 5GHz spectrum are developed by 802.11, 802.16 and 802.15.