## Slide 1: Dynamic Frequency Selection (DFS) and Transmit Power Control (TPC) Joint Proposal for 802.11h
S. Choi1, S. Gray2, M. Kasslin2, S. Mangold3 and A. Soomro1 Philips Research1, Nokia Research Center2
and ComNets Aachen University3

## Slide 2: Outline
Dynamic Frequency Selection
Transmit Power Control

## Slide 3: Part I
Dynamic Frequency Selection

## Slide 4: DFS Procedure
Channel Monitoring
  AP Channel Measurement Requests
  Channel Measurement Process in STAs
    STA’s Measurements  AP’s Measurements
  Measurement reports from STAs to AP
AP decision making
AP Channel Switch Announcement
The new channel switch !

## Slide 5: AP Channel Measurement Requests
New Channel Measurement Request management frame
  Using generic action request frame format
  When, how, and which channel(s) to measure
  Two channel measurement method information elements
No Changes

## Slide 6: Channel Measurement Request Management Frame
Using generic action management frame - TGe

## Slide 7: Channel Measurement Method Information Elements
Basic channel measurement method information
CF channel measurement method information

## Slide 8: Channel Measurement Report Management Frame
Using generic action management frame from TGe

## Slide 9: Channel Measurement Report Information Element
To report results about n channels

## Slide 10: Channel Measurement Report Information (Cont.)
Measurement Summary field
Each octet in Received Signal Strength Range Indicator (RSSRI) Statistics Field

## Slide 11: Channel Switch Announcement
Channel switch announcement element information in beacon frames
No Changes

## Slide 12: (Re)Association Frame Request Frames
A STA conveys its supported channels via Supported Channels Information Element
Order
Information
5
Supported Channels
Modification to Association Request Management Frame
Order
Information
6
Supported Channels
Modification to Reassociation Request Management Frame

## Slide 13: Supported Channels Information Element
Each bit corresponds to a channel
  Bit 0  Channel 1
  Bit 199  Channel 200

## Slide 14: Capability Information
Two new bits added
  TPC: A STA can understand TPC related frames and information - bit 11
  DFS: A STA can understand all the DFS related frames and information, can perform the channel measurements and can generate measurement reports - bit 12
An 802.11h compliant AP and STA shall set both these bits

## Slide 15: Advantages
Adds minimal protocol to ensure interoperability
Provides good assessment of channel state via Measurement Summary and Reports
Enables detection of other licensed signals
Flexibility for vendors to include algorithms of their choice

## Slide 16: Part II
Transmit Power Control

## Slide 17: Outline
Overview of Revised TPC Proposal
  (E)DCF Mechanism
  PCF and HCF Mechanism
  Additions to Beacon and Probe Response/Request
  IBSS
Changes from March meeting
Conclusions

## Slide 18: Overview of TPC Methodology
(E)DCF
  One suggested power setting is used by all STAs1
  STAs indicate power capabilities in (Re)Association Request
PCF and HCF
  Transmit power may be different for all STAs where transmit power is set by each STA within maximum bounds set by AP
  Lowering power on a per STA basis will
    Improve battery life
    Improve network capacity
  Increasing power on a per STA basis for a short time can improve frame error rate
1. Steven Gray and Venkatesh Vadde, Throughput and Loss Packet Performance
of DCF with Variable Transmit Power, IEEE802.11-01/227

## Slide 19: TPC with (E)DCF
Existing Country Informational Element from TGd is used to communicate
  Frequency channels in the regulatory domain
  Maximum EIRP (relative to omni) for each frequency channel
New beacon order is added to accommodate power adjustments from the maximum level
(Re)Association Request is augmented to contain the maximum transmit power capabilities of the STA

## Slide 20: TPC with (E)DCF (2)
First Channel Number: first channel where power setting is valid
Number of Channels: self explanatory
Maximum Transmit Power Level: EIRP in dBm
AP has the discretion to determine how much information to send (minimum requirement is one set of First Channel Number, Number of Channels, and Maximum Transmit Power Level)
Country Information Element

## Slide 21: TPC with (E)DCF (3)
First Channel Number Field
Maximum Transmit Power Field
  Signed number from -127 to 128 dBm

## Slide 22: TPC with (E)DCF (4)
New Beacon Order allows the AP to adjust transmit power relative to the maximum in 3 dB steps
Power Setting Relative to the Maximum
  4 bits allow changes from 0 dB to -45 dB

## Slide 23: TPC with PCF and HCF
Power is up to STA
  Any power setting up to and including Power Setting Relative to Maximum from the Power Level Adjustment Information Element is allowed
  STAs can optimize for power consumption, error rate, etc
Service field is modified so all frames are stamped with transmit power (easy estimation of path loss)

## Slide 24: TPC with PCF and HCF(2)
New Service field definition uses currently undefined bits
Reserved
Power Setting Relative to Maximum
Scrambler Initialization
B1
B7 B8
B11 B12
B16

## Slide 25: TPC for IBSS
TPC requirements for the Ad Hoc mode are satisfied by reducing the power used by all STAs as suggested in [1] by 3 dB from the maximum allowed in the band
1. Greg Chesson and Bill McFarland, “Atheros DFS/TPC Proposal”, IEEE802.11-00/270, September 2000

## Slide 26: What Has Changed?
(E)DCF
  Transmit power setting is a “should” instead of “shall”
  Country Information Element is used as is from TGd work
  (Re)Association Request contains maximum transmit power information
  Service field is used to “stamp” each frame with the transmit power setting
PCF and HCF
  STAs decides what transmit power to use
  Service field is used to “stamp” each frame with the transmit power setting

## Slide 27: TPC Summary
Provides mechanisms for vendors to meet the minimum requirements of the ERC for transmit power control
DCF
  Flexible solution allowing AP to inform BSS of power setting
PCF and HCF
  STAs decide power autonomously
  Improve battery life
  Improve QoS