## Slide 1: Tiered Transmit Power Control, 01/215r1
Peter Larsson
Ericsson Research
Torshamnsgatan 23, Kista
164 80 Stockholm, Sweden
peter.larsson@era.ericsson.se

## Slide 2: Outline
Introduction
Functional description
  Illustration of function
  Formats and MSCs
Summary & Conclusions

## Slide 3: Introduction
TGh has as objectives to design TPC and DFS for 802.11.
TPC is considered in this proposal
Task: Design a TPC scheme that meet the following basic input
  “All requirements …. are to be met by IBSS and infrastructure BSS, during DCF or optional PCF operation…..”. [Functional Requirement 01/071]

## Slide 4: TPC design Philosophy
Solve the generic IBSS problem. BSS treated as a special case of IBSS.
Build solution on DCF, not PCF or HCF. DCF is widely deployed and it is the legacy access mechanism of 802.11.
TPC shall integrate well with power saving mechanisms.
TPC inherently interacts with MAC (for all proposals). Therefore, TPC shall integrate well with MAC mechanisms. Hence TPC frames & IEs must be put in a context to test viability. Ensure backward compatibility.
Generate least possible interference and consume least possible energy.

## Slide 5: TPC design Philosophy - Tiered TPC
Several TPC mechanisms and settings.
Bulk traffic uses the most accurate TPC. Energy minimization.
Topological constraints exists.
Transmit range
Rarely sent frames
Occasional sent frames
Prevalent sent frames
High transmit power
Moderate transmit power
Minimal transmit power

## Slide 6: TTPC Main Features
Distributed operation
DCF Integration
Tiered TPC mechanisms
  Fixed TP
  Open loop TPC
  Closed loop TPC

## Slide 7: Illustration of function
Reason: Important to understand what effects TPC has on channel access.
Start with an example scenario. IBSS with RTS-CTS-DATA-ACK phase.

## Slide 8: Beacon (IBSS)
Beacon sent around TBTT
STAs take turn to transmit Beacon (randomized)
Power save STAs (normally) wake up and listen for (or send) Beacon
Fixed Domain specific TP setting is adopted. Distribution of the same.
Enables open loop TPC

## Slide 9: Fixed domain transmit power information distribution
A STA initiating an IBSS determines transmit power levels from its MIB.
STAs joining the IBSS replicate and distribute the domain information

## Slide 10: Open Loop Path Gain Estimation in IBSS
Beacon
Beacon
transmit
range
Beacon
Beacon
Beacon
transmit
range
Beacon
Beacon
Beacon
Beacon
transmit
range
Legend:
STA
Range
IBSS 1
time
Beacon
Beacon
Beacon

## Slide 11: Minimum Receive Power PRX_min Estimation in IBSS
Legend:
STA
Range
IBSS 1
IBSS 2
Interference
Interference
IRX
IRX
IRX
IRX
Minimum required receive power PRX_min is determined with help of respective IRX
and noise level.
IRX
IRX
IRX
IRX
PRX_min
PRX_min
PRX_min
PRX_min

## Slide 12: Open Loop TPC estimation
OL transmit power = Prx_min - G [dB] G = RSSI - PTX [dB]
Algorithmic Complexity O(N) frames
  for N STAs to determine N·(N-1) power levels
  Each STA determines N-1 entries
  Low complexity compared to a individual request-reply scheme O(N2)
Interacts with power save mode

## Slide 13: Legacy STA in Open Loop TPC
Detection
Handling

## Slide 14: Legacy Detection
TPC enabled STAs sends special TPC information in Beacon and other frames. Legacy STA don’t send such information

## Slide 15: Legacy STA handling
Legend:
STA
Range
IBSS
A STA detecting a legacy STA uses max allowed transmit power.
A STA indicate detection of a legacy STA by setting PRX_Min= max.
STAs within own (I)BSS hearing Beacon with PRX_Min= max
uses maximum allowed transmit power.
Legacy
STA
Legacy
STA
transmit
range
TPC enabled STA
PRX_Min= max
TPC STA Beacon
transmit range
STA hears PRX_Min= max
uses max transmit power

## Slide 16: Example state diagram Legacy STA handling
S1
normal
TPC
S2
normal
TPC
S3
Indicate
use of max
power
At detection of
presence of
any legacy STA
and set timer 1
Detection of
transmission from
any legacy STA
and set timer 1&2
Timer 1
expires
Timer 2
expires
Detection of
transmission from
any legacy STA
and set timer 1&2

## Slide 17: Open Loop TPC usage
(I)BSS Group TPC
  RTS, CTS, ACK
  Single DATA frames shorter than dot11RTSThreshold
  Multicast/ Broadcast
Unicast setting (optional)
  Last ACK in a frame exchange sequence

## Slide 18: (I)BSS Group TPC Philosophy
The channel is seen as one resource in an (I)BSS
All nodes within the (I)BSS should be reached with both RTS and CTS.
  Reason: Physical carrier sense desirable for both RTS and CTS in the whole (I)BSS.
Floor in adjacent (I)BSS should preferably not be acquired unnecessary.
Avoid generating high interference (peaks).

## Slide 19: IBSS Group TPC determination
Transmit power = min( max( P1, P2,….PN-1), device TP limit)
  N.B. 3 dB mitigation factor shall be catered for. Shall be ensured that the device transmit power limit can be used for shorter time for maximum range.

## Slide 20: (I)BSS Group TPC
Legend:
STA
Range
IBSS 1
RTS
CTS
IBSS 2
Interference
IBSS 2
Interference
RTS
PRX_min
PRX_min
PRX_min
As PRX_min reflect the interference level
Transmit power will adjust accordingly

## Slide 21: Comment on Open Loop TPC
The proposed Open loop TPC acquire all knowledge and has all functionality needed for a rudimentary distributed TPC.

## Slide 22: Closed loop TPC philosophy & usage
Closed Loop TPC is used as a complement to further refine performance.
Utilize exchanged frames (e.g. RTS-CTS) to perform precise and instantaneous TPC.
Perform CL-TPC on bulk traffic, i.e. Unicast DATA/ Management frames longer than dot11RTSThreshold

## Slide 23: Closed Loop TPC
Legend:
STA
Range
IBSS 1
time
RTS
RTS
Power
CTS
CTS
RTS
DATA
DATA
RTS
CTS
ACK
RTS
CTS
DATA
ACK
This ACK may optionally
be sent with lower
transmit power

## Slide 24: Open & Closed Loop TPC MSC
RTS
CTS
DATA
ACK
IBSS group TPC setting
Closed loop TPC setting
IBSS group TPC setting
or optionally
unicast TPC setting
TPC setting
NAV setting upon
hearing source STA
NAV setting upon
hearing destination STA
CTS informs Source
about relative transmit
power change
Source
Destination
Concern about NAV being reset after detecting RTS but not DATA?
See Next page.

## Slide 25: NAV setting issue
IBSS
Large distance between
source and destination STA
RTS-DATA overlap
 NAV is not reset
RTS
CTS
DATA
ACK
IBSS
Short distance between
source and destination STA
RTS-CTS Overlap
 NAV is not reset
RTS
CTS
DATA
ACK
S
D
S
D

## Slide 26: NAV setting issue cont.
IBSS
RTS
CTS
DATA link rate =
RTS link rate
ACK
S
D
DATA overlap RTS
 NAV is not reset
DATA link rate >
RTS link rate
6  54 Mbps require
roughly 15 dB higher C/I

## Slide 27: BSS Open Loop TPC
In a BSS, as STAs do not send Beacons regularly. How should transmit power be estimated ?

## Slide 28: BSS Open Loop TPC
Legend:
STA
AP
Range
BSS
The AP selects a STA.
The AP selects a STA
Issues a Probe request asking the selected STA to respond with TPC information. Transmit just after the Beacon to align with the wake up phase.
Probe Request
IE Transmit power request
The AP selects a STA
Issues a Probe request asking the selected STA to respond with TPC information. Transmit just after the Beacon to align with the wake up phase.
The response is a Probe response containing PTX and PRX_min
Probe response
PTX, PRX_min
The AP selects a STA
Issues a Probe request asking the selected STA to respond with TPC information. Transmit just after the Beacon to align with the wake up phase.
The response is a Probe response containing PTX and PRX_min
Open loop transmit power is estimated as in the IBSS.

## Slide 29: BSS Open Loop TPC
AP determines polling sequence. Implementation specific.
Algorithmic complexity retained = O(N)

## Slide 30: New IEs
Transmit Power Information Request Element
Transmit Power Information Element

## Slide 31: IEs are conveyed in
Beacon modifications
Probe request modifications
Probe response modifications

## Slide 32: IE issues
The proposed IE extension is backward compatible to legacy STA, i.e. They neglect new IE fields.

## Slide 33: Frames
Frame
control
Duration
PTX_Req
RA
FCS
TPC CTS frame
MAC header
2
2
6
4
1
PTX_Request
Frame
control
Duration
PTX_Req
RA
FCS
TPC ACK frame
MAC header
2
2
6
4
1

## Slide 34: Frame format issues
PTX_req field incur no extra OH, merely a fuller OFDM symbol for all link rates.
TPC CTS (ACK) is only sent from and to TPC enabled STAs. If one or two legacy STAs are involved, legacy CTS (ACK) are used
TPC CTS (ACK) sets NAV on legacy STA, i.e. backward compatible.

## Slide 35: Frame format issues cont.
Legacy CTS (ACK) and TPC CTS (ACK) can coexist
  Method 1: Differentiate through PHY length or address information + CTS subtype field
  Method 2: Define new subtype for TPC CTS

## Slide 36: MSCs
RTS
CTS
DATA
ACK
Tier 2
Tier 3
RTS
CTS
DATA
ACK
DATA
ACK
DATA
ACK
Tier 2*
Tier 2
Tier 3
Tier 2
Tier 3
Tier 2
Tier 3
Tier 2*
Lower transmit power may be used
NAV setting- virtual channel sense
NAV setting - physical channel sense
DATA
ACK
Tier 2
DATA
ACK
Tier 2
Tier 3
DATA
ACK
DATA
ACK
Tier 2
Tier 3
Tier 2*
*
TPC setting
TPC setting
TPC setting
TPC setting

## Slide 37: Summary
A Tiered TPC scheme, able to operate in both BSS and IBBS network, on basis of the fundamental DCF channel access scheme has been presented.
TTPC uses fixed TP, OL and CL TPC

## Slide 38: Summary
It is characterize by low OH, low algorithmic complexity, insurance of backward compatibility, speed and precision
It has also been shown how the interaction between TPC and channel access scheme has been considered in this proposal.

## Slide 39: Conclusion
It is our belief that this proposal can meet current as well as future requirements on TPC.
It is our recommendation that this proposal shall be considered for TPC in 802.11a.