## Slide 1
Overview of the Proposal for DFS and TPC
Christopher J. Hansen and Joonsuk Kim
Broadcom Corporation

## Slide 2: Outline
Background
Review of PHY and MAC Modifications
TPC Operation
DFS Operation
Advantages of Our Proposal
Summary

## Slide 3: Background
Broadcom Complete DFS/TPC Proposal
  Proposal: 802.11-01/217
  Answers to Functional Requirements / Comparison Criteria: 802.11-01/218

## Slide 4: Background
Our proposal achieves several design goals
  Meet the requirements of TGh and ERC
  Minimize changes to 802.11a PHY / 802.11 MAC
  Simple to understand
  Flexible with regard to implementation

## Slide 5: PHY and MAC Modifications
Standardize power (EIRP) settings
Standardize RSSI Measurement Levels
Add TPC Status and DFS Status elements to Beacon Frames
Add TPC Inquiry, TPC Request, and DFS Request elements to Probe Request Frames
Add TPC Status, TPC Response, and DFS Response to Probe Response Frames

## Slide 6: TPC Operation
Fixed Maximum TX Power Level
  The maximum TX power level is mandatory for all STAs in the BSS
  AP announces this level with TPC Status element in the Beacon frame
  STAs can request the maximum TX power level information with a TPC Inquiry element in a Probe Request frame

## Slide 7: TPC Operation
Adjustable TX Power Levels
  “Receiving” STA can use a TPC Request element in a Probe Request frame to:
    Inquire about the current TX power level
    Request the TX power level be set
  “Transmitting” STA will respond with a TPC Response element in a Probe Response frame
  Following a TX power setting request is not mandatory, but using the closest possible power setting is recommended.

## Slide 8: TPC Operation
AP
STA
Interference

## Slide 9: TPC Operation
Desired signal path is symmetric
Interference paths are not
Signal-to-Interference ratio at each receiver is different
Receiver must instruct the corresponding transmitter to send the appropriate power level

## Slide 10: TPC Operation
STA sends Probe Request frame with TPC Request element to AP. Flag octet is set to zero.
AP responds with Probe Response frame with a TPC Response element. TX Power Level octet is set to 111000, indicating +23 dBm (200 mw) TX power.
STA determines that +23 dBm is more power than it requires and that +17 dBm is adequate. STA sends a second Probe Request frame with a TPC Request element. This time the Flag octet is set to 1 and the TX Power Level octet is set to 110010, indicating +17 dBm.

## Slide 11: TPC Operation
AP responds with a Probe Response frame containing a TPC Response element. The TX Power Level octet is set to 110010, indicating that is now using a TX EIRP of +17 dBm.

## Slide 12: DFS Operation
AP has two mechanisms for determining the channel state:
  It’s own receiver
  Request STAs within the BSS to make RSSI measurements on any channel (including the current BSS channel)
RSSI data is reported to AP in a simple histogram format

## Slide 13: DFS Operation
AP determines when a channel change is necessary
AP provides new channel information and a countdown in the DFS Status element of a Beacon frame

## Slide 14: Example DFS Scenario
BSS
AP requests RSSI information on channels #1, #2, and #3
  STA A sees alien interference on channel #1
  STA B sees another BSS on channel #2
AP selects channel #3
AP
STA A
STA B
Alien interference
Overlapping BSS

## Slide 15: Advantages of Our Proposal
Simplicity
No extra regulation when not required
Compatible with TGe without being dependent on rapid resolution of TGe ballot comments
Flexible implementations

## Slide 16: Summary
Our proposal provides a complete solution to the TPC/DFS requirements of Task Group H.
Our proposal provides the most flexibility, allowing equipment vendors to design and build interoperable solutions with the best technology.