## Slide 1: EAP Authentication Suite Advertising
Submitted to IEEE802.11 TGi
May 2001
J.P. Edney, Nokia

## Slide 2: Why have Authentication Suite Selector?
  To allow Access Point to advertise security capabilities
  To allow Client to select option(s) in association request
In current draft only few choices are possible (vendor proprietary excluded)
  Open Authentication (non ESN)
  Shared Key Authentication (non ESN)
  Kerberos over 802.1X
  Unspecified authentication over 802.1X

## Slide 3: What is value of choices?
  Open Authentication (non ESN)
  Shared Key Authentication (non ESN)
These are not understood by legacy non ESN clients and not likely to be used by ESN clients
  Kerberos over 802.1X
According to current draft this is mandatory so it is always advertised - only useful in selection process
  Unspecified authentication over 802.1X
No information provided by this element since this is always possible option in ESN

## Slide 4: Why provide more information?
  In some cases the network may support a limited or single EAP method other than Kerberos (e.g. EAP/TLS or EAP/GSMSIM)
  Under current draft AP can only advertise “unspecified EAP/802.1x”
  This means clients must associate and initiate EAP transaction to discover what EAP method is supported - and then disassociate when it is discovered that a compatible method is not available
  Overhead can be reduced if AP can advertise the supported EAP method(s) - clients need not associate unnecessarily

## Slide 5: Proposal to add new EAP Suite Specifier
Current
Proposed

## Slide 6: Details of Authentication Suite Element
Element ID (TBD)
Length
Authentication Suite List
Authentication Suite Element - Unchanged format
OUI (3 Octets)
Suite Specifier (1 Octet)
Authentication Suite Specifier (0 - 3) - Unchanged format
OUI (3 Octets)
Suite Specifier (1 Octet)
Authentication Suite Specifier 4 - New format
EAP Number (2 Octets)

## Slide 7: How does AP know what EAP methods are supported by network?
According to the general case of EAP/802.1X the access point need not know what EAP method is used.
EAP frames are forwarded to Authentication Server which generates EAP messages
AP just looks for EAP success / fail
In principle AP cannot know which EAP method is supported by network
To use advertising feature administrator must configure AP with selected EAP method(s)
This is ONLY required if using feature

## Slide 8: Summary
Current Authentication Suite Selectors are very limited
There is value to advertise EAP method for specialized networks
Addition of option “Specified EAP” selector provides required information
Recommend to adopt proposed text to draft: doc:IEEE 802.11-01/xxx

## Slide 9: Motion
Motion to adopt the changes identified in doc: IEEE 802.11-01/xxx into 802.11eD0