## Slide 1: 802.11a/e and HIPERLAN/2 Interworking using HCF
Stefan Mangold1, Sunghyun Choi2, Wolfgang O. Budde2, and Chiu Ngo2
1ComNets, Aachen University
2Philips Research

## Slide 2: Interworking between 802.11a/e and H2
Using upcomding 802.11e Hybrid Coordination Function (HCF)
Propose a hybrid of an H2 Centralized Controller (CC) and 802.11a/e Hybrid Coordinator (HC), referred to as CCHC, which works as
  HC to 802.11a/e enhanced stations (ESTAs)
  CC to H2 mobile and wireless terminals (MTs/WTs).
CCHC allows the support of all convergence levels of 802.11 and H2, specifically the interworking.

## Slide 3: The CCHC-Interworking Solution
CC (H2 Central Controller)
HC (802.11 Hybrid Coordinator)
Dual protocol inside coordinator
H2 MTs/WTs use AP_Absence

## Slide 4: Basic Access Mechanism
H2 MAC frames are integrated in CP and CFP

## Slide 5: When to Grab Channel for H2
CCHC should grab the channel and suppress other 802.11e ESTAs to schedule H2 MAC frames
If an H2 MAC frame is scheduled at t=0, CCHC should grab the channel within
  [- TXOP_limit - QoS CF-Poll duration - SIFS,
  - QoS CF-Poll duration - SIFS]
For EDCF TXOP is shorter than TXOP_limit

## Slide 6: How to Grab Channel (1)
QoS CF-Poll transmitted by CCHC and addressed to itself.

## Slide 7: How to Grab Channel (2)
CCHC transmits downlink frames right after PIFS and continues with H2 MAC frames.

## Slide 8: How to Grab Channel (3)
The CCHC grabs the channel by transmitting QoS CF-Poll to grant TXOP to ESTA(s).

## Slide 9: CCHC Benefits ...
H2 MAC frames are integrated in CFP as well as CP  flexible approach
CCHC is centrally coordinated by HCF  no QoS compromise
H2 MTs/WTs as defined in the standard are fully supported  no changes in the standard
802.11 ESTAs as discussed in TGe QoS draft 1.0 are fully supported  no changes in the standard

## Slide 10: Summary
A hybrid of 802.11e HC and H2-CC, called CCHC is proposed
CCHC has both 802.11a/e and H2 MAC/PHY implementation
Resource sharing between 802.11a/e and H2 without compromise of QoS
Base for a coexistence and interworking as discussed at 5GSG/TGj

## Slide 11: References
Stefan Mangold, Sunghyun Choi, “802.11a/(e) and HiperLAN/2 Interworking via CCEPC,” IEEE 802.11-01/067, January 2001.
Stefan Mangold, Sunghyun Choi, and Thorsten Wiemann, “Contention-Free Scheduling of HiperLAN/2 Frames without QoS Limitations,” IEEE 802.11-01/013, January 2001.
ComNets, Philips. “Coexistence and Interoperability of HiperLAN/2 and IEEE 802.11a”. ETSI BRAN#21, BRAN21d126.
NEC, NTT, Matsushita. “Convergence levels for 802.11a and HiperLAN 2”. ETSI BRAN#21, BRAN21d127.