## Slide 1: Time Synchronization Function for Low Jitter Applications
Toru Ueda
Yoshihiro Ohtani
Hiroyuki Nakaoka
Sharp Corporation
Nara, Japan
E-Mail: ueda@slab.tnr.sharp.co.jp

## Slide 2: An issue for very short jitter applications(1)
File data (Asynchronous)
Read request
1. DVD player with file sharing
Two important AV applications
Asynchronous Data
= The receiver will request data whenever it wants
There is no jitter problem
because the receiver controls the data flow.

## Slide 3: An issue for very short jitter applications(2)
Isochronous Data
No flow control
CS/BS tuner
D-VHS
HD-VCR
Digital Video
2. Tuner type applications(MPEG2TS/DV)
The source and destination time should be synchronized
for isochronous applications.
Application’s jitter requirements should be kept.

## Slide 4: Requirements for transmitting MPEG2-TS over 802.11
#1
188byte
#2
#3
T1
T2
T3
T4
MPEG2-TS
Interval
#1
#2
#3
#4
T1
T2
T3
T4
MPEG2-TS
Interval
( Transmission via 802.11 )
MPEG2 Encoder
PCR needs
+/- 500ns ( = 1us )
of clock accuracy
( ISO/IEC 13818-1 )
MPEG2 Encoder
MPEG2-TS packet includes
PCR ( Program Clock Reference )
#4

## Slide 5: Problem for transmitting MPEG2-TS over 802.11
Beacon from AP
- If the system clock accuracy is +/-100 PPM and the beacon
interval is 100ms, then, Max. 20us jitter (>> 1us) will occur.
- This jitter value(20us) over IEEE802.11 is much larger than
what is acceptable to MPEG2 System(1us).
Beacon Interval = 100ms
AP
(100PPM)
STA
(100PPM)

## Slide 6: Possible Solutions (1) Improve the clock accuracy of each station
Beacon from AP
- If the system clock accuracy is +/-5 PPM ( the beacon
interval is 100ms ), then, Max. jitter becomes 1us.
- However, getting the +/-5PPM is very difficult.
- The clock accuracy of AP station cannot be improved.
AP
(5PPM)
STA
(5PPM)
Beacon Interval = 100ms

## Slide 7: Possible Solutions (2) Shorten the beacon interval
Beacon Interval = 5ms
- If the system clock accuracy is +/-100 PPM and the beacon
interval is 5ms and, then, Max. jitter becomes 1us.
- 5ms beacon interval leads to inefficient media use.
- The beacon interval of AP station cannot be shortened.
AP
(100PPM)
STA
(100PPM)

## Slide 8: Proposed Solution QoS TSF Timer information in QoS CF-Poll
- HC sends QoS TSF Timer information in every CF Poll Packet.
( QoS TSF Timer value is not necessary to be synchronized
with TSF Timer in AP. )
- HC sends CF Poll Packet at least once in any 5ms for MPEG2TS.
Beacon from AP
Beacon Interval = 100ms
AP
(100PPM)
STA
(100PPM)
HC
(100PPM)
CF-Poll from HC

## Slide 9: Proposed Change
Frame
Control
Duration
/ID
Address
1
Address
2
Address
3
Sequence
Control
FCS
QoS
Control
2 byte
2 byte
6 byte
6 byte
6 byte
2 byte
4 byte
2 byte
QoS
TSF Timer
4 byte
2. Add QoS TFS timer field in QoS (+)CF-Poll frame.
1. Add QoS TSF mode bit in TS info field.
Traffic
Type
QoS
TFS
mode
Ack Policy
Reserved
(0)
Sequence
Control
Bits: 0
1
2
3
4
5
6
7
0: QoS TFS Timer is not used.
1: QoS TFS Timer is used.