## Slide 1: A Proposal for Dynamic Frequency Selection (DFS)
Simon Black, Qosine Mika Kasslin, Nokia
simon.black@qosine.co.uk mika.kasslin@nokia.com

## Slide 2: Objective
A reasonably complete and self-consistent proposal for DFS
  Cover BSS and IBSS
  Address comments made during the presentation of the 11-01-532 IBSS DFS proposal presented in January
  Attempt to limit complexity
  Attempt to write the submission in a draft-ready format

## Slide 3: Reference Material
IEEE P802.11h/D1.1, January 2002, Spectrum and Transmit Power Management extensions in the 5GHz band in Europe
11-01-532r0, Dynamic Frequency Selection (DFS) in an Independent BSS, S. Black/S. Gray – Nokia, S. Choi/A. Soomro – Philips
11-01-533r0, An IEEE802.11h MIB Definition, S. Black – Nokia
11-01-538r0, Layer Management Extensions for Spectrum Management, S. Black – Nokia, S. Choi/A. Soomro – Philips
11-02-154r2, Proposed DFS text, A. Myles – Cisco

## Slide 4: Key Principles – Role of IEEE802.11h
Objective of IEEE802.11h is to ensure that IEEE802.11a systems meet the regulatory rules
  Choice of BSS operating channel should meet regulatory rules
  Each device should adhere to the regulatory rules when a primary user is detected
  Mechanisms should be provided to assist in making accurate channel measurements
  A IEEE802.11 user should ideally not be aware that a primary user was detected
    Signalling of primary user detection within a BSS
    Organised re-location to an alternative channel

## Slide 5: Key principles – Device Responsibility
Every IEEE802.11h device is responsible for adhering to the regulatory rules
  Has the ability to measure a channel
  Has some algorithm to detect primary users that is compliant with the appropriate regulations and passes the relevant conformance test
  Stops transmission on the channel within the appropriate time after detection of a primary user

## Slide 6: Key Principles – This Proposal
Quieting channels for measuring
Requesting and reporting of channel measurements
Detecting licensed users
Discontinuing operations after detecting licensed users
Selecting and advertising a new channel

## Slide 7: Channel Measurements – Quiet Period
Define a BSS-wide channel quiet period to assist in making accurate channel measurements
Signalled using an element in Beacon and Probe Response Management Frames
MAC behaviour around a channel quiet period is as defined for a dwell period in clause 9 of IEEE802.11-1999
 | Element ID | Length | Measurement Count | Measurement Period | Measurement Duration
Octets: | 1 | 1 | 1 | 1 | 2

## Slide 8: Channel Measurements – Requests/Response
 | Element ID | Length | Measurement Token | Measurement ID | Measurement Request
Octets: | 1 | 1 | 1 | 1 | variable
 | Element ID | Length | Measurement Token | Measurement ID | Measurement Response
Octets: | 1 | 1 | 1 | 1 | Variable
Request Element Format
Response Element Format

## Slide 9: Basic Channel Measurement Request/Report
Measurement
Duration
Number of Channels
Channel a
2
1
1
1
Octets:
Channel b
Channel c
Channel List
1
 | Measurement Duration | 
 | Channel Number a | Basic Channel Report a
 | Channel Number b | Basic Channel Report b
 | Channel Number c | Basic Channel Report c
 | … | …
Octets: | 1 | 1
Basic Measurement Request Format
Basic Measurement Response Format

## Slide 10: Basic Channel Report
Consists of a set of flags to signal various measurement results
Local and Not-Supported flags are used to signal the significance of the report in Channel Maps for IBSS DFS
Bit | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Sub-field | Reserved | Unknown | BSS | Foreign PLCP | Primary User | Un measured | Not Supported | Local

## Slide 11: Organization Specific Request/Report
A container mechanism for any Organization Specific measurements
OID
Organization Specific Request/Report
3
Variable
Octets:

## Slide 12: Primary User Detection
STA stops transmission of data and control type frames within a period (x) defined within the MIB and set to meet regulatory requirements
STA stops transmission of management frames within an extended period (y) again defined within the MIB and set to meet regulatory requirements
Extended management period allows channel measurement reporting and channel switch signalling
Time
ALL
MANAGEMENT ONLY
Primary User Detected
y
x

## Slide 13: DFS in a BSS – Admission Control
If the MIB attribute dot11SpectrumManagementEnabled is set equal to true when the MLME-START.request primitive is issued, then the BSS will be spectrum managed
STAs dot11SpectrumManagementEnabled is set equal to true shall not join non-spectrum managed BSSs
An AP operating in a spectrum managed BSS shall not permit a STA to associate or re-associate unless the STA is has spectrum management enabled.

## Slide 14: DFS in a BSS – Measurement
Access Points may use the measurement request/report mechanism to collect data from associated STAs
If a primary user is detected by an associated STA an best effort attempt is made to send an autonomous channel report to the AP

## Slide 15: DFS in a BSS – Channel Switching
An AP may attempt to move the STAs that are associated in its BSS to a new channel by advertising a channel switch using the Channel Switch Announcement element in Beacon and Probe Response frames
The Channel Switch shall be scheduled to give the best chance for all STAs to receive the new channel information
Any new channel advertised shall comply with the regulatory rules regarding measurement & spreading
A Channel Switch event is equivalent to a dwell time in IEEE 802.11-1999 clause 9

## Slide 16: DFS in an IBSS – Background
DFS in an IBSS requires additional functions since:
  There is no central AP function for collating measurements, or channel switching, e.g. if STAs make independent decisions to move channel in the presence of a primary signal, there is a danger that all STAs will announce a switch to differing channels if several of them detect a primary user.
  There is no association protocol that can be used to (a) determine membership of the BSS at a given instant, or (b) establish the supported channel set.
  Beaconing is a shared process and therefore it cannot be guaranteed that an STA that has something to send such as a channel switch message will be the next STA to beacon.

## Slide 17: DFS in an IBSS – Start
STA that starts the IBSS
  Determines whether the IBSS is to be spectrum managed
  Selects the initial operating channel
  Selects the supported channel set – communicated in channel maps
  Is the initial DFS Owner
  Selects parameters for default measurement interval and DFS recovery timing

## Slide 18: IBSS DFS Element
 | Element ID | Length | DFS Owner | DFS Recovery Interval | Measurement Duration | Channel Map
Octets: | 1 | 1 | 6 | 1 | 2 | 2 * n
Supports the DFS process in an IBSS

## Slide 19: DFS in an IBSS – The DFS Owner
A STA within the IBSS that is responsible for coordinating the switch to a new channel in the case that a primary user is detected
DFS recovery ensures that the DFS owner function is regenerated if the DFS owner leaves, or cannot hear the report indicating detection of a primary user

## Slide 20: DFS in an IBSS – Measurement
STAs share information concerning supported channels and channel measurements via the channel map
  The channel map provides an equivalent mechanism to the supported channel information in association for infrastructure BSSs
  New STAs joining the IBSS have a baseline set of measurements and can take on the DFS owner role if DFS owner recovery occurs
Measurement request-report frames allowed
An STA that detects a primary user signals that immediately in an autonomous measurement report and via its channel maps

## Slide 21: DFS in an IBSS – Channel Switching
DFS owner is responsible for selecting and advertising a new channel
A direct channel switch advertisement frame is defined to overcome the fact that the DFS owner may not be the next STA to beacon
The channel switch advertisement is further communicated in beacon and probe response frames
If STAs that hear the primary user notification do not hear a channel switch within DFS recovery time, the first of those STAs to beacon shall assume the DFS owner role
There may be multiple new DFS owners, so a resolution process is defined

## Slide 22: Layer Management Extensions
SME
MLME
SME
MLME
Measurement Frame Exchanges
Measurement Requests
Measurement Reports
Channel Switch Requests
MLME Primitive additions for clause 10 to support channel measurements and channel switching

## Slide 23: A Proposal for Dynamic Frequency Selection (DFS)
Simon Black, Qosine Mika Kasslin, Nokia
simon.black@qosine.co.uk mika.kasslin@nokia.com