## Slide 1
Fast Channel Switching in 802.11h
Amjad Soomro
PHILIPS amjad.soomro@philips.com

## Slide 2: Introduction
Current Mechanism
  BSS
  IBSS
Issues
  Latency
  Potential Interference
Proposed Changes
Conclusions

## Slide 3: The Current Mechanism
The Channel Switch Announcement Element
BSS
  Transmitted by AP only
  May be repeated
IBSS (proposed, doc: 01/532)
  Initially by the DFS owner
  Re-transmitted in beacons
  May be repeated
Element ID (1 octet)
Length (2 octets)
New Channel Number (1 octet)
Channel Switch Count (1 octet)

## Slide 4: The Issues
Latency
  Several beacon periods
  Regulatory requirements
    Current European domain requirements
    Future regulatory requirements
  Potential interference/performance degradation before channel switch
NEED: A fast channel switch method

## Slide 5: The Proposed Scheme
Modify the current Channel Switch Announcement Element as:
Add field: Switch Mode
Element ID (1 octet)
Length (1 octets)
New Channel Number (1 octet)
Channel Switch Count (2 octets)
Switch Mode (1 octet)
F
Q
R
Reserved
0 1 2 3 4 5 6 7
bit

## Slide 6: Bit Field Interpretations
F: Fast Mode
  When this bit is set, the ‘Channel Switch Count’ field specifies the number of microseconds, after the end of reception of the MPDU containing this element, until the BSS or an IBSS network will move to the new channel.

## Slide 7: Bit Field Interpretations
Q: Quiet Mode
  When this bit is set, all STAs in the BSS or an IBSS shall not initiate any new frame exchange sequences in the current channel. A STA shall only transmit in the announced channel after the announced channel switch time and after the first TBTT in the new channel. In a BSS network, a STA shall wait to hear a beacon or a probe response from the AP before transmitting any Class 2 or Class 3 frames.

## Slide 8: Bit Field Interpretations
R: Repeat Mode
  When this bit is set, a STA is allowed to retransmit the channel switch information before the announced channel switch time once after reception of a management or a data frame, belonging to the same BSS.
  However, before re-transmitting the channel switch information the STA shall wait for a random backoff interval. If during the backoff time a channel switch information element, belonging to the same BSS, is received the re-transmission shall not be done.

## Slide 9: Bit Field Interpretations
  The retransmission shall be done at the minimum of the mandatory rates supported by the STA.

## Slide 10: Conclusions
A Fast Channel Switching Mechanism Proposed
Enhances the current proposal
Prudent to include in the draft.