## Slide 1: 1394 Clock Synchronization over 802.11
Javier del Prado, Sunghyun Choi, Sai Shankar, Takashi Sato, and Jeff Bennett
Philips Research-USA
Briarcliff Manor, New York
{sunghyun.choi,t.sato}@philips.com

## Slide 2: Outline
Introduction
1394 Clock Synchronization over IEEE 802.11
IEEE 802.11e MLME Higher Layer Synchronization Primitives
Conclusions

## Slide 3: Introduction
In an IEEE 1394 network, stringent clock synchronization is required to enable audio and video applications
For instance, in an audio application, trained ears can hear the clock jitter of 1.5 s [5][6]
To support a wide variety of applications, including professional audio, 1394 achieves the clock jitter of less than 41 ns (I.e., one clock tick) [4]
Wireless 1394 (by 1394 TA WWG) shall aim to achieve a similar (or the best possible/practical) accuracy in clock synchronization in order to replace wired 1394 or be seamlessly integrated into a 1394 network

## Slide 4: Introduction
A method to synchronize 1394 clocks across serial bus bridges is defined in [1], while a method to synchronize 1394 clocks over HL/2 WLAN is defined in [2]
No mechanism has been yet defined for the 1394 clock synchronization over 802.11 WLAN
In this submission we present a mechanism for stringent clock synchronization, and define a set of new 802.11 MLME primitives needed to support it

## Slide 5: Introduction
1394 Trade Association WWG has evaluated three possible solutions
  Use of Last_Symbol_On_Air timing (LSOA) (this submission)
  Use of TSF Timer
  A statistical method

## Slide 6: Introduction - Comparison
Proposal | Use of LSOA Timing | Use of TSF Timer | A Statistical Method
Accuracy of phase detection | Excellent ( 100 ns possible) | Insufficient (4 s or worse) | ??? (no valid data available)
Speed of lock-in | Fast (less than a sec) | Fast (less than a sec) | Too Slow (over a minute?)
Computational Requirement | Ok for any device | Ok for any device | Too much for non-PC
Change to 802.11 MAC | Minor (optional extension) | Impacts all devices | None
Notes: Page <number>
<header>
<date/time>

## Slide 7: Introduction
1394 Trade Association WWG (composed of many 1394 experts and a few 802.11 experts) has concluded that “Use of Last_Symbol_On_Air timing is the preferred solution and the only solution currently available that can satisfy the professional audio requirement of the clock jitter of less than 1.5 s”

## Slide 8: Wireless 1394 Scenario
(Virtual 1394 Bus)
CM

## Slide 9: Our Solution – CM transmits directly
<= 10 ms
a(n)
n
n'
1394 synchronization frame sent by CM
Cycle Master
CTR
a(n)
Cycle Slave
CTR
b(n)
a(n)

adjust
Last_Symbol_on_Air
Last_Symbol_on_Air
PHY_TXEND.confirm
PHY_RXEND.indication
1394 synchronization frame sent by CM
n
Frame
Sequence
Number
PHY_TXEND.confirm
PHY_RXEND.indication

## Slide 10: Our solution – CM transmits through HC
Cycle Master
CTR
a(n)
Cycle Slave
CTR
b(n)
a(n)

adjust
HC/ QAP
Last_Symbol_on_Air
Last_Symbol_on_Air
CM sends synchronization frame to HC
HC forwards the frame to the BSS
PHY_RXEND.indication
PHY_RXEND.indication
CM sends synchronization frame to HC with a(n)
PHY_RXEND.indication
PHY_RXEND.indication
1394 synchronization frame sent by HC
n
Frame
Sequence
Number
HC forwards the frame to the BSS
a(n)
n
n'
1394 synchronization frame sent by HC

## Slide 11: How It Works
At Cycle Master
  a(n) = CTR_Value (at observed Last_Symbol_On_Air event) – offset
  Multicasts a(n) and n in synchronization frame at a semi-regular interval (e.g. 10 ms)
At Cycle Slave
  b(n) = CTR_Value (at observed Last_Symbol_On_Air event) – offset
  Receive synchronization frames and retrieve a(n) and n
  Compare b(n) and a(n) and use  to adjust CTR appropriately
offset: delay from the end of the last symbol on the air to when capturing of the CTR value takes place

## Slide 12: Changes required in 802.11
No major change required!
Only three new primitives need to be defined to support the synchronization
The primitives will pass the 1394 synchronization frame information from the MAC to the SME
The communication between the SME and the 1394 PAL Layer is out of the scope of this submission

## Slide 13: Synchronization Primitives
MLME-HL-SYNC.request
MLME-HL-SYNC.confirm
MLME-HL-SYNC.indication

## Slide 14: MLME-HL-SYNC.request
This primitive requests activating the higher layer synchronization support mechanism
It is generated by the SME when a higher layer protocol, which requires a stringent synchronization, such as the 1394 PAL, is active in the STA
Semantics:
  MLME-HL-SYNC.request (
  RxAddress
  )
Name
Type
Valid Range
Description
RxAddress
MACAddress
A
multicast
MAC address
Specifies the
multicast MAC
address that the synchronization
frame
s are addressed
at
.

## Slide 15: MLME-HL-SYNC.confirm
This primitive confirms the activation of the higher layer synchronization support mechanism
It is generated by the MLME as a result of an MLME-HL-SYNC.request to activate the mechanism for the higher layer synchronization support
Semantics:
  MLME-HL-SYNC.confirm (
  ResultCode
  )
Name
Type
Valid Range
Description
ResultCode
Enumeration
SUCCESS,
NOT_SUPPORTED
Indicates the result of the
MLME
-
HL
-
SYNC.request

## Slide 16: MLME-HL-SYNC.indication
This primitive reports completed transmission or reception of a higher layer synchronization frame
This primitive is generated by the MLME when the successful reception/transmission of a synchronization frame is detected.
The synchronization frame is identified by the multicast MAC address indicated by the MLME-HL-SYNC.request primitive, in Address 1 field of the synchronization frame.
Semantics:
  MLME-HL-SYNC.indication (
  SourceAddress
  SequenceNumber
  ProcDelay
  )

## Slide 17: MLME-HL-SYNC.indication (II)
Parameters:
Name
Type
Valid Range
Description
SourceAddress
MACAddress
Any valid individual MAC address
Specifies the Source Address of the synchronization frame. In the case of the STA sending the frame, it will be its own MAC address.
SequenceNumber
Enumeration
As defined in the frame format
Specifies the sequence number of the synchronization frame received/transmitted.
ProcDelay
Enumeration
 0
Specifies the estimated time between the generation of this primitive and the time at which the end of the last symbol of the frame that generated this primitive was detected on the air.

## Slide 18: Summary (I)
A new clock synchronization mechanism defined for timing critical applications such as Wireless 1394
  Relies on a higher-layer clock in each node and the Last_Symbol_On_Air timing that occurs simultaneously across 802.11 WLAN
  Does not rely on TSF Timer, which may not be accessible, reliable, or accurate enough
Mechanism already approved by the 1394 WWG!
Any node can become the Cycle Master!!!
Not require any significant change in 802.11
    PHY_TXEND & PHY_RXEND are readily available
    Only three new primitives need to be defined

## Slide 19: Summary (II)
The MAC change is essentially optional !!!
    Look at MLME-HL-SYNC.confirm (Not Supported)
    E.g., no need to implement it if no plan to support timing-critical applications
Can be used for any higher layer protocol that requires stringent clock synchronization!!!

## Slide 20: References
[1] IEEE P1394.1 High Performance Serial Bus Bridge, Draft standard.
[2] ETSI TS 101 493-3 Broadband Radio Access Networks (BRAN); HIPERLAN Type 2; Packet Based Convergence Layer; Part 3: IEEE 1394 Service Specific Convergence Sublayer (SSCS), ETSI 200-09.
[3] IEEE Std 802.11-1999, Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications, Reference number ISO/IEC 8802-11:1999(E), IEEE Std 802.11, 1999 edition, 1999.
[4] IEEE Std 1394-1995, High Performance Serial Bus
[5] F. Wightman, D. Kistler: Hearing in three Dimensions: Sound Localization, AES 8th Int. Conference
[6] W. Hartmann: Localization of a Source of Sound in a Room, AES 8th Int. Conference

## Slide 21: Motion
Move to incorporate the normative text for new MLME primitives found in Section 3 (from 3.1.1) of 02/297r1 into Clause 10 of the 802.11e draft.