## Slide 1
Dynamic Update of the QoS Parameter Set
Eitan Solomon and Lior Ophir
Texas Instruments Incorporated
8 Hasadnaot St.
Herzlia, Israel
+972-9-970-6444
{eitan, lior.ophir}@ti.com

## Slide 2: Current Definition
QoS Parameter Set element transmitted by a QAP in Beacon Frames and Probe Response Frames
  CP TXOP limit, CWmin[UP], AIFS[UP]
  Section 7.3.2.14: “The QoS Parameter Set element provides information needed by QSTAs for proper operation of the QoS facility during the contention period. This information includes the CP TXOP limit, the contention window values, and AIFS values for HCF contention-based channel access. The format of the QoS Parameter Set element is shown in Figure 42.6. The QoS Parameter Set element shall be transmitted by a QAP in Beacon Frames and Probe Response Frames although its use is not necessarily limited to those frames. The QoS Parameter Set element is used by the QAP to establish policy (by changing default MIB values), to change policies when accepting new stations or new traffic, or to adapt to changes in offered load.”
Element ID (12)
Length (18)
CP TXOP Limit (2 octets)
CWmin[UP] values
(8 octets)
AIFS[UP]
values
(8 octets)

## Slide 3
Benefits of dynamic QOS parameter set
Enhance efficiency by dynamically following network changes (e.g. load changes, new QSTAs join/leave)
Example 1: A network is loaded with 10 Stations. Then 8 of them de-associate
An efficient network will reduce CWmin/Cwmax causing higher throughput on the network.
Example 2: A network consists of two QSTAs & QAP. After a while 10 other QSTAs associate
In order to reduce collisions on the network an efficient QAP will increase CWmin/CWmax

## Slide 4
Problem with Current Definition
The QAP is able to change policies by modifying the QoS parameter set element, but…
It is unclear how/when QSTAs shall act upon receiving an updated QoS parameter set element.
    Section 7.3.2.14: “CWmin[UP] values update the dot11CWmin[UP] MIB values when received by a QSTA” … “AIFS[UP] values update the dot11AIFS[UP] MIB values when received by an QSTA.”
    On Initialization? Association? Dynamically?
    Section 9.2.4: “The values of dot11CWmin[UP], and dot11AIFS[UP] are updated by information received in the QoS Parameter Set element of Beacons received from the QAP of the QBSS (see 7.3.2.14).”
    On Initialization? Association? Dynamically?
  Exception - CP TXOP Limit (section 9.10.2): “For TXOPs resulting from EDCF contention the TXOP limit value from the QoS Parameter Set element in the most recent Beacon frame shall be used.”

## Slide 5
Motivation
Define that QSTAs must update their QOS parameters dynamically according to the most recent QOS parameter set element transmitted by the QAP
2. Define when QSTAs need to change their parameter set element.

## Slide 6
Proposed solution
Add a new field to QoS parameter set element
  “QoS Parameter Set Count” - incremented by one each time the parameter set changes.
  Simplify the detection of a parameter change
Clearly define that a QSTA must update the QoS parameter set according to the most recent QoS parameter set received by the QSTA from the QAP
Define that the QSTA must effectively use the updated parameter set for all transmissions following the reception of the updated parameter set
  Friendly amendment: To accommodate software implementations this update can take effect “no later than TBD milliseconds after the reception of the updated parameter set”

## Slide 7
Benefits
Complexity
  Simpler detection of QoS parameter set changes
  Simplify H/W and S/W implementations
Interoperability
  Ensure interoperable dynamic QoS parameter set changes
QoS support
  Deterministic QSTA behavior allows for better QAP network management

## Slide 8
Motion
Move to incorporate the normative text for supporting dynamic update of the QoS parameter set, found in 02/341r0

## Slide 9
Motion
Move to direct the editor to modify the draft standard (sections 7.3.2.14, 9.2.3.4 and 9.2.4) with the following changes:
  Add a new “QoS Parameter Set Count” field to QoS parameter set element. The value in this field is initialized to zero and incremented by one each time the parameter set changes.
    The QoS Parameter set element will have the following form:
Element ID (12)
Length (19)
CP TXOP Limit (2 octets)
CWmin[UP] values
(8 octets)
AIFS[UP]
values
(8 octets)
QoS Parameter Set Count (1 octet)

## Slide 10
Motion (cont.)
  Define that a QSTA must update all QoS parameter set and associated MIBS according to the most recent QoS parameter set received by the QSTA from the QAP
  Define that the QSTA must effectively use the updated parameter set for all transmissions following the reception of the updated parameter set