## Slide 1: Discussion Introduction to Consolidated TS Normative Text
Adrian P Stephens, Mobilian Corporation
  (adrian.stephens@mobilian.com)
Purpose
  To get consensus on the essential features of a Traffic Spec (TSPEC)
Document 802.11-02/348 (without “a”) will eventually contain normative text for the TGe draft.

## Slide 2: What is a TSPEC?
A Traffic Specification (TSPEC) describes the QoS characteristics of a traffic stream. The purpose of the TSPEC is to reserve resources within the HC and modify the HCs scheduling behavior. It also controls the transmit lifetime and use of FEC and ACK policy in the downlink (defined below).

## Slide 3: What is a TSPEC? - II
Three types of TSPEC exist – specifying downlink, sidelink and uplink traffic. Uplink and sidelink TSPECs cause the HC to allocate polled TXOPS to meet a specified QoS commitment. All types of TSPEC control tx lifetime, FEC and ack policy. A TSPEC can have an optional “liveness” timer that is used to destroy a TSPEC when no traffic is exchanged on the link.
A TSPEC specifies the properties of a direct link between receiver and transmitter. In the case of a relay, each WSTA separately negotiates any QoS it needs for its link.

## Slide 4: TSPEC Lifecycle
A TSPEC is created by a request to the WSTA MLME, is transferred on-air using management frames containing the TSPEC element, is indicated via the QAP MLME to its SME. The SME’s response is carried in a management frame and generates a confirm in the WSTA MLME. This process can fail because of transmit failures, lack of response by HC, refusal by HC. The HC can propose an alternative QoS if the request is not acceptable.
A TSPEC is identified by a combination of an ID chosen by the WSTA and the WSTA’s AID.

## Slide 5: TSPEC Lifecycle - II
A TSPEC can be re-negotiated at any time, and the re-negotiation can result in an acceptance, refusal or counter proposal.
A TSPEC can be destroyed using an MLME primitive at either HC or WSTA that causes a management frame to be sent. There is no negotiation.
A TSPEC may be implicitly destroyed at the HC by expiry of a liveness timer causing a TSPEC destroy notice from the HC.

## Slide 6: TSPEC Operation
While a TSPEC exists, the HC will attempt to service the TSPEC by scheduling either TXOPs of the transmission of buffered MPDUs for that TS.
If the HC fails to meet the quality commitment, it may generate an indication via its MLME to its SME. This is optional. The HC does not attempt to monitor a sidelink.
If the WSTA detects that the HC has failed to meet a TSPEC, it may generate an indication via its MLME to its SME. This is optional.

## Slide 7: Interaction of Q-State Element and TSPEC (This section highly TBD)
A Q-state element (terminology TBD) can be sent by a WSTA that has a negotiated uplink TSPEC
A Q-state element either implicitly decreases, leaves unchanged or increases the size of the next TXOP
The HC shall honor an implicit decrease, but does not have to honor an implicit increase
In the case of a periodic TXOP, the Q-state element affects only the next sheduled TXOP