## Slide 1
Description of Requirements for Scheduler Behavior & Suggested Modifications to TSPEC
John Kowalski
Sharp Labs
July, 2002

## Slide 2: Outline
How to define normative behavior for a scheduler
Suggestions for new TSPEC parameters
Unnecessary TSPEC parameters
Conclusions

## Slide 3: How to define normative behavior for a scheduler
Parameterized QoS transmission characteristics
Constraints and conditions unique to 802.11e/ parameterized QoS transfer
Defining normative requirements of a scheduler

## Slide 4: The Scheduling Problem is an Allocation Problem
Over several beacon intervals, “blacking out” time for beacons, contention, etc. we are left with an amount of time for allocating TXOPs.
Beacon Interval

## Slide 5: Typical Assumptions
We can partition the beacon interval into those parts that are allocated for beacons & contention. Further partitions are made up to a particular granularity and no finer.
Polls, ACKs, etc. are subsumed into the allocation as needed (Poll is not part of TXOP).
Thus for the purposes of the scheduler, we basically still just have an allocation problem. However, to simplify things this allocation can be performed as part of the bandwidth management/admission control process.

## Slide 6: Constraints and conditions unique to 802.11e/ parameterized QoS transfer (1)
The medium drops packets.
The PHY rate changes.
The medium retransmits packets
Collisions happen.
The TSPEC represents an agreement between HC, WSTA, (and direct link receiver, if direct link), to provide transmission within certain bounds of latency, jitter, and throughput. But this guarantee is, because of the wireless link, probabilistic in nature.
The TSPEC supplies data on MSDU characteristics.
Many applications contend for BW with differing parameter objectives.

## Slide 7: Constraints and conditions unique to 802.11e/ parameterized QoS transfer (2)
BUT
The queue sizes are knowable by the HC.
The PHY rate is knowable by the HC
Because of the wireless medium, if the STA can, it’s always best to transmit at the highest “reliable” PHY rate, to maximize capacity & avoid collisions.
Because of parameterized QoS characteristics & wireless medium, it’s best to make polling equally distributed on the medium.

## Slide 8: Defining normative requirements of a scheduler (1)
Assume an i.i.d. channel, say, with 10% PER for a 1000 octet packet.
Assume a maximum number of retransmissions (determined from the delay bound).
Assume a maximum TXOP allocation (greater than the nominal TXOP allocation required by an error-free channel). (The scheduler would allocate more TXOPs).
The maximum TXOP allocation can be determined as follows.

## Slide 9: Defining normative requirements of a scheduler (2)
Example:
1000 octet packets (including all overhead), 4ms TXOP time, 36Mbps transmission, 8Mbps required MAC transfer rate (including all overhead), 24Mbps ACK, beacon interval of 100ms, 10% PER (no FEC). Assume i.i.d. channel. (Channel is memoryless.)
->1000 packets per second must be transmitted MAC SAP to MAC SAP.
-> 13 PPDUs can fit in a 4ms TXOP.
-> Up to 8 retries are needed for high-quality video

## Slide 10: Defining normative requirements of a scheduler (3)
Probability that at least M errors in TXOP (first row is “error free”) probability):
We can view the stream as a continuous sequence of packets, and
over-allocate TXOPs based on them. In such a case, a TSPEC violation
happens if there are more than the over-allocation bounded number of errors.

## Slide 11: Defining normative requirements of a scheduler (4)
Based on the above, we can compute, for TXOP allocations above the minimum, what the probability of schedule violation.
Consider a “naive” scheduler that allocates only 8% more TXOPs above the error-free rate. P[TSPEC violation in 1 hour]= 0.75
Consider, OTOH, a scheduler that allocates 10% more TXOPs above the error free rate. Then P[TSPEC violation in 8 hours]  3.5X10-4
Normative requirements for a scheduler can thus be formulated for admitted streams that have a certain probability of not meeting the TSPEC over a certain period of time.

## Slide 12: Defining normative requirements of a scheduler -final comments
Note: Actual 802.11 channels will often have correlated errors (dependent error rates). However, as long as the dependency 0 “fast enough” a similar approach may be taken if the dependency can be characterized.
Rate dynamically changes in practical 802.11 systems. This approach may be taken for an “average” PHY rate, or minimum PHY rate (which might be too conservative & waste bandwidth).

## Slide 13: This suggests a way to determine normative scheduler behavior - and a modification to the TSPEC
TSPECs are considered to be scheduled correctly if, with some probability pviolate the TSPEC is violated in a period of time TTSPEC.
With these parameters, some form of admission control, as well as normative behavior of scheduling, and inference of TSPEC violation could be implemented.
There is a simplification of this idea that permits simple schedulers to be built.
In addition, there are parameters in the TSPEC that we don’t feel are really needed.

## Slide 14: Definition of new TSPEC parameters (1)
T1,1
T1,3
Tcycle
T1,2
T1,N
Tcycle
Tmin
Tgap
TXOPmin
The basic time of TXOP allocation (Typically O(Beacon Interval) )
The minimum amount of total TXOP duration
which should be allocated in Tcycle.
The maximum amount of gap time between each TXOP.
The minimum amount of any one TXOP duration (useful for Burst ACK, etc.)
Tmax
The maximum amount of total TXOP duration
which is allocated in Tcycle.
…
T1,1 +T1,2 +T1,3 + … + T1,N >= Tmin
T2,1 +T2,2 +T2,3 + … + T2,N >= Tmin
Tcycle
T2,3
T2,2
T2,1
T2,N
…
Ti,j >= TXOPmin ( for all i, j )
G1,i =< Tgap ( for all i )
G2,i =< Tgap ( for all i )
G1,1
G1,2
G1,N
G2,1
G2,2
G2,N

## Slide 15: Definition of new TSPEC parameters (2)
Thus, one can infer a TSPEC violation if one asks for Tmin (which is more than enough to get the stream through assuming errored transmissions but consistently uses Tmax seconds. OTOH this Tmax parameter may be chosen to ensure robustness of the transmission while constraining the stream’s overall bandwidth requirement.
Tgap is chosen based on the number of retries permitted, the overall delay bound of the application, Burst ACK buffer size, etc.
TXOPmin is useful to guage how many retransmissions may be made per TXOP, which is useful for matching Burst ACK buffer size and TXOP size with application delay requirements.
Sender would choose these parameters- scheduler need not guess them!

## Slide 16: Definition of new TSPEC parameters (3)
Note that Tmin and Tmax can be chosen to perform the behavior to detect a TSPEC violation: if “enough” Tmax allocations (or failures to transmit a QoS Null) happen, it might be assumed the TSPEC is violated- action could be taken subject to new admission control parameters.
Bandwidth Management Policy 4 Options:
  Never tear down a stream by the HC but do not give it more bandwidth.
  Never tear down a stream by the HC but give it more bandwidth if available, without re-negotiation of the TSPEC1.
  Keep it up until the TSPEC violations are detected N times, at which point re-negotiation is done by the sender without tearing down stream (HC never tears down stream nor gives it more BW w/o re-negotiation.)
  HC may “tear down” the stream when the TSPEC is violated N times. (By simply not polling the STA).
It is assumed that the sender station will re-negotiate the TSPEC most of the time. However, the HC cannot realistically guarantee extra bandwidth beyond that negotiated for streams that go bad outside of its bandwidth management policy.
1. Someday this might cost money to an end-user.

## Slide 17: New TSPEC parameters accommodate RSVP and existing 802.11e parameters.
Path bandwidth can be mapped into the above time parameters.
Path latency and jitter can be inferred from the parameters TGAP+ knowledge of number of retries (when Burst ACK is used).
Path_MTU can be inferred from nominal MSDU size, and queue size at higher layer- there really is no need seen to negotiate this at the MAC layer, which uses fragmentation in any event.

## Slide 18: What’s not really needed in the TSPEC
Mean Data Rate
Minimum Data Rate
Delay Bound
Jitter Bound
Max Burst Size
Inter-arrival Interval
Hard to do with a scheduler
that’s working with a Burst
ACK buffer anyway. Moreover
these are collapsed
into only 1 bound in this proposal.

## Slide 19: Scheduler Model
Everybody’s TSPECs - mapped into scheduling parameters
Queue Size Information (now optional!)
For Each Flow , for each STA:
Knowledge
about “blacked out”
times (beacon, contention, OBSS info…)
A polling
Sequence
Detections of
Bad TSPECs.

## Slide 20: New TSPEC

## Slide 21: Conclusions
We’ve defined a way to characterize scheduler behavior
We’ve considered a model that allows for an HC, with minimal knowledge of stream, to infer TSPEC violations if desired.
We’ve proposed a way to simplify the TSPEC
Additional benefit: An HC need not have any additional higher layer signaling to coordinate polling!
Motion.