## Slide 1: Use-of-802.1X-with-IBSS
Tim Moore

## Slide 2: Objectives of proposal
Support “ad-hoc” nature of IBSS
Consistent with ESS solution in approach
Uses Pre-shared Master key and live session keys
Solution provides for both Pairwise and Group key

## Slide 3: Proposed IBSS Security Model
Fully Distributed (no master)
Every client has an 802.1X Authentication Server combined with an 802.1X Authenticator (abbreviated AS/A)
AS/A simple to implement with pre-shared master key.
Every client also has an 802.1X Supplicant (S)
Each pair of stations must authenticate and share keys both ways: each must be successful supplicant to the other
Once the client’s AS/A has authenticated a supplicant, it will unblock traffic and may communicate with the supplicant.

## Slide 4: Authentication Server combined with an authenticator
The authentication server does not need to be a RADIUS server.
  In the case of IBSS, there isn’t any RADIUS communication.
Each AS/A authenticates each supplicant, S
In an IBSS, each client has a supplicant.
In an IBSS, the supplicant is insufficient for communication.
  The client must also have an AS:A
AS/A
S
AS/A
S
STA1
STA2

## Slide 5: IBSS keying
Pairwise keying
Group keying

## Slide 6: Pairwise Key Exchange
Follow same approach as for ESS but with subtle difference as below:
  Each pair of stations perform key exchange separately in each direction (since each acts as supplicant in turn)
  Therefore two sets of pairwise keys are produced
  Unicast messages are encrypted with key from the Authenticator with the lower MAC address

## Slide 7: Group key
Each STA uses its own group key for its multicast transmissions – this is same concept as in ESS AP case.
Consider STAx. All other STAs that want to communicate with STAx must first exchange keys. STAx sends its multicasts using its own group key. All valid STAs can understand if they know STAx’s group key.
This is true for every STA – it has own group key and shares it only with those STAs that exchange pairwise key.
Method for creating and sending group key is the same as for ESS case (AP to STA)

## Slide 8: Details
Remove AKMP None – not required
Counter measures – same as ESS except add clarification that EAPOL-Key Requests are to go to the Authenticator that supplied the key
Discovery – when should a station authenticate to another
  Receive a packet from an unknown MAC address
Cipher negotiation
  AKMP and multicast must be the same
  Unicast negotiation is in the 4-way handshake

## Slide 9: Details
Authenticator state machine
  Change to check MAC addresses before setting the Pair variable (install Pairwise keys)
Add checks in Tx/Rx Pseudo code to check for RSN/IBSS and change key mapping rules to match for broadcast packets
Add variable to MIB dot11WEPKeyMappingsKeyBroadcast used to check if a key mapping key is for unicast or broadcast
Add flag to SetFlags – keys now come from Authenticator or Supplicant and Michael key changes

## Slide 10
Motion to include document 02/499r1 into TGi draft