## Slide 1: Enforcing QAP Policy to Deliver QoS Traffic
Amjad Soomro
Philips

## Slide 2: Current APSD Mechanisms
Legacy Power Save
  Delivery based via DTIM wakeup periods and PS-Poll
APSD Mechanism
  QSTA requests schedule and QAP responds with a schedule (may be modified) for delivery of all traffic

## Slide 3: Current APSD Mechanisms
Unscheduled Service Periods
  On demand data delivery by QAP
  Any uplink frame by a QSTA requires QAP to deliver all buffered packets for that QSTA

## Slide 4: Issues with the Multiplicity of Mechanisms
QAP is required to accept unscheduled data delivery request for all traffic
  No limit on number of QSTAs asking for such mechanism
  Large number of QSTAs using this mechanism could lead to throughput degradations
    Ref: 11-03-861r1
  Admission control not applicable for power saving devices

## Slide 5: Issues with the Multiplicity of Mechanisms
Affects on scheduler design and execution
  Scheduled and unscheduled service periods may happen simultaneously
    The scheduler design is made challenging
    The data delivery through scheduler execution is uncertain
    The delivery of scheduled data delivery in QBSS is compromised

## Slide 6: Proposed Resolution
Retain the precedence for scheduled data delivery
Allow QAP to accept unscheduled or scheduled power save mechanism
Proposed normative text in 11-03/659r0