## Slide 1: Uplink MU-MIMO Sensitivity to Power Differences and Synchronization Errors
Richard Van Nee, rvannee@qualcomm.com

## Slide 2
UL-MIMO was presented in July meeting (11-09-0852)
Several questions came up regarding sensitivity to differences in power, timing, and frequency of uplink clients
This presentation describes simulation results of the sensitivities mentioned above
Introduction

## Slide 3
Clients needs to respond to an AP uplink start indication with a timing accuracy in the order of 100 ns
    This should not be a problem, several current 11n products already have this accuracy in their SIFS response
    Use 800 ns long guard interval only for uplink SDMA to get 400 ns guard time to absorb timing errors + round trip delay differences between uplink clients
Synchronization in Time

## Slide 4
Clients need to correct uplink transmissions for the frequency offset relative to the AP
    Similar to how a receiver corrects for frequency offset in carrier and symbol clock
    Frequency error is already measured on every AP packet with a typical accuracy in the order of a kHz or better for SNR>10dB
    Correct for carrier frequency offset by applying the inverse offset to the transmitted samples
    Correct for sampling offset by applying a phase slope across the transmitted subcarriers and skipping or adding a guard time sample whenever the maximum phase slope exceeds 
    Hardware to do the above already is exactly the same as required to correct for carrier and sampling offset in an 11n receiver
Slide 4
Synchronization in Frequency
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 4

## Slide 5
Clients may need to apply some power correction provided by the AP such that they are received at some maximum SNR at the AP
Far-away users that cannot meet the maximum SNR can still participate in UL-SDMA but at a lower MCS
Clients that are too strong or too weak may be excluded from UL-SDMA by AP
Slide 5
Uplink Power Differences
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 5

## Slide 6
For both power and synchronization, only relative differences between uplink clients are relevant
Absolute power, frequency and timing errors do not cause problems
  AP receiver can correct for average received power, frequency, and timing
  Differential errors remain
Slide 6
Differential Accuracy
Slide 6
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 6

## Slide 7
Channel training
  AP needs to train up to 8 spatial streams based on VHT-LTFs in the uplink preambles from up to 8 clients
MIMO decoding
  Decoding complexity similar to SU-MIMO
    Maximum number of spatial streams up to 8
Pilot tracking
  UL common phase estimation performed on a per-client basis
    accounts for different phase noise and residual frequency error per client
    No change to pilot tone allocation required
    AP can perform an MMSE on the pilot subcarriers to get per-user estimates
Per user decoding, deinterleaving and descrambling
Slide 7
Changes in AP Processing
Slide 7
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 7

## Slide 8
Simulated 6 single stream clients where half of the clients have x/2 kHz offset relative to the AP, while the other half has a –x/2 kHz offset relative to the AP
Slide 8
Uplink Frequency Differences Simulation
Slide 8
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 8

## Slide 9
8 AP antennas, 6 single stream uplink clients
MMSE with ideal training but with pilot phase tracking per client
1000B packets, 64-QAM, rate 5/6, channel D-NLOS
Frequency errors are a) 0, b) 2 kHz, c) 4 kHz, d) 8 kHz
Slide 9
Uplink Frequency Differences
Slide 9
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 9

## Slide 10
Simulated 6 single stream clients where half of the clients have x ns extra delay relative to the other half
Slide 10
Uplink Timing Differences Simulation
Slide 10
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 10

## Slide 11
Overall TX&RX filter response modelled as a 10th order Butterworth filter with single-sided bandwidth of 18.125 MHz
Response length is about 300 ns when looking at the -40dB point relative to the peak
Slide 11
Overall Filter Response
Slide 11
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 11

## Slide 12
8 AP antennas, 6 single stream uplink clients
MMSE with ideal training
1000B packets, 64-QAM, rate 5/6, channel D-NLOS
Timing differences are a) 0, b) 200ns, c) 400ns, d) 600 ns
Slide 12
Uplink Timing Differences With Filtering
Slide 12
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 12

## Slide 13
Ran uplink SDMA simulations with a -40dBc SSB suppression at AP RX
SSB suppression or any other nonlinear distortion causes cross-products of strong and weak uplink users that limit the tolerable power differences
Simulated 6 single stream clients where half of the clients are x dB weaker than the other half
Look at PER of the weaker clients only to get the worst case performance metric
Slide 13
Uplink Power Differences Simulation
Slide 13
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 13

## Slide 14
8 AP antennas, 6 single stream uplink clients
MMSE with ideal training
PER and SNR shown are from the clients with smallest power
1000B packets, 64-QAM, rate 5/6, channel D-NLOS
AP receiver has a -40 dBc I/Q imbalance
Power differences are a) 0, b) 4 dB, c) 6 dB, d) 8 dB
Slide 14
Uplink Power Differences with -40 dBc Nonlinearity at RX, Highest Rate
Slide 14
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 14

## Slide 15
8 AP antennas, 6 single stream uplink clients
MMSE with ideal training
PER and SNR shown are from the clients with smallest power
1000B packets, BPSK, rate 1/2, channel D-NLOS
AP receiver has a -40 dBc I/Q imbalance
Power differences are a) 0, b) 6 dB, c) 12 dB, d) 18 dB, e) 24 dB
Slide 15
Uplink Power Differences with -40 dBc Nonlinearity at RX, Lowest Rate
Slide 15
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 15

## Slide 16
With long guard interval, timing differences between uplink clients can be in the order of 400 ns
  This is consistent with the fact that short GI works well in practice, hence long GI has 400 ns excess delay
Frequency differences between uplink clients can be in the order of 4 kHz
Power differences between uplink clients can be about 6 dB for highest rates and much more for lower rates
Conclusions (1)

## Slide 17
Implementation complexity of UL-MU-MIMO seems reasonable for both AP and client
  Main impact is for AP that has to build MIMO decoding for more than 4 streams
  Above needs to be done anyway if 11ac includes SU-MIMO for more than 4 streams
Notice UL-MU-MIMO does not require CSI feedback
  In this respect it is actually simpler than DL-MU-MIMO or single user beamforming
Slide 17
Conclusions (2)
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 17