## Slide 1
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Authors:
Radio Resource Measurement Type and Procedure for TVWS application under FCC rules
Date: 2010-02-24

## Slide 2: Motivation
According to FCC rule, all devices to be used for TVWS must have sensing capability.
The 802.11 WLAN devices inherently embrace sensing capability for media access purpose.
The sensing capability of the 802.11 WLAN devices should be extended/modified to suite the TVWS domain.

## Slide 3: Summary
Part I
  Measurement Type
Part II
  Measurement Procedure

## Slide 4: Wireless LAN Radio Measurements
WLAN Radio Measurements (RM) enable STAs to understand their radio environment
It enables to observe and gather data on radio link performance and on the radio environment
A STA may request, or provide RM data
RM data is made available to STA management and upper protocol layers for a number of application

## Slide 5: Logical service interfaces
Authentication
Association
Deauthentication
Disassociation
Distribution
Integration
Data confidentiality
Reassociation
MSDU delivery
DFS
TPC
Higher layer synchronization (QoS facility only)
QoS traffic scheduling (QoS facility only)
Radio measurement

## Slide 6: Station service (SS)
Authetication
Deauthentication
Data confidentiality
MSDU delivery
DFS
TPC
Higher layer timer synchronization (QoS facility only)
QoS traffic scheduling (QoS facility only)
Radio measurement

## Slide 7: Radio measurement service Extend the service for TVWS applicability
It provides the following
  The ability to request/report radio measurements.
  The ability to perform radio measurement
  The ability to identify presence of primary signals
  An interface for upper layer applications to retrieve radio measurements using MLME primitives and/or MIB access.
  Information about neighbor APs.

## Slide 8: Radio Resource Measurement Service
Radio Resource Measurement Service (RRMS) includes measurements that extent the capability, reliability, and maintainability of WLANs
The request/report measurements are:
  Beacon -Location Configuration Information
  Frame -Neighbor Report
  Channel Load -Link Measurement
  Primary Signal Identification –Transmit Stream /Category measuremt.
  Noise Histogram
  STA Statistics

## Slide 9: Request-only mechanism and Report only mechanism
Request-only mechanism
  Measurement Pause: permits inclusion of quantified delay b/n execution of measurements .
Report-only mechanism
  Measurement pilot:
  Primary Signal Identification (triggered and non-triggered)
The measurement mechanism in general is the first step in making WLAN smart and capable of appropriate decisions.

## Slide 10: Channel load and Noise histogram
The channel load request/report pair returns the channel utilization measurement as observed by the measuring station
The noise histogram request/report pair returns a power histogram measurement of non 802.11 noise power by sampling the channel when virtual carrier sense indicates idle and the STA neither transmitting or receiving.
Note: The above measurements may provide an indication to the presence of signal in general (which could be either secondary or primary signal) in the measured channel.

## Slide 11: Measurement type definitions for measurement requests/reports
Basic request/report
Clear Channel assessment (CCA) request/report
Received power ind.(RPI) histogram request/report
Channel load request/report
Noise histogram request/report
Beacon request/report
STA statistics request/report
LCI request/report
Transmit stream/category measurement request/report
Reserved
Measurement pause request
For spectrum
management
For radio resource
measurement

## Slide 12: Remark
For TVWS use, once the “Received Power Indicator”, “Channel load” or “Noise Histogram” indicates presence of signal, signal identification should follow to determine if it is primary signal or not.
In the event of successful primary signal detection FCC rule requires immediate evacuation of the channel.
  Requires
  dot11RRMPrimarySignalIdentificationEnabled=true
  dot11RRMNoiseHistogramMeasurementEnabled=true

## Slide 13: Proposal
Include
  Primary Signal Identification as one measurement type to be supported by the dot11 radio measurement service.
Note: the actual algorithms to be used for primary signal identification is out of the scope of 802.11af draft standard.

## Slide 14: Signal identification request frame format
Information element | Regulatory Class | Channel Number | Measurement Duration | Identification level | Reporting Condition
Octets | 1 | 1 | 2 | 1 | 1
Identification level | Description
0 | Report of the signal identification consists “one” if the signal detected is a primary signal according to the primary signal class information, otherwise “0” is reported
1 | Report of the signal identification consists signal type information as shown in the signal type table in addition to “identification level 0” information
2 | Report of the signal identification consists of only signal type information as shown in the signal type table
Reserved | 3-255
Identification level descriptions for signal identification
request

## Slide 15: Signal identification report frame format
Information element | Regulatory Class | Channel Number | Measurement Start time | Measurement Duration | Signal Identification | Optional Subelements
Octets | 1 | 1 | 8 | 2 | 2 | variable
It is implicitly assumed that signal identification follows channel load measurement
The channel load measurement reporting condition information element is reused in the frame format of the signal identification request
The measurement start time is assumed immediately after channel load measurement is finished.

## Slide 16: Primary signal class information
Primary Signal ID (country A) | Frequency MHz | Service type | Modulation | Restriction | Additional Information
1 |  | TV broadcast |  |  | 
The primary signal class information is intended to provide minimum profile of primary signals at a specific place.
Alternatively, primary signal class information could be included in the country information and country regulatory class.

## Slide 17: Signal Type
Type | Description | Remark
0 | Unknown | Unknown is selected if the STA couldn’t determine valid signal type
1 | Compound | If the STA detects a signal too complex to describe by a single parameter
2 | Noise | Is selected if the STA detects structured noise (colored) but couldn’t determine the underlying signal type (e.g. due to low power level)
3 | Single carrier | 
4 | Multicarrier | 
Reserved |  | 

## Slide 18: RRM Enabled Capabilities definition
Table 7-43e 802.11k
  Include a new capability as follows
Bit position in the RRM Enabled Capabilities field | Field name | Notes
31 | Primary Signal Identification Capability enabled | A STA sets Signal Identification Measurement capability enabled bit to 1 when the MIB attribute dot11RRMPrimarySignalIdentificationEnabled is true and sets it to 0 otherwise

## Slide 19: Part II Radio Resource Measurement Procedures

## Slide 20: Outline
On Request Reporting
Triggered Autonomous Reporting
Non-Triggered Autonomous measurement

## Slide 21: On Request Measurement
Signal Identification Report
  If dot11RRMPrimarySignalIdentificationEnabled is true, and a station accepts a Primary Signal Identification measurement Request,
    it shall respond with a primary signal identification measurement report frame with one or more measurement report elements

## Slide 22: Non-triggered Autonomous Measurement
This measurement scheme is a mandatory measurement to
  Perform measurement on operational channel a fixed interval according to regulatory requirement .
  Perform measurement on non-operational channel for a given duration according to regulatory requirement before such channels are classified as backup channels.
It allows a client STA to report the results of measurements to Master STA (AP) for which there was no explicit measurement request.
The measurement should contain Signal Identification measurement
The reporting mechanism is triggered by successful detection of primary signal (incumbent signal)

## Slide 23: Triggered Autonomous Reporting
The triggered autonomous reporting is an existing procedure in 802.11k.
  The assumed trigger conditions are not sufficient enough for TVWS application.
  Triggered autonomous reporting is defined only for the Transmit Stream/Category measurement type

## Slide 24: Triggered Autonomous Reporting
This reporting scheme is a mandatory reporting scheme for TVWS application.
It allows a client STA to report the results of measurements to Master STA (AP) for which there was no explicit measurement request.
The measurement should contain Signal Identification measurement
The reporting mechanism is triggered by
  immediate detection of primary signal (incumbent signal)
  when a channel measurement for a duration of time as specified by regulation indicates the channel is not occupied by primary signal