## Slide 1
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Authors:
Radio Resource Measurement Type and Procedure for TVWS application under FCC rules
Date: 2010-02-24

## Slide 2: Motivation
According to FCC rule, all devices to be used for TVWS must have sensing capability.
In the event of successful primary signal detection FCC rule requires immediate evacuation of the channel.
The 802.11 WLAN devices inherently embrace sensing capability for media access purpose.
The sensing capability of the 802.11 WLAN devices should be extended/modified to suite the TVWS domain.

## Slide 3: Summary
Part I
  Measurement Type
    We propose a new measurement type to compliment existing measurement service in 802.11k and to suite TVWS domain
Part II
  Measurement Procedure
    We also propose corresponding procedure for the proposed measurement type request/report

## Slide 4: Part I Measurement Type

## Slide 5: Extend the service for TVWS applicability
It provides the following
  The ability to request/report radio measurements.
  The ability to perform radio measurement
  The ability to identify presence of primary signals
  An interface for upper layer applications to retrieve radio measurements using MLME primitives and/or MIB access.
  Information about neighbor APs.

## Slide 6: Background
In the event of successful primary signal detection FCC rule requires immediate evacuation of the channel.

## Slide 7: Proposal
Include
  Primary Signal Identification as one measurement type to be supported by the dot11 radio measurement service.
Note: the actual algorithms to be used for primary signal identification is out of the scope of 802.11af draft standard.

## Slide 8: Signal identification request frame format
Information element | Regulatory Class | Channel Number | Measurement Duration | Identification level | Reporting Condition
Octets | 1 | 1 | 2 | 1 | 1
Identification level | Description
0 | Report of the signal identification consists “one” if the signal detected is a primary signal according to the primary signal class information, otherwise “0” is reported
1 | Report of the signal identification consists signal type information as shown in the signal type table in addition to “identification level 0” information
2 | Report of the signal identification consists of only signal type information as shown in the signal type table
Reserved | 3-255
Identification level descriptions for signal identification
request

## Slide 9: Signal identification report frame format
Information element | Regulatory Class | Channel Number | Measurement Start time | Measurement Duration | Signal Identification | Optional Subelements
Octets | 1 | 1 | 8 | 2 | 2 | variable
It is implicitly assumed that signal identification follows channel load measurement
The channel load measurement reporting condition information element is reused in the frame format of the signal identification request
The measurement start time is assumed immediately after channel load measurement is finished.

## Slide 10: Primary signal class information
Primary Signal ID (country A) | Frequency MHz | Service type | Modulation | Restriction | Additional Information
1 |  | TV broadcast |  |  | 
The primary signal class information is intended to provide minimum profile of primary signals at a specific place.
Alternatively, primary signal class information could be included in the country information and country regulatory class.

## Slide 11: Signal Type
Type | Description | Remark
0 | Unknown | Unknown is selected if the STA couldn’t determine valid signal type
1 | Compound | If the STA detects a signal too complex to describe by a single parameter
2 | Noise | Is selected if the STA detects structured noise (colored) but couldn’t determine the underlying signal type (e.g. due to low power level)
3 | Single carrier | 
4 | Multicarrier | 
Reserved |  | 

## Slide 12: RRM Enabled Capabilities definition
Table 7-43e 802.11k
  Include a new capability as follows
Bit position in the RRM Enabled Capabilities field | Field name | Notes
31 | Primary Signal Identification Capability enabled | A STA sets Signal Identification Measurement capability enabled bit to 1 when the MIB attribute dot11RRMPrimarySignalIdentificationEnabled is true and sets it to 0 otherwise

## Slide 13: Part II Radio Resource Measurement Procedures

## Slide 14: Proposal
On Request Reporting
Triggered Autonomous Reporting
Non-Triggered Autonomous measurement

## Slide 15: On Request Measurement
Signal Identification Report
  If dot11RRMPrimarySignalIdentificationEnabled is true, and a station accepts a Primary Signal Identification measurement Request,
    it shall respond with a primary signal identification measurement report frame with one or more measurement report elements

## Slide 16: Non-triggered Autonomous Measurement
This measurement scheme is a mandatory measurement to
  Perform measurement on operational channel a fixed interval according to regulatory requirement .
  Perform measurement on non-operational channel for a given duration according to regulatory requirement before such channels are classified as backup channels.
It allows a client STA to report the results of measurements to Master STA (AP) for which there was no explicit measurement request.
The measurement should contain Signal Identification measurement
The reporting mechanism is triggered by successful detection of primary signal (incumbent signal)

## Slide 17: Triggered Autonomous Reporting
Triggered autonomous reporting for primary signal identification measurement is proposed as mandatory scheme for TVWS application.
The scheme allows a client STA to report the results of measurements to Master STA (AP) for which there was no explicit measurement request.
The reporting mechanism is triggered when
  1) a primary (incumbent) signal is detected
  2) a channel measurement for a duration of time as specified by regulation indicates the channel is not occupied by primary signal

## Slide 18: Conclusion
Measurement Type
    A new measurement type called primary signal identification is proposed
Measurement Procedure
    Three basic procedures namely, on-request measurement request/report, non-triggered autonomous measurement, triggered autonomous measurement reporting are proposed