## Slide 1: Performance evaluation of MU-RTS under OBSS environment
Date: 2010-11-08
Authors:
Name | Affiliations | Address | Phone | email
B. A. Hirantha Sithira Abeysekera | NTT | 1-1, Hikarino-oka, Yokosuka-shi, Japan | +81-46-859-8266 | hirantha.abeysekera@lab.ntt.co.jp
Shoko Shinohara | NTT | 1-1, Hikarino-oka, Yokosuka-shi, Japan | +81-46-859-5107 | shinohara.shoko@lab.ntt.co.jp
Yusuke Asai | NTT | 1-1, Hikarino-oka, Yokosuka-shi, Japan | +81-46-859-3494 | asai.yusuke@lab.ntt.co.jp
Yasuhiko Inoue | NTT | 1-1, Hikarino-oka, Yokosuka-shi, Japan | +81-46-859-5097 | inoue.yasuhiko@lab.ntt.co.jp
Takeo Ichikawa | NTT | 1-1, Hikarino-oka, Yokosuka-shi, Japan | +81-46-859-3079 | ichikawa.takeo@lab.ntt.co.jp
Masato Mizoguchi | NTT | 1-1, Hikarino-oka, Yokosuka-shi, Japan | +81-46-859-3758 | mizoguchi.masato@lab.ntt.co.jp
Philippe Christin | Orange lab | 4, rue du clos courtel 35512 Cesson-Sévigné | +33 2 99 12 47 93 | philippe.christin@orange-ftgroup.com
Laurent Cariou | Orange lab | 4, rue du clos courtel 35512 Cesson-Sévigné | +33 2 99 12 43 50 | laurent.cariou@orange-ftgroup.com

## Slide 2
Name | Affiliations | Address | Phone | email
Yuichi Morioka | Sony Europe Ltd. | Jays Close, Viables, Basingstoke, Hampshire, RG22 4SB, UK | +44 (0) 1256 828114 | Yuichi.Morioka@eu.sony.com
Ted R. Booth III | Sony Electronics Inc. | 16530 Via Esprillo Building 7, MZ7021 San Diego, CA 92127 | +1 858 942 8044 | ted.booth@am.sony.com
André Bourdoux | IMEC | Kapeldreef 75, 3001 Leuven, Belgium | +32-16-288.215 | bourdoux@imec.be

## Slide 3: Abstract
In this document, we first present some results of a statistical analysis of housing conditions in Japan, and show that more than 40% among all dwellings are the apartment houses.
Then, we show the numerical results of the number of OBSSs that can be happen in such an apartment environment.
Finally, we present simulation results of a simple OBSS scenario, and as an operator, we show the importance of a MAC protection mechanism for TGac.

## Slide 4: Statistical analysis for the number of OBSSs according to “Housing and Land Survey*” in Japan
The Japanese governmental survey shows:
  More than 40% houses are apartment houses (about 20 million in all of 49.6 million dwellings).
  The average area of floor space per dwelling in apartment house is about 520 ft2 (= 48 m2).
  About 75% apartment houses are made of reinforced steel-framed concrete.
Operators’ perspective:
  It is expected that 11ac standard will extend capacity of wireless home network which conveys network services (ex. on-demand video streaming services) to subscribers not only detached house but also apartment house users.
It is important to examine the wireless environment in apartment house users
*“Housing and Land Survey in 2008” done by
Statistics Bureau in Ministry of Internal Affairs and Communications, Japan. http://www.stat.go.jp/english/data/jyutaku/index.htm

## Slide 5: Statistical analysis for the number of OBSSs according to “Housing and Land Survey*” in Japan
Evaluation conditions:
  Ave. dimensions of each apartment*: W / L / H = 16.5 / 33 / 10 [ft]
  Tx power: 17 dBm@5GHz
  Power loss of room wall and floor [1]: 13 [dB]
  APs location: Each AP is placed at the center of each apartment house
  Carrier sense level (which is equal to interference threshold):
  -82dBm@20MHz / -79dBm@40MHz / -76dBm@80MHz / -73dBm@160MHz
Bandwidth expansion to more than 40MHz causes one or more OBSSs in above apartment environment.
  Some kinds of techniques to reduce the influence of OBSSs should be considered.
Bandwidth per channel | The # of interfering BSSs | The # of available channels | The # of OBSSs in expectation
20MHz | 12 | 19 | 0
40MHz | 10 | 9 | 0.22
80MHz | 10 | 4 | 1.75
160MHz | 10 | 2 | 4.50
(AP)
-56.33
-79.87
-48.72
-71.71
-93.53
-72.25
-89.20
-108.2
-91.42
-106.4
-123.2
Interference level [dBm] in each apartment because of the AP in the top left apartment**.
* Based on the “Housing and Land Survey, 2008.”
** IEEE 802.11n channel model B – Residential.

## Slide 6: OBSS issue
Consider frame transmissions using 80MHz (or 160 MHz) channel bandwidth.
  As shown in previous slide, OBSS is likely to happen due to lack of channels when using 80MHz (or 160MHz) bandwidth.
  This increases the frame collision probability at STAs which are placed in OBSS environment (especially, when APs are hidden to each other).
Moreover, TGac allows transmitting very large (up to 1 MB) A-MPDUs in one transmission attempt.
  Therefore, the duration of a frame transmission becomes longer (ex. 1MB/270Mbps = 30ms).
  This also may increase the frame collision probability especially at STAs in OBSS environment.

## Slide 7: TGac background
DL MU-MIMO, which allows simultaneous frame transmissions to different STAs, is a key feature in TGac.
Multi-RTS [2], Multiple CTSs [3] schemes (hereafter called MU-RTS scheme) were presented in September 2010 meeting, and showed qualitatively the importance of MAC protection mechanism [4] for TGac.
  Straw Poll results are summarised in page 3 of Ref. [5].
Even though OBSS scenarios are complicated [6], TGac agrees to see how 11ac devices behave in OBSS environment [7, 8].
  So far, however, not that much evaluation results were presented.
In next slides we show some OBSS simulation results.

## Slide 8: Simulation topology
2
1
3
4
3
1
2
4
AP-1
AP-2
BSS-2
BSS-1
Consider only downlink UDP traffic
Two overlapping BSSs
Each BSS consists of one AP and 4 STAs
All STAs hear signal of both AP-1 and AP-2
APs are hidden or non-hidden to each other
STAs can receive any frames correctly unless there
are collisions (bit errors caused by thermal noise or
channel fading are not considered)
MPDUs for each STA are generated at the corresponding
AP by i.i.d.
This figure illustrates the hidden AP case
(i.e., Case-1)
Case-1: APs are hidden
Case-2: APs are non-hidden

## Slide 9: Simulation topology
2
1
3
4
3
1
2
4
AP-1
AP-2
BSS-2
BSS-1
Consider only downlink UDP traffic
Two overlapping BSSs
Each BSS consists of one AP and 4 STAs
All STAs hear signal of both AP-1 and AP-2
APs are hidden or non-hidden to each other
STAs can receive any frames correctly unless there
are collisions (bit errors caused by thermal noise or
channel fading are not considered)
MPDUs for each STA are generated at the corresponding
AP by i.i.d.
This figure illustrates the non-hidden AP case
(i.e., Case-2)
Case-1: APs are hidden
Case-2: APs are non-hidden

## Slide 10: Parameter values
Parameter | Value
Bandwidth per channel | 80 [MHz]
The # of subcarrier per spatial stream | 216
MCS | 64QAM, 5/6
Data rate | 270 [Mbps]
Basic rate | 6 [Mbps]
The # of APs | 2
The # of STAs per AP | 4
The # of antennas per AP | 8
The # of antennas per STA | 2
The # of streams towards STA in a single transmission | 2
Parameter | Value
MU-RTS length | 37[B]=76 [usec]
CTS length | 14[B]=44 [usec]
BA length | 28[B]=52 [usec]
SIFS | 16 [usec]
DIFS | 34 [usec]
SlotTime | 9 [usec]
ACK timeout interval | 58 [usec]
MSDU size | 1,500 [B]
Max. A-MPDU size | 65,535 [B]
CWmin | 15
CWmax | 1,023
Retry Limit (Long, Short) | (4, 7)
Simulator: OPNET 15.0.A

## Slide 11: Frame sequence
AP
STA-1
STA-2
STA-N
SIFS
…
…
…
…
max (N) = 4
CTS
BA
CTS
BA
CTS
BA
DATA (AP STA-1)
DATA (AP STA-2)
MU-RTS
DATA (AP STA-N)
AP can transmit A-MPDUs to up to 4 STAs simultaneously using DL MU-MIMO technique.
Length of an A-MPDU depends on the current number of MSDUs buffered at the AP.
All BAs are scheduled and transmitted in the same order as CTSs.
When AP accesses to medium, it first transmits a MU-RTS [2, 3].
Each STA responds with a CTS frame if it is ready to receive DATA frame from the AP.

## Slide 12: Simulation results
non-hidden AP,
without MU-RTS
non-hidden AP,
with MU-RTS
hidden AP,
with MU-RTS
hidden AP,
without MU-RTS
250 Mbps
1100 Mbps
1400 Mbps
1200 Mbps

## Slide 13: Summary
We evaluate the performance of MU-RTS scheme.
MU-RTS scheme slightly degrades the system throughput when APs are known (non-hidden) to each other, because of the additional overhead due to MU-RTS and multiple CTSs.
When APs are hidden, MU-RTS greatly improves the system throughput.
Needs some sort of protection mechanism for TGac.
Frame sequences, Frame formats, and ACK mechanism (polled or scheduled) are TBD.

## Slide 14: References
[1] Rec. ITU-R P.1238-3, "Propagation data and prediction methods for the planning of indoor radio communication systems and radio local are networks in the frequency range 900MHz to 100GHz," ITU-R Recommendation P Series, 2003.
[2] Y. Morioka et al., “Multi-RTS Proposal,” Doc.: IEEE 802.11-10/1124r2.
[3] T. Kaibo et al., “Multiple CTSs in MU-MIMO Transmission,” Doc.: IEEE 802.11-10/1067r0.
[4] Y. J. Kim et al., “Considerations on MU-MIMO Protection in 11ac,” Doc.: IEEE 802.11-10/0335r1.
[5] B. Hart et al., “TGac MU-MIMO Ad Hoc Minutes,” Doc.: IEEE 802.11-10/1161r0.
[6] A. Ashley et al., “OBSS Requirements,” Doc.: IEEE 802.11-08/0944r7.
[7] Y. Takatori, “Importance of Overlapped BSS issue in 802.11ac,” Doc.: IEEE 802.11-09/0630r1.
[8] P. Loc et al., “TGac Functional Requirements and Evaluations Methodology Rev. 15,” Doc.: IEEE 802.11-09/0451r15.

## Slide 15: Thank you!