## Slide 1
Slide 1
White Space Map Notification
Date: 2011-01-04
Authors:

## Slide 2: Abstract
Contact Verification Signal Definition from FCC Rule
How to implement this regulation into IEEE 802.11af standard
  Propose WSM Contact verification as a Contact Verification Signal

## Slide 3: Contact Verification Signal from FCC rule (15.703 (b))
Definition and Requirements
  An encoded signal broadcast by a fixed or Mode II device
  For reception by Mode I devices to which the fixed or Mode II device has provided a list of available channels for operation
  It shall be encoded to ensure that the signal originates from the device that provided the list of available channels

## Slide 4: Contact Verification Signal from FCC rule (15.703 (b))
Purpose
  To establish that the Mode I device is still within the reception range of the fixed or Mode II device
  To validate the list of available channels used by the Mode I device

## Slide 5: Contact Verification Signal from FCC rule (15.703 (b))
Device Operation
  A Mode I device may respond only to a contact verification signal from the fixed or Mode II device that provided the list of available channels on which it operates.
  A fixed or Mode II device shall provide the information needed by a Mode I device to decode the contact verification signal at the same time it provides the list of available channels.

## Slide 6: WSM Notification as a CVS
WSM Notification element format
  Enabling STA Address : Address of Fixed or Mode II device that provided available channel list
  When a fixed or Mode II device provide a list of available channel list, it shall provide decoding information for decryption
  WSM Hash (WSMH) = HMAC-SHA1-64(“WSN”, WSM_Information), then truncated to the first 64 bits of this function.

## Slide 7: WSM Notification as a CVS
White Space Map Information
  Format of ‘WSM Information’ in current draft
  Only Channel Number and Maximum Power Level Pairs with increasing order are hashed
 | These two fields are repeated, as determined by the Length field | 
Map ID | Channel Number | Maximum Power Level
1 | 1 | 1

## Slide 8: WSM Notification as a CVS
WSM Notification frame format
 | Category | Public Action | WSM Notification IE
Octets: | 1 | 1 | 16

## Slide 9: WSM Notification as a CVS

## Slide 10: WSM Notification as a CVS

## Slide 11: Further Consideration
WSM Notification as a termination signal
  WSM Hash field may not be present when no channels are available, AP only transmit WSM Notification without WSM Hash field
  STA receiving WSM Notification indicating empty channel stop transmission in TV White Spaces
 | Element ID | Length | Enabling STA Address | WSM Hash (Optional)
Octets: | 1 | 1 | 6 | 8

## Slide 12: Further Consideration
STAs in Power Save Mode
  In order to receive WSM Notification Signals, STAs always have to stay awake if the delivery information has not been provided
  However, for the sake of battery power STAs usually go into sleep mode if the traffic is not busy
  STAs in sleep mode do not need to hear WSM Notification signals but when transition from sleep mode to active mode STAs needs to receive WSM Notification signal or transmit Channel Availability Query for WSM
  To reduce OTA traffics that request available channel list, it would be better to signal WSM Notification delivery information to STAs so that they can receive WSM Notification signal whenever they want even in sleep mode

## Slide 13: Remaining Works
Security protocol and procedure
  Enabling STA Address that provided a list of available channel list shall be securely encoded
  Security Key Exchange shall be exchanged during association or enablement
  Reuse of 11w security protocol that is able to encrypt management frame may be useful