## Slide 1: Use Case Scenario for TGai
Date: 2011-01-18
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Marc Emmelmann | Fraunhofer Fokus | Kaiserin-Augusta-Allee 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Hiroshi MANO | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Hiroki NAKANO | Trans New Technology | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-771-7630 | cas@trans-nt.com

## Slide 2: Abstract
This presentation shows an expected use case scenario for TGai.

## Slide 3: Use Cases for TGai
Hot-Spot Pass-Through
Train
Simultaneous channel switch of large user groups
Coupons Distribution
Toll / Weight Station Drive By

## Slide 4: Parameter Definition
Transmission range of AP [m]
User Velocity [m/s]
User Arrival Rate [users/s]
User Departure Rate [users/s]
Assuming equal

## Slide 5: Use Case 1: Hot-Spot Pass-Through: Overview
A user passes by (several, non overlapping) publicly accessible WiFi hot-spots (e.g. ATTwifi @ Starbucks)
While having connectivity, the user’s smart phone up-&downloads e-mails, twitter / facebook messages etc.
3/4G networks face a severe amount of non-voice traffic, hence such behavior (instead of using cellular 3/4G bandwidth) could also be encouraged by the user’s provider with a special subscription plan in order to release traffic from the 3/4G network
Other scenarios with similar characteristics:
  Passengers onboard a train pass trough a train station
  Unmanned Air Vehicle collecting surveillance data flies through a dedicated hot-spot for data download

## Slide 6: Use Case 1: Hot-Spot Pass-Through: Characteristics
Characteristic | Value
Transmission range of AP passed by [m] | 100 m
Users’ velocity [km/h] | 5 (walking) – 50 km/h
Dwell time in AP’s coverage [s] | 7 – 70 s
User arrival / departure rate [user / s] | 3 -- 50
User flux [user /s m^2] | 4.7 e-5 -- 7.9 e-4

## Slide 7: Use Case 2: Train: Overview
Onboard a train, WiFi service is provided to customers via a local AP. This AP uses a wireless, 802.11-based backbone to connect to track-side infrastructure.
Directional antenna are used to provide continuous coverage along the tracks
Note: Individual connectivity of users to track-side AP (e.g. at a train station) is covered by the Use Case 1.

## Slide 8: Use Case 2: Train: Characteristics
Characteristic | Value
Transmission range of AP passed by [m] | 500 -- 1000 m (using directional antennae)
Users’ velocity [km/h] | 400 km/h
Dwell time in AP’s coverage [s] | 4 -- 9 s
User arrival / departure rate [user / s] | 0.5 -- 2
User flux [user /s m^2] | 8 e-8 -- 1.3 e-6

## Slide 9: Use Case 3: Simultaneous channel switch of large user groups: Overview
A large number of users are connected to an AP.
A group of users is required to switch to another frequency or AP due to
  Load balancing between APs in the area
  Detected interference or regulatory requirements force to switch to another frequency band
As a result, a large number of users simultaneously (re-)establish a link

## Slide 10: Use Case 3: Simultaneous channel switch of large user groups: Characteristics
Characteristic | Value
Transmission range of AP passed by [m] | 5 – 10 m
Users’ velocity [km/h] | 2 – 5 km/h
Dwell time in AP’s coverage [s] | 3.6 – 18 s
User arrival / departure rate [user / s] | 1 -- 300
User flux [user /s m^2] | 1.6 e-3 – 2.5 e-1

## Slide 11: Use Case 4: Coupons Distribution: Overview
A user passes through in front of a shop or a digital signage.
The user can get a couple of discount coupons and may connect to the Internet.
A shop or a digital signage can identify the user.
They can give him/her adaptive advertisement and coupons.

## Slide 12: Use Case 4: Coupons Distribution: Characteristics
Characteristic | Value
Transmission range of AP passed by [m] | 20 -- 30 m
Users’ velocity [km/h] | 5 – 50 km/h
Dwell time in AP’s coverage [s] | 1.5 – 6 s
User arrival / departure rate [user / s] | 7 -- 70
User flux [user /s m^2] | 2.5e-3 – 5.6e-2

## Slide 13: Use Case 5: Toll / Weight Station Drive By: Overview
A car or a truck on a highway drives through a toll station or passes by a weight station
While driving by (or being weighted) information such as billing the customer with tolls or exchange of freight information is necessary
Enabling applications build upon standard IP protocol suite and potentially trust in the underlying wireless technology to establish a secure link
Communication devices are expected to be on-board the vehicle

## Slide 14: Use Case 5: Toll / Weight Station Drive By: Characteristics
Characteristic | Value
Transmission range of AP passed by [m] | 100 -- 200 m
Users’ velocity [km/h] | 60 – 120 km/h
Dwell time in AP’s coverage [s] | 3 – 12 s
User arrival / departure rate [user / s] | < 10
User flux [user /s m^2] | 4 e-5 -- 1.5 e-4

## Slide 15: Scenarios

## Slide 16: Expected User
Hiroshi is a businessperson living in Tokyo, Japan.
He uses e-mail, Twitter and many other internet services with his smart phone supporting WLAN.
He wants to update his e-mail, Twitter timeline and flight information as possible as often.
He prefers to access to the Internet by WLAN rather than 3G because of cost, speed and battery life.

## Slide 17: Scenario : Travel (from office to station) TGai
He travels to a city for his business. The city locates 300km away from his office. He goes there by train and car.
He updates information in his home by his own private AP with TGai before departing his home.
He walks to the station. There are several APs along the street. Some of them are operated by an commercial ISP (ISP-A) and he has an account to access them. When he walk through the AP cover area, his smart phone automatically trys to connect to the Internet by TGai and updates information. It can smoothly connect and update update information because of short latency for connection by TGai. (Use Case 1)
He walks in front of a digital signage with an AP for distributing coupons and he is a registered user of the AP. When his smart phone connects to the AP, the signage identifies him. The signage displays a couple of advertisement which matches his preferences and gives him a couple of coupons for discount. (Use Case 1 and 4)

## Slide 18: Scenario : Travel (On train) TGai
He arrives at the station. The station is very crowded by passengers. Here are some APs which are operated by ISP-B and available for roaming to ISP-A. His smart phone automatically trys to connect to the AP with the account of ISP-A. It can smoothly connect and update information because of small air time occupancy of TGai. So he can check updated information on the train. (Use Case 1 and 3)
He gets on a express train. The train has APs for passengers to connect to the Internet. And an STA is also installed on the train for connection between the train and rail-side APs. The train is always connected to the Internet by these STA and APs, and the passengers can connect to the Internet via the internal APs. So he can check the newest information even in the train. (Use Case 2)
He gets off the train and transfer to another express train which does not have APs. The train passes through some stations. ISP-B operates APs at all stations along the route. When the train is passing a station, his smart phone trys to connect to a AP at the station. It can smoothly connect and update information because of short connection latency of TGai. So he can check the newest information even in the train without APs. (Use Case 1)
He gets off the train and arrives the station. His smart phone connects and updates information. (Use Case 1 and 3)

## Slide 19: Scenario: Commute (On a car) TGai
He rents a car and drives to the destination. There are some APs operated by ISP-C along the road. ISP-C doesn’t have roaming agreement with ISP-A. But he also has an account for ISP-C. His smart phone can smoothly connect and update information. (Use Case 1)
He drives onto the toll expressway. The toll gate has an AP to collect the toll. When he drive through the toll gate, his smart phone automatically connects to the AP at the gate and pays the toll. (Use Case 5)
He drives off the expressway and arrives the destination.
He is so happy because he can always update information on his way from home to the office.

## Slide 20: Questions & Comments