## Slide 1: VHT Supported MCS Field
Date: 2011-01-17
Authors:

## Slide 2: Abstract
This document proposes a design of the VHT Supported MCS Set Field of the VHT Capabilities element

## Slide 3: Introduction
Goal is to design “The Supported MCS Set field” that indicates which MCSs a STA supports
  Different from 11n
    In 11n, an MCS was identified by an MCS index, which was represented by an integer in the range 0 to 76 (included the different Nss possibilities)
    In 11ac, MCS and Nss are disjoint quantities
  Aim to reduce the number of options available and remove possibility of “holes” in supported MCS table
    Cleans up the standard and rate adaptation
Assumptions
  Transmit and receive support for MCS 0 through 7 in all the supported (BW, Nss) combinations unless
    It is a restricted MCS
    Data rate cut-off of a device forbids such a support (only allowed in highest BW)
  Allowance for optional modes
    Support of MCSs 8 and 9
    Support for more than 1 spatial stream.

## Slide 4: Proposed Contents of VHT Supported MCS field
Rx MCS Map
  This consists of a 16 bit field which specifies max MCS supported for every Nss
    2 bit number for each Nss value
      00 will denote support for up to MCS 7
      01 will denote support for up to MCS 8
      10 will denote support for up to MCS 9
      11 will denote no support for that Nss
Rx Highest Supported Data Rate
  This field is needed to place a limit on the max data rate (13 bits)
    In units of Mb/s where 1 represents 1 Mb/s, and incrementing in steps of 1 Mb/s
  This cutoff can over-ride a claim for support of a certain (MCS, Nss) combination for the highest supported BW
Rx MCS map

## Slide 5: Proposed Contents of VHT Supported MCS field
Tx MCS Set Defined
  1 bit specifying whether the Tx is advertising its MCS capability or not
  Subsequent fields on this slide are irrelevant if this bit is set to 0
  When set to 1
    Subsequent fields help the STA in choosing a more powerful AP or an AP more commensurate with its own capability
Tx MCS Map
  Exactly same as Rx MCS map defined in slide 3
Tx Highest Supported Data Rate
  This field is needed to advertise the max data rate a device can transmit (13 bits)
    In units of Mb/s where 1 represents 1 Mb/s, and incrementing in steps of 1 Mb/s
  This cutoff can over-ride a claim for support of a certain (MCS, Nss) combination for the highest BW

## Slide 6: Frame Format: VHT Supported MCS
Proposed frame format for the VHT Supported MCS field

## Slide 7: Conclusion
We proposed a simple way to convey the supported MCS set for 11ac

## Slide 8: Pre-motion
Do you agree with the VHT Supported MCS Set Field proposed in this presentation and agree to add it to the spec framework document ?

## Slide 9: References
        [1] IEEE 802.11 document 09/0992r18 , “Proposed Specification Framework for TGac”, Robert Stacey et al