## Slide 1: VHT Control and Link Adaptation
Date: 2011-01-18
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: HT control field in spec framework
Spec framework document defines a VHT link adaptation, MCS feedback, by enhancing the HT control field design
In VHT, most of the HT indications are not used
  TRQ: Not Needed (VHT supports explicit FB only)
  Calibration Position: Not Needed (VHT supports explicit FB only)
  Calibration Sequence: Not Needed (VHT supports explicit FB only)
  CSI/Steering: Not Needed
  NDPA: Not Needed (VHT supports explicit NDPA Frame)

## Slide 3: VHT Control field
We propose to define a completely new VHT Control field
  Use 1 bit in HTC to indicate that frame is VHT
  Redefine the meaning of all remaining bits
We propose to use B0 of HT Control field (reserved) to indicate
  B0 = 0: field is HT Control
  B0 = 1: field is VHT Control
Remainder of this presentation defines the frame format for the case of B0=1, i.e. when the frame is VHT

## Slide 4: Summary of Link Adaptation proposal
We propose to augment the Link Adaptation feedback for VHT by adding an SNR indication (MCS and NSTS are kept as well)
  Please refer to slide 5 for the details
We propose to keep both the Solicited and Unsolicited Link Adaptation
Solicited Link Adaptation is kept similar to the one defined in 802.11n
  Details of proposed new design are provided in slides 6
For the unsolicited case: we propose to enhance the frame format by including indications that allow to identify the type of PPDU from which the MCS, NSTS and SNR are estimated (see slide 7 for details)
  GID (allows also to identify SU/MU)
  Beamformed/non-beamformed,
  Coding type (BCC/LDPC),

## Slide 5: Feedback
Proposed feedback includes the following fields
  MFB (15bits), which includes
    MCS (4 bits): indicates the suggested VHT MCS index
    NSTS(3 bits): indicates the suggested VHT Nsts value
    SNR (8 bits): indicates the estimated SNR value
MCS and NSTS computation is implementation dependent
Note: SNR provides additional information on the link quality
  Rx does not know what the Tx power per each MCS will be and whether the sender will apply optional modes such as STBC, LDPC, TxBF, or other proprietary technology.
  SNR offers useful information for the transmitter to make a better choice
  Please refer to [1] for further details on SNR definition

## Slide 6: Solicited behavior
Request is indicated by a MRQ field (1bit) and identified by a MSI (3 bits)
  The requester may set the MRQ field to 1 in the VHT Control field of a +VHTC frame to request a STA to provide feedback
  Requester chooses an (arbitrary) MSI that identifies the request
Response carries MCS, NSTS, SNR and a sequence indication MFSI which matches the sequence indication of the request (MSI)
  Note: Allows to track the PPDU from which the feedback is computed
Feedback is computed based on the requesting PPDU; If the requesting PPDU is an NDPA, feedback is computed based on following NDP
MCS and Nsts computations in implementation dependent; SNR is TBD [1]
  [Nsts, MCS] = 127 indicates that feedback is not provided (as in 11n)
  The NSTS shall not exceed the requester MCS capabilities

## Slide 7: Unsolicited behavior
In the unsolicited case the feedback is computed based on the most recent PPDU received, that matches the description provided by the (newly defined) fields present in the same VHT Control field
  Coding Type: indicates either BCC or LDPC
  GID: indicates the Group ID, which also allows to determine if PPDU was SU or MU
  FB TX Type: either Beamformed or non-Beamformed

## Slide 8: Proposed frame format
The proposed VHT frame format which hosts the fields described in the previous slides, is the following one
B0 | B1 | B2 | B3-B5 | B6-B8 | B9-B11 | B12-B15 | B16-B23
HT/ VHT | Solicited/ Unsolicited | MRQ | MSI | MFSI/ GID-L | Nsts | MCS | SNR
1 | 1 | 1 | 3 | 3 | 3 | 4 | 8
B24-B26 | B27 | B28 | B29 | B30 | B31
GID-H | Coding Type | FB TX Type | Reserved | AC Constraint | RDG/More PPDU
3 | 1 | 1 | 1 | 1 | 1
MFB

## Slide 9: Details of VHTC bit field
Solicited/Unsolicited (B1)
  0: Solicited link adaptation
  1: Unsolicited link adaptation
MRQ (B2)
  0: non-request
  1: MFB request frame
MSI (B3-B5)
  If MRQ=1: sequence number in the range 0 to 6 that identifies the specific request; value of 7 is reserved
  If MRQ=0: reserved
MFB (B9~B23)
  NSTS (3bits):suggested number of spatial streams
  MCS (4bits): suggested VHT MCS
  SNR (8 bits): estimated SNR

## Slide 10: Details of VHTC bit field
In case B1 = 0 (solicited MFB)
  B6-B8 define the MFSI field: Set to the received value of MSI contained in the frame to which the MFB information refers; value of 7 is reserved
  B24 -B29 are reserved
In case B1 = 1 (unsolicited MFB)
  B6-B8 are defined as the LSBs of the GID field (GID-L)
  B24-B26 are defined as the MSBs of the GID field (GID-H)
  The GID field is set equal to the GID of the corresponding frame
  Coding Type (B27):
    0:BCC; 1:LDPC
  FB Tx Type (B28)
    0 : Un-beamformed, TxD (Alamouti), Open Loop; 1 : Beamformed
  B29 is reserved

## Slide 11: Details of VHTC bit field
B30: AC constraint
  As in HT Control (11n)
B31: RDG/More PPDU
  As in HT Control (11n)

## Slide 12: Pre-motion 1
Do you accept to update the spec framework document with
  The bit B0 in HT Control field is defined as ‘HT/VHT’ field and indicates:
    B0 = 0: field is HT Control
    B0 = 1: field is VHT Control
  If B0 = 1, B1-B31 are TBD

## Slide 13: Pre-motion 2
Do you support to update the spec framework document with the VHTC frame and Link Adaptation design as described in slides 5 to 11 of document IEEE 802.11-11/0040r0 (excluding the Notes)?

## Slide 14: References
[1] VHT Link Adaptations: doc.:IEEE 802.11-11/0047r0

## Slide 15: Feedback
SNR
  The SNR feedback in VHT Control Field is defined as the SNR value averaged over all the spatial streams and data subcarriers, and is encoded to 8 bits two’s complement number as below [1]: where is the SNR value measured in dB at the k-th tone and iSTS-th space-time stream, and is the feedback SNR value before the 8-bit quantization. The MFB requester may use either MFB, or SNR feedback, or both to compute the appropriate MCS and NSTS.