## Slide 1: Use Case Ref List Doc Discussion
Date: 2011-03-12
Authors:

## Slide 2: Abstract
This slide set is to be used as a vehicle to discuss form and content of 11-11-0238-03-00ai-Use-Case-Reference-List-for-TGai.docx
Changes / directions discussed in Monday PM1 meeting of TGai are in red

## Slide 3: Introductory Text
IEEE 802.11 devices are increasingly becoming more mobile devices. TGai project’s primary need comes from an environment where a large number of mobile users are constantly entering and leaving the coverage area of an access point (AP) in an extended service set (ESS). Every time the mobile device enters an ESS, the mobile device has to do an initial set-up to establish wireless local area network (LAN) connectivity. This works well when the number of new stations (STAs) in a given time period is small. It requires efficient mechanisms that scales well when a high number of users simultaneously enter an ESS. This requires the ESS to minimize the time the STAs spend in initial link setup, while maintaining secure authentication.

## Slide 4: Text to be added to Intro
Discussion of pre-knowledge needs to be added: e.g. a database downloaded that might give clues to know which channels are available or different secure ID scheme. Shortcut to authentication (perhaps pre-cached credentials). [ACTION ITEM TO ASSIGN TEXT WRITING]
Need to clarify purpose of document 0238 in the introduction.
  The general purpose is to establish small set reference use cases for the purpose of evaluating proposals to TGai. The methodology for this is to:
  Gather all use cases and group them into categories of similar traits
  Characterize specific requirements of each use case
  Combine use cases which have the same requirements
Also need to clarify that the “requirements” specified are NOT for the proposals, they are what is required to satisfy the particular use case

## Slide 5: TOC
1 Introduction 3
2 Use Cases 4
3 Use case categories 6
3.1 Pedestrian 6
  3.1.1 Electronic Payment 6
  3.1.2 Traveler Information 6
  3.1.3 Internet Access 7
  3.1.4 Mobile Accessible Pedestrian Signal System 7
3.2 Vehicle 7
  3.2.1 Electronic Payment 7
  3.2.2 Traveler Information 8
  3.2.3 Internet Access 9
  3.2.4 Emergency Services 9
  3.2.5 Inspections 10
  3.2.6 Resource Management 11
3.3 Mass Transit 12
  3.3.1 Station arrival 12
  3.3.2 Passenger In-transit access 12
  3.3.3 Station Lobby 12
  3.3.4 Connection Protection 12
  3.3.5 Dynamic Transit Operations 12
3.4 Switchover 13
Alternate classification scheme was discussed in the Monday PM session. Submissions for alternate schemes were requested.

## Slide 6: Pedestrian Use Cases
3.1.1 Electronic Payment
3.1.2 Traveler Information
3.1.3 Internet Access
3.1.4 Mobile Accessible Pedestrian Signal System

## Slide 7: Vehicle Use Cases
3.2.1 Electronic Payment
3.2.2 Traveler Information
3.2.3 Internet Access
3.2.4 Emergency Services
3.2.5 Inspections
3.2.6 Resource Management

## Slide 8: Transit Use Cases
3.3.1 Station arrival
3.3.2 Passenger In-transit access
3.3.3 Station Lobby
3.3.4 Connection Protection
3.3.5 Dynamic Transit Operations

## Slide 9: Switchover Use Case
[text needed]

## Slide 10: References
11-11-0238-03-00ai-Use-Case-Reference-List-for-TGai.docx
11-11-0281-00-00ai-proposed-dynamic-mobility-use-cases-for-tgai.docx
11-11-0148-05-00ai-use-cases-for-tgai.docx