## Slide 1: Use Case: Network Mobility
Date: 2011-05-02
Authors:
Name | Affiliations | Address | Phone | email
Jihyun Lee | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1860 | Jihyun1220.lee@lge.com
Eunsun Kim |  |  |  | 
Yongho Seok |  |  |  | 

## Slide 2: Abstract
This presentation shows an expected use case for TGai

## Slide 3: Use case: transit
3.3.1 Station arrival
  Link setup between passengers to AP at a station
  A train with no Wifi
3.3.2 Passengers in-transit access
  Link setup between passengers to mobile AP
  Passengers to fixed AP is not considered
3.3.5 Dynamic transit operations
  Either passenger to fixed AP or mobile router to fixed AP
  Train V2I Access
    Link setup between mobile router to infrastructure, e.g. AP on roadside

## Slide 4: Use case: network mobility
We suggest 3.3.5 to include “network mobility”
  Which may include access to an AP from
    Mobile AP(or router) on board
    STAs on board/in transit
  None of transit use cases covers network mobility
    It is more likely that a train will provide Wi-fi connection to its passengers, equipped with mobile AP
    Link setup from mobile AP to fixed AP
      Backhaul link transition (e.g. 3G to WLAN handover or handover from another fixed AP roadside)
      No backhaul link to fixed AP (e.g. VOD storage update through WLAN)
    Unlike the other use cases, it may require a means to differentiate a link between a mobile AP and a fixed AP from the one between a non-AP STA and a fixed AP

## Slide 5: Use case: network mobility
Fixed AP
Waiting area
Train
Train
Passengers
Rail or subway tunnel
Mobile AP
Rail or subway tunnel

## Slide 6: Use case scenario
Scenario
  Network standing for a short period of time (e.g. transit)
    Passengers connect to a mobile AP on train whilst travelling. The mobile AP may provide internet access to the passengers via backhaul connection. The train makes a quick stop at a station. On arrival, the mobile AP on train, the passengers whom have been served by the mobile AP including those taking off at the station and possibly passengers waiting on platform including those getting on the train at the station want to establish a connection to an AP mounted at the station simultaneously.
  Network moving through (e.g. vehicle)
    A group of passengers on a bus may have access to the internet via AP on board. When the bus drives through available coverage of a fixed AP on roadside, the AP and the passengers on-board want to establish a connection to the fixed AP.

## Slide 7: Use case traits
Traits
Summary
  FILS enables the use case
Impact
  High
Traits | Expected Value | Difficulty designation
Link-Attempt Rate | More than 50 | High
Media Load | More than 50% | High
Coverage Interval | More than 2 sec | Low to medium
Link Setup Time | Less than 100ms | High