## Slide 1: Supporting Large Number of STAs in 802.11ah
Date: 2011-05-09
Authors:

## Slide 2: Summary
A 802.11 ah network must support up to 6000 STAs
  Smart Grid, long range data collection and monitoring system
Current 8a02.11 MAC/PHY specification has to be modified in order to accommodate this large number of STAs
  Desirable to minimizes the degree of changes from the baseline spec
Issues
  AID
    The current AID field has 14 bits but is limited to 2007 STAs only
  Authentication and Association issue
  Channel resource allocation for data communication
    CCA centric approach has severe performance limitations

## Slide 3: Number of AIDs
Does the current specification support 6000 STAs?
  The AID field has 14 bits but the number of AIDs is limited to 2007
    From Clause 8.4.1.8 of 802.11mb-D8 [7.3.1.8 of 802.11-2007]
      The value assigned as the AID is in the range 1–2007 and is placed in the 14 LSBs of the AID field, with the two MSBs of the AID field set to 1 (see 8.2.4.2 (Duration/ID field)). 2008-12768 (reserved)
        From 8.2.4.2: a) In control frames of subtype PS-Poll, the Duration/ID field carries the association identifier (AID) of the STA that transmitted the frame in the 14 least significant bits (LSB), and the 2 most significant abits (MSB) both set to 1. The value of the AID is in the range 1–2007.
  Proposal
    TGah use one of two reserve bits to accommodate 6000 STAs
    A Proposal for addressing the PS-Poll DTIM issue is outlined in Slides 7.
    A Proposal for addressing the Upstream transmission issue is outlined in Slides 6, and 7.

## Slide 4: Authentication and Association
For TGah, the amount of time (association time) it will take for an STA to join a BSS is an important performance metric
  It is preferred to define an upper bound for the association time of a STA
  The association time determines the BSS set up time which is the duration from AP power up till 95% (TBD) of STAs join the network
The current Authentication and Association is based on contention access process
  The AP must be able to manage association time of an STA under the maximum network load
  Current channel access protocol with a adaptive scheduler design should be capable of allocating CBP and TXOP adaptively according to the load capacity in order to meet the association time
Notes: It

## Slide 5: Data Communication
For applications supporting 6000 STAs, the data communication is mostly uplink only
  The inter STAs communication is still supported by the 802.11 MAC/PHY specification
A CCA centric process will not work
  A coordinated process is essential to guarantee that all STAs can send uplink traffic regularly
    AP sends a pre-assigned resource allocation scheduling information to STAs at least once in every (TBD) beacon periods
    An STA transmits data to AP according to the scheduled time
MAC/PHY specification change required
  Current 802.11 specification does not have a mechanism supporting scheduled uplink data transmission
    The DTIM is used for downlink data transmission only and there is no actual scheduling information

## Slide 6: Proposals: Data Communication
How to indicate who can transmit data to AP?
  Option 1: modify the definition of DTIM to support both uplink and down link data transmission
    Will have to change the baseline behavior which will create more issue and is not preferred
  Option 2: Introduce a new element UTIM, Upstream Traffic Indication MAP
    A new element will not affect baseline behavior
How to indicate orders/time of upstream transmission for each STA
  Uplink DTIM/DRIM message will have to carry uplink scheduling information by either explicitly spelling out the time slot for each STA transmission or the STAs need to figure out the time slot according to an offset from a fixed point.

## Slide 7: Proposals: Data Communication
How to deal with 6000 STAs with existing DTIM?
  Must modify the MAC protocol to indicate the following information:
    A method to specify up to 6000 STAs with a DTIM map only support 2007 STAs
      For example,
        (1) For ah, the partial virtual map is reduce by two bits and only support 2005 STAs. The last two bits are reserved to indicate STA groups 2006-4010, and 4011 – 6000s
How to deal with 6000 STAs by using UTIM?
  Add a new element, UTIM
    The UTIM support a map of 6000 STAs
    The scheduling information can be explicit or implicit
    The UTIM and scheduling information element are sent only when there is a change of ordering or number of STAs
      The overhead is reduced by only transmit the UTIM when it is necessary