## Slide 1: Use Case Document Definitions
Date: 2011-05-10
Authors:

## Slide 2: Abstract
Discussions of the Use Case Reference List r15 have uncovered the need to make sure the definitions used to describe use cases are precise. This presentation is to be used as a vehicle to make sure we have consensus.
Reference:
https://mentor.ieee.org/802.11/dcn/11/11-11-0238-15-00ai-use-case-reference-list-for-tgai.docx

## Slide 3: Missing Use Case
Enhanced MDSS Communications (3.2.4)
In existing Maintenance Decision Support Systems (MDSS), there is a reliance on commercial wireless networks to communicate with snowplows or other maintenance vehicles. In many rural areas, access to commercial networks is limited and/or expensive. Using IEEE 802.11ai APs installed either specifically for this application or using an AP that offers multiple applications could be a better alternative. MDSS equipped maintenance vehicles would use the strategically placed APs to download treatment recommendations and upload recent maintenance activities.
11-11-0281-00-00ai-proposed-dynamic-mobility-use-cases-for-tgai.docx]
Expected Value Difficulty designation
Link-Attempt Rate 10 or less Medium
Media Load %50 High
Coverage Interval Less than 5 Medium
Link Setup Time 100 ms High
Summary: FILS enables this use case.
Impact: High, but for a small market

## Slide 4: Text of 2.1
Each of the use cases also have the determination of the level of difficulty to achieve with the now-current 802.11 technology. The traits which differentiate the use cases are summarized in a table at the end of each use case description. The traits, defined below, are “Link-Attempt Rate”, “Media Load”, “Coverage Interval”, and “Link Setup Time”. An expected value or each of these traits is listed as well as a general indication of difficulty in terms of high, medium, low.
High = very difficult to achieve
Medium = difficult
Low = nominal behaviour, expected to be achieved with current technology

## Slide 5: Link-Attempt Rate
Link-Attempt Rate is the number of STAs attempting to establish a link for the first time to an AP within an ESS as measured over a one second time interval.
  High: more than 50
  Medium: 10 to 50
  Low: less than 10

## Slide 6: Media Load
Media Load is the “busyness” of the wireless medium of the ESS. It is measured as the percentage of time the medium is in use.
  High: More than 50%
  Medium: 10 to 50%
  Low: Less than 10%

## Slide 7: Coverage Interval
Coverage Interval is the time the STA is within the range of an AP within an ESS. This time is the maximum available time for establishing a link and exchanging data. Coverage Interval does not include hand-off time within an ESS.
  High: less than 1 second
  Medium: between 1 and 10 seconds
  Low: more than 10 seconds

## Slide 8: Link Setup Time
Link Setup is defined as the process of gaining the ability to send IP traffic with a valid IP address through the AP. Link Setup may involve more than one AP in an ESS. This includes AP/Network discovery and (secure) Association and Authentication. Link Setup Time is the amount time required in the use case to establish link setup. Timing starts when the STA elects to perform Link Setup.
  High: less than 100 ms
  Medium: between 100 ms and 2 seconds
  Low: more than 2 seconds
NOTE: “link”, “association”, and “authentication” are as defined per 802.11