## Slide 1: Use Case: Mobile hotspot
Date: 2011-05-12
Authors:
Name | Affiliations | Address | Phone | email
Jihyun Lee | LG Electronics | LG R&D Complex 533, Hogye-1dong, Dongan-Gu, Anyang, Kyungki, 431-749, Korea | +82-31-450-1860 | Jihyun1220.lee@lge.com
Eunsun Kim |  |  |  | 
Yongho Seok |  |  |  | 

## Slide 2: Abstract
This presentation proposes an expected change in 11-11-0238-18-00ai Use case reference list for TGai
Editing instructions in the next slides

## Slide 3: Mobile hotspot scenario
Insert the following in 3.3
3.3.6. Mobile hotspot
  A train may have a "mobile hotspot" which comprises an 802.11 AP, a non-AP STA interface, and a third non-802.11-based interface.
  Users on board the train may connect to the AP interface of the mobile hotspot. The mobile hotspot may connect via its third, non-802.11-based interface to the Internet while the train is driving.
  As soon as the train enters a train station, the mobile hotspot may try to connect to an AP situated at the train station using the mobile hotspot's non-AP STA interface.
  While attempting to connect to the AP at the train station, users may leave the train and simultaneously try to connect directly to the AP situated at the train station.
  Note--from the perspective of the AP situated at the train station, the arriving "mobile hotspot" is not distinguishable from a single user arriving at the train station since the "mobile hotspot" uses its non-AP STA interface for connecting to the AP situated at the train station.

## Slide 4: Mobile hotspot scenario
Traits
Summary
  FILS will help the use case be more viable
Impact
  Medium
Traits | Expected Value | Difficulty designation
Link-Attempt Rate | 100s | High
Media Load | 50+ | High
Coverage Interval | Less than 10 sec | Medium to high
Link Setup Time | Less than 2 sec | Medium to high

## Slide 5: Alternative
Insert the underlined paragraph in 3.3.1
3.3 Transit
  3.3.1 Station arrival
    A train with no Wi-Fi access arrives at a station and the passengers want to connect to the AP. A small number (less than 25%) of the passengers will remain in the AP range when the train leaves, 90 seconds after arrival. Large portion of passengers who leave will leave within 10 seconds.
    A train may have a "mobile hotspot" which comprises an 802.11 AP, a non-AP STA interface, and a third non-802.11-based interface. Users on board the train may connect to the AP interface of the mobile hotspot. The mobile hotspot may connect via its third, non-802.11-based interface to the Internet while the train is driving. As soon as the train enters a train station, the mobile hotspot may try to connect to an AP situated at the train station using the mobile hotspot's non-AP STA interface. While attempting to connect to the AP at the train station, users may leave the train and simultaneously try to connect directly to the AP situated at the train station.