## Slide 1: Undetected Duplicate Frame Reception
Date: 2011-05-12
Authors:

## Slide 2: Abstract
A discussion and proposed solution regarding the problem of undetected duplicate frame receptions.

## Slide 3: Purpose of MAC Sequence Number
Duplicate detection
    (original 802.11 use)
    Retry attempts due to failed ACK reception can lead to the reception of multiple copies of a single MPDU
    The sequence number allows identification of such duplicate frames
    This issue is applicable to MPDU as well as MMPDU
Re-ordering of frames included in a Block Ack agreement
    Out of order transmission is allowed among the frames covered by a Block Ack agreement
    MAC Sequence numbers allow recipient to determine correct order for delivery to layer above
    BlockAck is not supported for MMPDU

## Slide 4: 802.11 Baseline SEQ NUM Allocation
Non-QoS STA (DCF)
  All SEQ NUM from one counter for all frames (9.3.2.11)
QoS STA (EDCA)
  MMPDU SEQ NUM assigned from a SEQ space shared with MCAST QoS MSDUs and all non-QoS Data frames (9.3.2.11)
  Other frames use one SEQ NUM counter per TID, RA (9.3.2.11)

## Slide 5: 802.11 DCF Duplicate Detection
Recipient can detect duplicates by storing one SEQ NUM per TA = last received SEQ NUM
This originally (mostly)* worked because there can only be one frame from any TA outstanding at any time
  I.e. pre-11e-QoS-baseline had only one TX queue
      Transmissions are always in queue order, with no attempts from later frames until current frame has been completed
  Recipient keeps only the last received SEQ NUM for that TA
  Rejects as duplicate only if RETRY=1 and SEQ NUM + TA is an EXACT MATCH – i.e. NOT a check for “old”
* see Address 1-induced false positive duplicate

## Slide 6: DCF-PS-Induced Undetected Duplicate
  At least one STA is PS in the BSS
  AP transmits UCAST MSDU SEQ=N, STA receives SEQ=N
  AP fails to receive ACK for SEQ=N
  TBTT occurs, AP sends Beacon + MCAST
  AP sends MCAST frames following Beacon
    STA receives MCAST with SEQ=N+1
  AP finishes MCAST, resends SEQ=N with RETRY=1
  STA receives SEQ=N, RETRY=1, compares to SEQ=N+1, does not declare duplicate, does not discard duplicate
  Problem is avoided if SEQ=N retry is completed BEFORE Beacon transmission begins
    Spec seems to mandate this (see 10.1.3.2)
  Problem also avoided if recipient follows 9.3.2.11 recommendation
    See next slide

## Slide 7: 10.1.3.2 Transmission of Beacon
At each TBTT, the AP shall schedule a Beacon frame as the next frame for transmission according to the medium access rules specified in Clause 9 (MAC sublayer functional description).
  Next frame implies behind the current frame and following all retransmissions of the current frame, given that there is a single queue for transmission of all frames per the original standard

## Slide 8: 9.3.2.11 Permission to ignore SEQ NUM
A receiving STA may omit tuples obtained from group addressed or ATIM frames from the caches.
  E.g. Beacon = BCAST = Group addressed

## Slide 9: DCF-PS Undetected Duplicate
Only happens when PS is used and 10.1.3.2 and 9.3.2.11 are ignored
Data
SEQ=N
AP
STA
ACK
SEQ=N
MCAST
SEQ=N+1
DCF TX
PS-mode MCAST
STA passes Data SEQ=N to next layer
Data
SEQ=N
ACK
SEQ=N
STA passes Data SEQ=N to next layer
DUPLICATE DELIVERED TO NEXT LAYER!
BCN
TBTT
Cache entry <= N
Cache entry <= N+1

## Slide 10: EDCA-Induced Undetected Duplicate
EDCA-induced missed duplicate
    Same as previous but can occur when there are no PS STAs causing PS buffering of MCAST
      Non-QoS Data sent as AC_BE
      MGMT sent as AC_VO
    AP can switch between these queues on successive retry attempts
      Because EDCA protocol requires switching queues based on backoff outcome
    Problem is due to frames from different priorities sharing a single SEQ space
      Non-QOS DATA using AC_BE
      MGMT using AC_VO
    Transmitter is QOS, Recipient is non-QOS
Note that PS-Induced Undetected Duplicate can still occur in EDCA context

## Slide 11: EDCA-Induced Missed Duplicate
Transmitter is QOS, Receiver is non-QOS
Happens if PS is not used
Not fixed by 9.3.2.11 or 10.1.3.2
Non-QOS DATA
SEQ=N
AP
STA
ACK
SEQ=N
MGMT
SEQ=N+1
AC_BE TX
AC_VO TX
STA passes DATA SEQ=N to next layer
Non-QOS DATA
SEQ=N
ACK
SEQ=N
AC_BE backoff
STA passes DATA SEQ=N to next layer
DUPLICATE DELIVERED TO NEXT LAYER!
ACK
SEQ=N+1
AC_BE RE-TX
Cache entry <= N
Cache entry <= N+1

## Slide 12: EDCA-Induction additional comments
Non-QOS DATA and MGMT can be in opposite order
  E.g. sequence begins with a MGMT TX failure
    Middle reception is non-QOS DATA frame
  Less likely to occur because
    Ratio of non-QOS DATA to MGMT >> 1
    AC_VO more likely to beat AC_BE for retransmission
  Depicted case is more detrimental, and more likely
    Duplicate MGMT receptions generally not harmful
    Duplicate DATA receptions potentially harmful

## Slide 13: Special-MGMT Undetected Duplicate
  Does not depend on PS
  Arises from special transmission permissions for some frames
    E.g. MGMT ACTION NOACK used in sounding exchange for FeedBack (FB)
  Does not occur because of explicit priority differentiation
    Occurs because of special transmission rules
    E.g. immediate response “higher priority” than even AC_VO
  Problem is due to frames from different “implicit priorities” sharing a single SEQ space
  Transmitter is QOS, Recipient is non-QOS
    E.g. mix of non-QOS DATA and MGMT frames
  Transmitter is QOS, Recipient is QOS
    E.g. all frames are MGMT frames
  Not fixed by 9.3.2.11 or 10.1.3.2

## Slide 14: Special MGMT-Induced Missed Duplicate Transmitter QOS, Receiver QOS
Not fixed by 9.3.2.11 or 10.1.3.2
MGMT not-FB
SEQ=N
AP
STA
ACK
SEQ=N
MGMT FB
SEQ=N+1
AC_VO TX
Imm_Resp TX
STA passes MGMT SEQ=N to next layer
MGMT not-FB
SEQ=N
ACK
SEQ=N
AC_VO backoff
STA passes MGMT SEQ=N to next layer
DUPLICATE DELIVERED TO NEXT LAYER!
ACK
SEQ=N+1
SOUNDING
Cache entry <= N
Cache entry <= N+1

## Slide 15: Address 1-Induced False Positive Duplicate
    Applicable to frames that share a single sequence number space independently of Address 1 value
      E.g. non-QoS Data + Management + MCAST
    PS not required
    AP sends SEQ=N to RA=STA1
      STA1 places <TA=AP, SEQ=N> into cache after reception
    AP sends SEQ=N+1 through N+4095 to RA ≠ STA1
      AP sequence numbers have wrapped, next sequence number will be N
      Next frame for transmission is to STA1
    AP sends SEQ=N to RA=STA1
      STA1 fails to receive this transmission
      AP retransmits SEQ=N to STA1, with RETRY=1
      STA receives SEQ=N, RETRY=1, compares to cache entry, >TA=AP, SEQ=N>, incorrectly declares reception as a duplicate
    Problem is not solved by 10.1.3.2 or 9.3.2.11
    Low probability of occurrence

## Slide 16: Solution Discussion
Modify TX behavior
  Fixed SEQ value for MGMT frames
    Does not eliminate problem
    Does not allow for duplicate detection of MGMT frames
    Not backwards compatible
  New SEQ space for UCAST MGMT frames
    Apply only to capable recipients through capability advertisement
    MCAST MGMT frame problem not fixed
  Put UCAST MGMT frames to non-QoS STA in AC_BE queue
  Cache last used SEQ per RA, do not re-use same SEQ serially per RA
Modify RX behavior
  Add more caches
    See next slide

## Slide 17: Proposed Solutions: Transmitter Undetected Duplicate
Transmitter to place UCAST MGMT frames to non-QOS STA into AC_BE queue
  Existing language from 9.2.4.2:
      Management frames shall be sent using the access category AC_VO without being restricted by admission control procedures.
  Proposed modification to 9.2.4.2:
      A QoS STA should send individually addressed Management frames that are addressed to a non-QoS STA using the access category AC_BE and shall send all other mManagement frames shall be sent using the access category AC_VO. A QoS STA that does not send individually addressed Management frames that are addressed to a non-QoS STA using the access category AC_BE shall send them using the access category AC_VO. No management frame is without being restricted by admission control procedures.

## Slide 18: Proposed Solutions: Transmitter False Positive Duplicate
Transmitter to maintain cache of last used SEQ per RA
Transmitter should ensure that sequential frames to same RA do not have same SEQ number
  9.3.2.11 – add the following:
    STAs should cache the last used sequence number per RA for frames that are assigned sequence numbers from a counter that is shared by more than one RA and should ensure that the sequence numbers for successively transmitted frames to a single RA are not the same by incrementing the counter by 2, if incrementing by 1 would have produced the same sequence number as is found in the cache for that RA.

## Slide 19: Proposed Solutions: Receiver
9.3.2.11 – Specify separate cache entries at recipient for
  MGMT
  SMGMT
    i.e. Special Management, i.e. priority > AC_VO
  non-QOS DATA
9.3.2.11 - Change “may omit” to “should omit”
  A receiving STA may should omit tuples obtained from group addressed and or ATIM frames from the caches.
    Maybe also add a note indicating why it should omit these

## Slide 20: SMGMT Definition
Any frame that could be transmitted outside of the AC_VO queue
    Immediate response
    Time-event directed transmission
Proposed SMGMT list:
    PSMP
    Set PCO Phase
    CSI
    Noncompressed Beamforming
    Compressed Beamforming
    ASEL Indices Feedback

## Slide 21: References
11-11-0835-00-000m-undetected-duplicate-reception-proposed-text.docx