## Slide 1: Verification of TGai Requirements
Date: 2011-05-24
Authors:

## Slide 2: Abstract
This document provides initial discussion points to decide on how to show compliance to TGai Requirements.

## Slide 3: Verification of Requirements vs. System Performance
Verification of Requirements
  Very abstract, synthetic scenarios
  Focus on a single aspect of the system
  Represent the best case behaviour that can be expected
  Usually do not show interaction between parameters
  Define conditions for “being compliant” to a requirement
System Performance
  More complex evaluation
    to show interaction between parameters, or
    to evaluate proposals in scenarios reflecting considered use cases
  Ideal (e.g. fixed data rate, free space los LOS channel) and/or more realistic conditions (other channel model, rate adaptation, etc.)
Focus of today’s presentation

## Slide 4: ToC Evaluation Methodology Document
Introduction
  <General introduction to methodology. Two parts of methodology: a) showing compliance to functional criteria, b) system evaluation based on scenarios from the use case document>
Metrics
  <we have them already as part of the use case doc. But having them again in this document makes it self-contained. Also, we might end up with additional metrics>
  Link Set-Up Time
  User Load
  Background load
System Evaluation
  Compliance to System Requirements
    <one sub-heading per requirement. Simple / synthetic scenarios: ideal channel, very few nodes.>
    FC-1
    FC-2
  Use-Case-based Performance Evaluation
    <complex scenarios with “more” interaction between nodes. Closer to real world situation than scenarios above.>
Annex
  Channel Models
    LOS free-space channel
  Evaluation Scenarios / Set-Up
    <detailed spec of recurring / useful scenarios / set-ups>

## Slide 5: Verification of FUNCTIONAL Requirements
Req. 2.1.1.1 (Link Set-Up): Support of link set-up (includes AP detection, network discovery, association and auth., IP-address assignment
  Abstract analysis of features showing “existence” of feature
Req 2.1.2.1 (Robustness against large number of users)
  Experiment to show how well an approach scales with different number of users.
  Metric: Link-Set-Up Time (as function of link attempt rate)
    Direct-proportional, over-proportional, or sub-proportional (?)
  Ideal channel (LOS free-space path loss), fixed data rate

## Slide 6: Verification of FUNCTIONAL Requirements (2)
Req.2.1.3.1 (concurrency in information exchange)
  Abstract analysis of features showing “existence” of feature

## Slide 7: Verification of PERFORMANCE Requirements
Req.2.2.1.1 (Link-Set-Up Time):
  Report Link Set-Up Time for
    Single STA, single AP
    LOS free-space loss channel, fixed data rate
    Assumptions / knowledge used to minimize LSU Time (e.g. external knowledge on used channels);
    Should we define one scenario for “know knowledge at all?”
    LSU Time shall be < 100ms to for compliance to requirement
  Additional performance evaluations for general performance evaluation section:
    LSU-Time as function of a) link attempt rate, b) background load
      Report percentile for LSU-Time < 100ms as a function of parameter
      Other values useful ? (e.g. percentile for LSU Time < 5, 10, 20, 50 ms)
      Other channel models / rate adaption as options

## Slide 8: Verification of PERFORMANCE Requirements (2)
Req.2.2.2.1 (support of min. user load)
  Metric: Link Set-Up Time as function of link attempt rate
  LOS free space channel, fixed data rate
  Report 100% percentile of LSU Time for an attempt rate of 100 (note: if not *all* STAs can conduct a link set-up, “infinite” shall be reported; avoid just reporting the maximum of measured LSU Times as this might not show that not all STAs have successfully conducted a LSU). To show compliance, this value has to be a finite value.
  Additional performance evaluations for general performance evaluation section: see Req. 2.2.1.1

## Slide 9: Verification of PERFORMANCE Requirements (3)
Req.2.2.2.2 (robustness against background load)
  Metric: Link Set-Up Time as function of background load
  Single AP, Single STA to establish a link
  Fixed STAs producing background load (need to define traffic profile. What to choose here? UDP-based traffic causing xxx Mbps per STA)
  LOS free space channel, fixed data rate
  Report 100% percentile of LSU Time for a background load of 50% (note: if not *all* STAs can conduct a link set-up, “infinite” shall be reported; avoid just reporting the maximum of measured LSU Times as this might not show that not all STAs have successfully conducted a LSU). To show compliance, this value has to be a finite value.
  Additional performance evaluations for general performance evaluation section: see Req. 2.2.1.1

## Slide 10: Verification of CONSTRAINTS
Req.2.5.1.1 (Maintaining RNSA’s security level)
  The TGai amendment shall assure maintaining RSNA’s security level. Solutions shall demonstrate that they do not degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11. Solutions employing security schemes other than RSNA shall demonstrate that they are at least as secure as RSNA
  How do we show this? What shall be provided for verification purposes?
  It should be in a form that can be used to proof to 802.11 WG that the requirement is met (to be useful as part of security review).

## Slide 11: Verification of CONSTRAINTS (2)
Req.2.5.1.2 (Backward compatibility)
  Abstract analysis of features showing “existence” of feature
  Can be as simple as showing that any STA can at any time fall back to existing link set-up schemes in case a non-TGai STA is involved in the process of establishing a link.

## Slide 12: References
11-11/0745r05: TGai Requirements Document
11-11/0238r19: Use Case Reference List for TGai