## Slide 1: Upper Layer Data on Management Frames
Date: 2011-07-18
Authors:
Name | Affiliations | Address | Phone | email
Hiroki Nakano | Trans New Technology, Inc. | Sumitomo Seimei Kyoto Bldg. 8F, 62 Tukiboko-cho, Shimogyo, Kyoto 600-8492 JAPAN | +81-75-213-1200 | cas@trans-nt.com

## Slide 2: Abstract
To reduce total time for connection setup through all layers, processing for each layer should be running in parallel and data for each layer should be conveyed in the same packet if possible.
This presentation introduces technical proposal that 802.11ai provides container framework for data of upper layers.

## Slide 3: Desirable nature of “container”
Compatibility with existing 802.11 (Required)
Convey multiple upper layer protocols simultaneously
Big enough to accommodate upper layer data
Take opportunities effectively for sending and receiving data and easy for upper layer to use
Declare and check security conditions of each container
Do not care of inside of upper layer data
Least limitation on behaviours of upper layers

## Slide 4: Compatibility
Convey on Beacon, Association Request/Response.
Use newly-defined IE
  Old AP and stations ingore it.
ID of new IE is larger than one of vendor specific IE.
  keep the order of IEs

## Slide 5: Multiple protocols
Each of data frame has a protocol type.
  IPv4/v6 uses SNAP header (RFC1042)
Each of data block can be had a protocol type in the same manner.

## Slide 6: Size of data block and IE
IE has 1-byte length field.
  Maximum size of IE is 1(type) + 1(length) + 255(data)
  This is too small for some kinds of upper layer protocols.
Data for an upper layer protocol should be fragmented when needed.
New IE has to have the ‘More IE Fragment’ bit.
Order of New IEs must not be changed during transmission.

## Slide 7: More opportunities for data exchange
Action frames with new IEs should be permitted to be exchanged between Association Request and Response, moreover, after Association Response.
For a convenience for upper layer programmers, MLME interface of this framework should be able to used after association completed (that is, after Association Response)

## Slide 8: Declare and check security status
802.11ai may provide multiple authentication and key management protocols.
Security status of a packet varies according to protocols and their state.
  No security
  Signed (data can not be altered during transmission)
  Encrypted (data can not be revealed during transmission)
802.11ai should tell upper layers such status.
Upper layers should tell 802.11ai requirement of security nature of data to be sent, and 802.11ai checks it.

## Slide 9: Discussion